## Slide 1: Location Measurement Protocol for 11ax
Date: 2016-07-26
Authors:

## Slide 2: Abstract
In this presentation we describe how an 11ax scheduling protocol may be used for performing location measurements.

## Slide 3: Recap: Accepted Functional Requirements
Addressed by this submission:
The location protocol shall support positioning measurement of unassociated and associated STAs in the HE MU mode.
The 11az amendment shall have a mode supporting concurrent positioning measurements of multiple STAs, in both associated and (unassociated) states in the HE MU mode.
The 11az amendment shall have a mode supporting concurrent measurement from several transmit chains of an AP in HE operation mode. The same requirement shall also apply to VHT operation mode.
The 11az amendment shall have a mode supporting concurrent measurement from several transmit chains of each non-AP STA in the HE operation mode. The same requirement shall also apply to the VHT operation mode.

## Slide 4: 802.11ax UL MU Operation using Trigger Frame
AP transmits a Trigger frame to initiate UL MU transmission
  Resource allocation (RUs and spatial streams) signaled in Trigger frame
  Mixed UL transmission in frequency and spatial domains, i.e., UL-OFDMA or UL MU-MIMO
STAs transmit UL MU frames simultaneously after SIFS of Trigger frame transmission
AP transmits ACK/BA/M-BA frame to STAs
  Multi-STA BA (M-BA) is a new MU DL BA defined in 11ax as an extension of baseline Multi-TID BA for ACK/BA of multiple TIDs per STA

## Slide 5: UL OFDMA-based Random Access Metrics in 802.11ax
Random access RU
  An RU allocated to AID 0 signaled in Trigger frame
  TFR is a Trigger frame (TF) with at least one RU assigned to AID 0
OCW
  Contention Window for OFDMA
OCWmin, OCWmax
  Min and max values for OCW
OBO (OFDMA Backoff Count)
  A counter maintained by the STA that determines the random access RU the STA utilizes

## Slide 6: UL OFDMA-based Random Access Procedure in 802.11ax
AID 0
AID 0
AID 0
STA 1 and STA 2 have something to send.
They randomly select Backoff Counts (BOs) of 11 and 5, respectively
STA 1 BO = 10
STA 2 BO = 4
STA 1 BO = 9
STA 2 BO = 3
STA 1 BO = 8
STA 2 BO = 2
AID 0
AID 0
STA 1 BO = 7
STA 2 BO = 1
STA 1 BO = 6
STA 2 BO = 0
STA 2 wins channel access
Trigger Frame (TFR)
(random access)
Trigger Frame (TF)
(no random access)
Nothing in this TF causes STA 1 to decrement its BO
Contention in time
Contention in frequency
1 RU slot
Trigger Frame (TFR)
(random access)

## Slide 7: Frame exchange flow description
Similar to FTM, the proposed mechanism is composed of 3 stages:
  Measurement negotiation
  Measurement exchange
  Termination (can be implicit or explicit, to be discussed at a later time)

## Slide 8: Proposed Service Negotiation Phase
TF Service Request
FTM Request
AP
STA
FTM Response
Propose to define a new Trigger frame type (currently there are 5 types of Trigger frames in 11ax
  The Trigger type is for service negotiation / request
  The frame format of the TF Service Request is TBD
  Proposed mechanism is adaptable for both scheduled and random-access based STAs
Propose that the TF Service Request frame solicits an FTM Request from STAs allowing capability exchange
The AP sends an FTM Response to complete the service negotiation phase
  Reuse legacy and add 11az IEs
  Legacy STAs skip the 11az IEs
SIFS
M-BA
SIFS
Same as REV\mc
SIFS
Ack

## Slide 9: Measurement exchange
Following the service negotiation, AP allocates resources for UL sounding (NDP);
  UL sounding is followed by DL sounding
The 2nd TF allocates resources for STA to provide location measurement report (LMR) to AP
  Followed by reciprocal report from AP to STA (Location Measurement Report)
TF (Sounding)
NDP
AP
STA
LMR (AP to STA)
SIFS
NDP
SIFS
SIFS
LMR (STA to AP)
SIFS
SIFS
TF

## Slide 10: Protocol properties
The UL NDPs may be staggered in time or spatial domain and are 11az NDP; format of NDP is TBD
Adapting the FTM protocol to 11ax scheme
Based on the 11ax scheduling infrastructure with STAs 1 to n
Constant interval between measurement and report
Possibly reusing the previously proposed VHT protocol to the 11ax
Power efficient – completes within a single TxOP
Location measurement exchange part
UL sounding
part
SIFS
Tx OP
NDP n (sound)
:
:
NDP 1 (sound)
TF
SIFS
SIFS
SIFS
AP2STA LMR
part
AP2STA
STA n
(LMR)
:
:
AP2STA
STA 1
(LMR)
SIFS
STA2AP LMR
part
STA2AP
STA n
(LMR)
:
:
STA2AP
STA 1
(LMR)
TF
SIFS
DL sounding
part
DL
NDP

## Slide 11: Conclusion
In this contribution, we have discussed about the UL MU operation as defined in 802.11ax
We have also discussed the UL OFDMA-based random access mechanism introduced in 802.11ax for STAs with transmit power asymmetry with respect to that at the AP