## Slide 1
Scheduling Allocation on Multi-channels in 11ay
Date: 2016-09-13
Authors:

## Slide 2: Background
It was agreed that 11ay shall support allocation of SP(s) and scheduled CBAP(s) over more than one channel and over a bonded channel [1].

## Slide 3: Background
In 11ad, DTI is coordinated as CBAP and SP using a schedule by PCP/AP, and the scheduling allocation can occur every BI by beacon or announce frame.
Flexible channel allocation can maximize the use of all available channels, the method of allocation based on 11ad is not efficient in respect of multi-channel operation.
In [2], the reserved bits in Extended Schedule element are proposed to be used for signaling the channel allocation to EDMG STAs for multi-channel operation.

## Slide 4: Recap on channelization and bandwidth signaling for EDMG [3]
It has been agreed that in 11ay, up to six 2.16 GHz channels as well as the overlapped bonded channels can be used.
The following fields are agreed to be added in EDMG-Header-A to indicate the channel allocation
  1 bit “channel aggregation” field
  8 bits “bandwidth” field
11ay shall only allow the following
combinations for channel aggregation:
  2.16GHz + 2.16GHz
  4.32GHz + 4.32GHz

## Slide 5: Recap on channelization and bandwidth signaling for EDMG [3]
CA (Channel Aggregation) field
  Set to zero for channel bonding or single 2.16GHz channel
  Set to one for channel aggregation
BW (Bandwidth) field
  Bit 1-8 corresponds to channel 1-8
  For each channel, the corresponding bit is set to 1 if modulated and to 0 if not modulated
For example:

## Slide 6: Channel allocation for 6 and 8 channels*
Total 39 possible channel combinations for 6 channels and at least 6 bits needed
Total 69 possible channel combinations for 8 channels and at least 7 bits needed
* 8 channels are considered if 71-76 GHz are open for unlicensed use

## Slide 7: Extended Schedule Element
At most 6 reserved bits could be used for channel allocation in Extended Schedule Element. However, it seems the reserved bits are not enough for up to 8 channels operation.
A new Information Element (IE) named EDMG Extended Schedule Element should be defined to support the scheduling allocation of multiple channels for EDMG STAs.
b4 | b5 | b6
SP or CABP | Reserved | 

## Slide 8: EDMG Extended Schedule Element
A channel allocation field is defined in EDMG Extended Schedule Element as the incremental signaling to the DMG Extended Schedule element for the scheduling over more than one channel.
One Element ID reserved for 11ad could be selected to indicate this new IE.
The Allocation ID field could be used to correlate the information across the DMG Extended Schedule element and EDMG Extended Schedule element.

## Slide 9: Indication of channel allocation
The indication of the channel allocation defined in EDMG-Header-A could be reused for indicating the scheduling over more than one channel.
Following two subfields are reused in the channel allocation field.
  1 bit “channel aggregation”
  8 bits “bandwidth”

## Slide 10: Conclusions
A new EDMG Extended Schedule Element is introduced to support the scheduling allocation of multiple channels for EDMG STAs.
A channel allocation field is defined in EDMG Extended Schedule Element as the incremental signaling to the DMG Extended Schedule element for the scheduling over more than one channel.
The indication of the channel allocation defined in EDMG-Header-A can be reused for indicating the scheduling over more than one channel.

## Slide 11: References
[1] 11-15-1358-05-00ay, Specification Framework for TGay
[2] 11-16-0401-00-00ay, Multi-channel Operation in 11ay, LGE
[3] 11-16-0266-03-00ay-a-compendium-of-motions-related-to-the-contents-of-the-specification-framework-document-for-tgay

## Slide 12: Straw Poll 1
Do you agree to add the following text into the SFD:
  An EDMG Extended Schedule element shall be defined to include incremental signaling to the DMG Extended Schedule element, including channel allocation indications if allocations are scheduled over more than one channel and the Allocation ID field shall be used to correlate the information across the DMG Extended Schedule element and EDMG Extended Schedule element.
  Yes
  No
  Abstain

## Slide 13: Straw Poll 2
Do you agree to add the following text into the SFD:
  A channel allocation field in the EDMG Extended Schedule element shall be defined to indicate the channel allocation for SP and CBAP in 11ay.
  Yes
  No
  Abstain

## Slide 14: Straw Poll 3
Do you agree to add the following text into the SFD:
  The channel allocation field in the EDMG Extended Schedule element shall reuse the indication in EDMG-Header-A with 9 bits to indicate the channel aggregation and BW.
  Yes
  No
  Abstain