## Slide 1: EDMG Block Acknowledgement frame format
Date: 2016-09-11
Authors:

## Slide 2: Abstract
EDMG BA format

## Slide 3
Purpose and definitions
The purpose of this presentation is to provide more details to NG60 BA frame format
Adopt smart idea presented in TGax to have few sizes of bitmap
Unify BA frame format to support Flow control
Support “The size of the Block Ack window bitmap for EDMG STAs shall be 1024 bits.”

## Slide 4
Extended compressed BA variant

## Slide 5
Extended compressed BA Format
New definition of the subfield is presented in next slide

## Slide 6
EDMG BA Information filed
 | Block Ack starting Sequence Control | Block Ack Bitmap | RBUFCAP
Octets | 2 | N i | 1
BA information field
B0 B3 | B4 B15
Reserved (0) | Starting Sequence Number
4 | 12
Block Ack Starting Sequence Control subfield
Bitmap size index i | N i
0000 | 8
0001 | 16
0010 | 32
0011 | 64
0100 | 128

## Slide 7
Relevant rules
BA Bitmap length is negotiated during BA setup (for each TID) [2]
The size of the Block Ack window bitmap for EDMG STAs shall be one of 64, 128, 256, 512 or 1024 bits. The size of the Block Ack bitmap for a TID shall be the smallest size that is greater than the minimum between the value of the Buffer Size field in the ADDBA Request and Response frames that set up the block ack agreement for the TID.

## Slide 8: Straw Polls
Do you agree to change the following sentence in section 2.2.1 of the SFD: “The length size of the Block Ack window bitmap for EDMG STAs shall be one of 64, 128, 256, 512 or 1024 bits.

## Slide 9: Straw Polls
Do you agree to insert the following sentence in section 3 of the SFD: “The length of the Block Ack bitmap is determined as a result of the Buffer Size negotiation in the ADDBA Request/Response frame exchange as specified in <slide 7>”

## Slide 10: Straw Polls
Do you agree to insert the following in section 2.2.1 of the SFD: “EDMG BA format is as defined in <slide 5> and <slide 6>

## Slide 11: References
11-16-0616-02-00ax-blockack-generation-and-selection-rules
11-16-0308-00-00ay BA performance for high EDMG PHY rates