## Slide 1: EDMG link access of bonded channels
Date: 2016-09-12
Authors:

## Slide 2: Abstract
Link access for bonded channels

## Slide 3
Purpose and definitions
Purpose of this presentation is to provide more MAC specific details in relation to CBAP in multiple channels

## Slide 4
Basic principles
Two types of multiple channels:
  Contiguous channel bonding of two or more adjacent channels
  Channel aggregation
Proposed solutions are applicable for both types of multiple channels

## Slide 5
Tx Sequence in multiple channels BW allocation from 2016-TECH-Intel-0031-01-NG60 channel bonding more details r1
Tx Sequence in multiple channels NAV setup
Duplicated RTS/CTS allows STA C to set up NAV
ACK/BA wideband versus duplicated

## Slide 6
Tx Sequence in multiple channels BW allocation from 2016-TECH-Intel-0031-01-NG60 channel bonding more details r1
STA A decides not to use secondary channel due to CCA busy and still use primary channel to utilize opportunity to deliver data
RTS/CTS provides BW indication
Energy is detected by STA A in Secondary channel
TXOP initiator is able to change Tx BW at the time it issues RTS in response to conditions changes
TXOP responder is able to receive frame sent not in full BW
Tx Sequence in multiple channels BW allocation

## Slide 7
No use of primary channel
Introduces substantial complication in CBAP with multiple accesses (CBAP only=1, both AID = broadcast)
Since full carrier sense is required on primary channel only, this approach can cause excessive unfairness and interferences even in the same BSS as not all STAs in the BSS may be aware of such access when trying to access the channel

## Slide 8: Straw polls
Do you agree to insert the following sentence in section 3.1.2 of the SFD "A TXOP responder shall be able to receive a frame sent on a channel that does not include all secondary channel(s)“
Do you agree to insert the following sentence in section 3.1.2 of the SFD "Multiple channel access in the DTI shall include the primary channel if the CBAP Only subfield in the DMG Parameters field is set to 1"
Do you agree to insert the following sentence in section 3.1.2 of the SFD "Multiple channel access in the DTI shall include the primary channel if both source and destination AID fields of an allocated CBAP are equal to broadcast"

## Slide 9: Straw polls
Do you agree to insert the following sentence in section 3.1.2 of the SFD "At least CCA of energy detection shall be performed on each non-primary channel“
Do you agree to insert the following sentence in section 3.1.2 of the SFD "A TXOP initiator shall not use a secondary channel if CCA of the channel is busy and may use the channel otherwise"

## Slide 10: References