## Slide 1: Heads We Win, Tails We Don’t Lose: Proposals for Dynamic CCA
Date: 2016-09-12

## Slide 2: Abstract
Dynamic CCA performance is known to vary widely depending on device configuration. In many cases parameters that improve performance in one configuration make matters worse (sometimes much worse) in many others.
This presentation argues that the mode is worth the trouble of including it, and that we can achieve the upside while avoiding (most of) the downside, provided we have an effective protocol control.
This presentation also proposes such a protocol control.

## Slide 3: Statement of goals
A basic ax goal is to improve system throughput
  Simulations involve “random drops” and result in averages across a great many configurations
  It’s difficult to analyze any given mode to isolate its strengths and weaknesses and thereby improve the mode
  It doesn’t correspond to how we usually think of WLAN
    E.g., 256-QAM: a 33% increase in date rate … but only usable about 4% of the time under random drops, so < 1.5% increase overall … no good
An even more basic goal
  A mode that produces significant and predictable gains in common and easily understandable conditions, and that doesn’t make matters worse in other conditions, is worth including in the spec

## Slide 4: Performance of Dynamic CCA
The effects of altering CCA levels ripple far beyond any given device pair and generate complicated consequences
  “Effects of changing the CCA levels are highly scenario and parameters dependent” [1, slide 11]
  “The smooth curves seen on simulations of total or average throughput get much more complicated when you look at individual BSSs” [2, slide 2]
  Cf. multi-company calibration of very simple, favorable case generating a wide range of results, no clear convergence [3, 4]
Interpretation
  There have been enough presentations to enable interpretations
  Next few slides review and add new observations

## Slide 5: Performance of Dynamic CCA—I
A favorable scenario:
AP1
AP2
STA1
STA2
35.6 m
3.35 m
3.35 m
50.2 m
5 GHz, 80 MHz channel
MCS 7 (64-QAM, rate 5/6)
Other assumptions as in [3, 4]

## Slide 6: Performance of Dynamic CCA—I, contd.
A favorable scenario:
Noise floor = 95 dBm
CCAT current = 76 dBm
+15 dBm
75 dBm
STA2 not permitted to transmit under
current rules
STA2 permitted to transmit if CCAT raised
76 dBm
44.3 dBm
AP1
AP2
STA1
STA2
35.6 m
3.35 m
3.35 m
50.2 m
SNR 50.7 dB
(Noise figure = 0 dB)

## Slide 7: Performance of Dynamic CCA—I, contd.
A favorable scenario:
Under relaxed CCAT, STA2 may transmit
Both AP1 and AP2 see SINR of 31.7 dB, much greater than the needed 20.4 dB [5]
So both transmissions are successful  2x improvement (though TPC gets same)
+15 dBm
76 dBm
/  44.3 dBm
44.3 dBm
/ 76 dBm
AP1
AP2
STA1
STA2
35.6 m
3.35 m
3.35 m
50.2 m
SINR 31.7 dB
SINR 31.7 dB
+15 dBm

## Slide 8: Comments—I
SINR vs. SNR
  Usually SINR is compared directly to AWGN curves
  Too optimistic: interference varies in frequency domain and over time, and arrives on frequency-selective channel
  Performance is disproportionally influenced by worst-case SINR over tones and time, which may be 5+ dB worse than average
    In this example there’s enough margin that it probably still works
    However if both transmitted MCS 9 (requiring 25.0 dB in AWGN), then with extra cost of SINR v. SNR, plus implementation losses, it would be unlikely to work

## Slide 9: Comments—II
Effect of mid-packet interference
  STA2 remains subject to EDCA and can’t transmit immediately on detecting STA1’s BSS Color
  Delayed start means channel estimates at AP1 will be incorrect
    In general, will cause some more performance loss
    If AP1 detects very high SNR on all tones, it could clip its estimates to minimum required to process that MCS, providing safety margin
    But probably not safe to assume that legacy devices all do this
Data
Preamble
STA1
STA2

## Slide 10: Performance of Dynamic CCA—II
A less favorable scenario:
AP1
AP2
STA1
STA2
35.6 m
11.9 m
3.35 m
50.2 m
STA1 to AP1 now D-NLOS
Otherwise same assumptions
MCS7 operating point 31.5 dB [6]
 STA1-AP1 can support MCS7
Wall
+15 dBm
SNR 32 dB
63 dBm

## Slide 11: Performance of Dynamic CCA—II, contd.
A less favorable scenario:
AP1
AP2
STA1
STA2
35.6 m
11.9 m
3.35 m
STA2 sees same RSSI as before
But SINR at AP1 drops to 13 dB
 STA1-AP1 now supports MCS0
Wall
+15 dBm
SINR 13 dB
63 dBm
+15 dBm

## Slide 12: Performance of Dynamic CCA—II, contd.
An even less favorable scenario:
AP1
AP2
STA1
STA2
35.6 m
11.9 m
11.9 m
Both MCS0 simultaneously, instead each MCS7 alternating  5x lower data rate
Wall
+15 dBm
SINR 13 dB
63 dBm
+15 dBm
Wall

## Slide 13: Comments—III
RSSI is not enough
  Here STA2 sees exactly the same RSSI from both STA1 and AP1, and it’s still not enough: STA2 lacks information about the link between STA1 and AP1
The current baseline does not provide a “safe harbor”
  Current baseline permits transmission by STA2 (in effect) if interference at STA1 is 76 dBm or less
  This doesn’t mean it has no effect: even the (better) reducing interference at AP1 to 76 dBm or less reduces the SINR by 20 dB +
  Relying on TPC to reduce interference at other receivers to 76 dBm significantly increases that interference (many interferers at exactly 76 dBm, whereas currently that’s an improbable worst case)

## Slide 14: Comments—IV
Sources of Dynamic CCA gain (when there’s a gain)
  Difference in interference measured at Tx and at Rx
    CCAT deals with Tx, whereas what matters is Rx
  (If no interferers) Excess Rx RSSI beyond that needed for highest MCS
    With no excess, a 20+ dB jump in SINR reduces link to lowest MCS
    MIMO, 256-QAM, 1024-QAM reduce Dynamic CCA gains [7]
  (With interferers) SINR, MCS caused by new transmission
    With other interferers, new transmission may cause small SINR
    MCS of ongoing transmission determined by presence of other interferers
      Even if no other interferers in one individual packet
      In effect the other interferers may cap the “highest MCS”
    So Dynamic CCA is more likely to contribute a gain in dense deployments with many OBSSs, where there are already several interferers

## Slide 15: Another use case
Sketch of scenario:
AP1
AP2
STA
Managed deployment
Multiple APs, part of same ESS, mutually isolated
Simultaneous UL works if CCAT increased, to any level (not achievable with TPC)

## Slide 16: Comments—V
Is Dynamic CCA worth it?
  The gains in the right circumstances are significant (even with caveats): ordinarily that would be enough
  Unlike ordinary modes, though, it causes significant losses in the wrong circumstances—and they’re not self-correcting
  The key is harvesting the gains without suffering the losses
  Predominantly a protocol issue: measuring RSSIs only takes us so far

## Slide 17: Comments—VI
Protocol considerations
  It must be possible to turn Dynamic CCA off
    Enables network diagnostics, on/off comparisons, “first do no harm”
    Already in spec, though conditions completely TBD
  There must be some incentive to turn Dynamic CCA on
    TPC model is not sufficient—TPC is already included but is hardly used
  On / off choice must be configurable per device
  The protocol must avoid hard choices
    An “optimal” protocol involves many tradeoffs between different BSSs; mean v. 5% outage throughputs; high data rate v. long range; ax v. ac/n/g
    It has been difficult for Wi-Fi to make such tradeoffs in the past
      Cf. the extreme difficulty even in deprecating 1 Mbps modes

## Slide 18: Proposed approach—I
Interferee-based signalling
  Each packet indicates whether other devices may use relaxed CCAT with respect to that packet
  If no such signalling present, Dynamic CCA may not be used
Interferee AP makes permission decision
  A non-AP STA may only disallow Dynamic CCA if permitted by its AP
  That AP has sole discretion on granting such permission
  Permission is per-STA and for limited duration
    Signaled and acknowledged per STA; valid for 100 (say) successful Tx’s
Protocol only specifies ‘permission’
  Both interfere and prospective interferer may choose default CCAT, whatever permissions are assigned

## Slide 19: Proposed approach—II
Protocol outline, restated:
  (1) each ax PPDU contains an “SR Allowed” bit
  if SR Allowed = 0, all devices (from any BSS) that decode that preamble successfully must use current CCAT for that PPDU (82 dBm for 20 MHz, etc.)
    Similarly if SR Allowed bit not present, e.g., legacy
  if SR Allowed = 1, all devices (from any BSS) that decode that preamble successfully may use ax Dynamic CCA for that PPDU
  non-AP STAs may only set SR Allowed = 0 in PPDUs they transmit if so permitted by their AP
  (4) all such permissions are for limited durations.

## Slide 20: Summary
Dynamic CCA performance
  Brings significant gains but in limited circumstances
    Increases overall interference levels
    Has greater impact on legacy receivers, depending on design
    May have more potential in managed environments
  Brings significant losses in other circumstances—not self-correcting and pits different BSSs against each other
  Potential interferer does not have enough information to determine impact on interferee
    RSSIs are not enough—even if potential interferer RSSIs at interferee Tx and interferee Rx are known
Protocol
  Interferee AP controls—guarantees acceptable results

## Slide 21: References
[1] IEEE doc. 11/14-1119r1, “Effect of CCA in residential scenario part 2”, G. Barriac (Qualcomm) et al., September 2014
[2] IEEE doc. 11/15-0357r4, “802.11ax scenario 1 CCA”, K. Odman (Broadcom), March 2015
[3] IEEE doc. 11/15-0652r1, “Reference Simulation Model for Dynamic CCA / DSC Calibration”, M. Mori (Sony) et al, May 2015
[4] IEEE doc. 11/15-0801r0, “DCCA/DSC Reference Simulation Results”, M. Mori (Sony) et al., July 2015
[5] IEEE doc. 11/14-0571r12, “11ax Evaluation Methodology”, R. Porat (Broadcom) et al., January 2016
[6] E. Perahia and R. Stacey, Next Generation Wireless LANs. Cambridge University Press 2008.
[7] IEEE doc. 11/15-0050r0, “Modeling Components Impacting Throughput Gain from CCAT Adjustment”, Y. Wang (Ericsson) et al., January 2015
[8] IEEE doc. 11/14-0872r0, “A Protocol Framework for Dynamic CCA,” S. Coffey (Realtek) et al., July 2014