## Slide 1: IEEE 802.11-IETF Liaison Report
Date: 2016-11-08
Authors:

## Slide 2: Abstract
This presentation contains the IEEE 802.11 – IETF liaison report for November 2016.

## Slide 3: IETF Meetings
Upcoming Meetings:
  November 13-18, 2016 – Seoul Korea
  March 26-31, 2017 – Chicago
  July 16-21, 2017 – Prague
  November 12-17, 2017 – Singapore
http://www.ietf.org
  Newcomer training: https://www.ietf.org/edu/process-oriented-tutorials.html#newcomers
  April 2016: Wireless Tutorial (Donald Eastlake), 802.11 & 802.15 tutorials (Dorothy Stanley, Charlie Perkins), see 11-16/500, July 2016: Pat Thaler & Juan Carlos – 802.1E (Privacy Considerations) and 802.c (Local MAC address usage) https://www.ietf.org/edu/tutorials.html
  http://tools.ietf.org/dailydose/

## Slide 4: IETF- IEEE 802 Liaison Activity
Joint meetings, agenda and presentations
  http://www.iab.org/activities/joint-activities/iab-ieee-coordination/
  2016-09-09 teleconference held; topics included Multicast, ITS, OWE, 5G, IoT, IRTF activities
  Tutorial request: present 802.11/.15 updates in Nov 2016
RFC 7241, “The IEEE 802/IETF Relationship” has been published (RFC4441 update)
  https://datatracker.ietf.org/doc/rfc7241/
IEEE 802 Liaisons list is available
  http://ieee-sa.centraldesktop.com/802liaisondb/FrontPage
802 EC “IETF/IAB/IESG” 802 EC Standing Committee
  Formed March 2014, Pat Thaler as chair
  Met during November 2016 Plenary: Tuesday PM1, reviewed
  Next meeting during March 2017 plenary

## Slide 5: Multicast Topics
Multicast issues were discussed at the IETF-IEEE 802 meeting Sept 29th 2015 and a presentation given at the November 2015 IETF meeting
  See https://mentor.ieee.org/802.11/dcn/15/11-15-1261-02-0arc-mulicast-performance-optimization-features-overview-for-ietf-nov-2015.ppt
  Further actions: ietf mailing list has been established for ongoing discussion, will include additional 802. wireless groups, see http://www.ieee802.org/11/email/stds-802-11/msg01838.html
  Multicast considerations Internet draft describing use cases, issues, etc. under development, see https://tools.ietf.org/html/draft-perkins-intarea-multicast-ieee802-01
Insights
  Multicast used for multiple types of traffic including ARP/ND, routing protocols, video applications, and these might need to be transmitted at different MCS
  Implementations might consider APIs to allow MCS differentiation
  Current Proxy ND support does not address Secure ND, see RFC 3971
  RFC 6775, Neighbor Discovery Optimization for IPv6 over Low-Power Wireless Personal Area Networks (6LoWPANs) defines a registration mechanism for accomplishing proxy ND: IoT and other applications motivating registration over discovery

## Slide 6: IETF BOFs at IETF November 13-18, 2016 meeting
See https://datatracker.ietf.org/wg/bofs/
banana | BANdwidth Aggregation for interNet Access, also see https://datatracker.ietf.org/wg/banana/charter/ and https://datatracker.ietf.org/doc/draft-zhang-banana-problem-statement/
dnsbundled | Bundled Domains, also see https://datatracker.ietf.org/wg/dnsbundled/charter/

## Slide 7: IETF Charters under consideration
IPv6 over Low Power Wide-Area Networks (lpwan), see https://datatracker.ietf.org/doc/charter-ietf-lpwan/ and also https://tools.ietf.org/html/draft-farrell-lpwan-overview-04
IP Wireless Access in Vehicular Environments (ipwave), see https://datatracker.ietf.org/doc/charter-ietf-ipwave/ and also https://datatracker.ietf.org/wg/its/documents/

## Slide 8: IRTF Drafts of interest
Recall PKEX removed from 11ai, modified protocol review and discussion in IRTF: Password-authenticated protocol to allow two devices to exchange "raw" (uncertified) public keys and establish trust that the keys belong to their respective identities (PKEX) see https://www.ietf.org/id/draft-harkins-pkex-01.txt

## Slide 9: Of Interest to Smart Grid
6LO
  Working Group website: http://datatracker.ietf.org/wg/6lo/charter/
  Focus: IPv6 over Networks of Resource-constrained Nodes
  See WNG presentation: https://mentor.ieee.org/802.11/dcn/15/11-15-1085-00-0wng-6lowpan-over-802-11.pptx and
  http://datatracker.ietf.org/doc/draft-delcarpio-6lo-wlanah/
  https://tools.ietf.org/html/draft-thubert-6lo-routing-dispatch-06
  https://tools.ietf.org/html/draft-thubert-6lo-backbone-router-02
  Unique IPv6 Prefix Per Host, https://tools.ietf.org/html/draft-jjmb-v6ops-unique-ipv6-prefix-per-host-00
    The concepts in this document were originally developed as part of a large scale, production deployment of IPv6 support for a community Wi-Fi service.
ROLL: Working Group website: http://datatracker.ietf.org/wg/roll/
  Focus: Routing over Low Power and Lossy Networks
  Of interest: https://tools.ietf.org/html/draft-ietf-6lo-ethertype-request-01
CORE : (Constrained RESTful Environments) Working Group website: http://datatracker.ietf.org/wg/core/
  Focus: framework for resource-oriented applications intended to run on constrained IP networks.

## Slide 10: CAPPORT WG
CAPtive PORTal: https://datatracker.ietf.org/wg/capport/charter/
The CAPPORT Working Group will define secure mechanisms and protocols to
  allow endpoints to discover that they are in this sort of limited environment,
  provide a URL to interact with the Captive Portal, - allow endpoints to learn about the parameters of their confinement,
  interact with the Captive Portal to obtain information such as status and remaining access time, and
  optionally, advertise a service whereby devices can enable or disable access to the Internet without human interaction. (RFC 7710 may be a full or partial solution to the first two bullets)
Note: related to OWE proposal in TGmc, see https://mentor.ieee.org/802.11/dcn/15/11-15-1184-05-000m-owe.docx
IETF draft Last call to start shortly: see https://tools.ietf.org/html/draft-harkins-owe-04

## Slide 11: RADEXT WG
See http://datatracker.ietf.org/wg/radext/
RADIUS Extensions
  The RADIUS Extensions Working Group will focus on extensions to the RADIUS protocol required to define extensions to the standard attribute space as well as to address cryptographic algorithm agility and use over new transports.
  In addition, RADEXT will work on RADIUS Design Guidelines and define new attributes for particular applications of authentication, authorization and accounting such as NAS management and local area network (LAN) usage.
Updates [Nov 2016]
  Submitted for publication: RADIUS Extensions for IP Port Configuration and Reporting. See https://datatracker.ietf.org/doc/draft-ietf-radext-ip-port-radius-ext/
  Considerations regarding the correct use of EAP-Response/Identity, see https://datatracker.ietf.org/doc/draft-ietf-radext-populating-eapidentity/
  (Related) RFC 7664, “Dragonfly Key Exchange” published, see https://datatracker.ietf.org/doc/rfc7664/
  Updated: Adding Support for Salted Password Databases to EAP-pwd has completed IETF last call, see https://datatracker.ietf.org/doc/draft-harkins-salted-eap-pwd/

## Slide 12: Home Networking (homenet) WG
See https://datatracker.ietf.org/wg/homenet/
This working group focuses on the evolving networking technology within and among relatively small "residential home" networks
  The task of the group is to produce an architecture document that outlines how to construct home networks involving multiple routers and subnets.
  Home Networking Architecture for IPv6, Published as IPv6 Home Networking Architecture Principle: http://datatracker.ietf.org/doc/rfc7368/
  Home Networking Control Protocol, published as RFC 7788, see https://datatracker.ietf.org/doc/rfc7788/
Updates [Nov 2016] Documents of interest:
  New individual submission: Special Use Top Level Domain '.homenet‘, see https://datatracker.ietf.org/doc/draft-pfister-homenet-dot/
  Home Networking Control Protocol (revisions), see https://datatracker.ietf.org/doc/draft-ietf-homenet-hncp-bis/
  Of Interest (no longer active): Home Network Wi-Fi Roaming, see https://datatracker.ietf.org/doc/draft-barth-homenet-wifi-roaming/

## Slide 13: Operations Area Working Group
http://datatracker.ietf.org/wg/opsawg/
  Area WG processes submissions related to Operations Area WGs that have closed
  Control and Provisioning of Wireless Access Points (CAPWAP) Working Group closed in 2009
Responded to requests from OPSAWG chairs for IEEE 802.11 review
  “Alternate Tunnel Encapsulation for Data Frames in CAPWAP” http://www.ietf.org/id/draft-zhang-opsawg-capwap-cds-02.txt , see Slide 5 in11-14-0368-01
  “IEEE 802.11 MAC Profile for CAPWAP” https://datatracker.ietf.org/doc/draft-ietf-opsawg-capwap-hybridmac/ , see 11-14-0684-01
  CAPWAP Hybrid MAC published as RFC7494, http://datatracker.ietf.org/doc/rfc7494/
  “CAPWAP extension for 802.11n and Power/channel Autoconfiguration” http://datatracker.ietf.org/doc/draft-ietf-opsawg-capwap-extension/ , see 11-14-0913-01
Updates [Nov 2016] Operations Area Working Group work group items
  Updated: The TACACS+ Protocol, see https://datatracker.ietf.org/doc/draft-ietf-opsawg-tacacs/
  Updated: In IESG evaluation: Alternate Tunnel Encapsulation for Data Frames in CAPWAP, see http://datatracker.ietf.org/doc/draft-ietf-opsawg-capwap-alt-tunnel/
  Of interest: RFC6632, An Overview of the IETF Network Management Protocols, see https://tools.ietf.org/html/rfc6632
  Of Interest: RFC7548, Management of Networks with Constrained Devices: Use Cases, see https://datatracker.ietf.org/doc/rfc7548/

## Slide 14: Transport Layer Security (TLS)
Transport Layer Security Working Group website: http://datatracker.ietf.org/wg/tls/charter/
Work underway on a new version of TLS (used in EAP methods): Transport Layer Security Protocol Version 1.3
Updates [Nov 2016]
  Updated: TLS version 1.3 https://datatracker.ietf.org/doc/draft-ietf-tls-tls13/
  Updated: Elliptic Curve Cryptography (ECC) Cipher Suites for Transport Layer Security (TLS) Versions 1.2 and Earlier, see http://datatracker.ietf.org/doc/draft-ietf-tls-rfc4492bis/

## Slide 15: Extensions for Scalable DNS Service Discovery (dnssd)
Working Group website: http://datatracker.ietf.org/wg/dnssd/charter/
Charter: Develop scalable DNS-SD/mDNS Extension requirements and standard solutions to address problematic use of mDNS and DNS-SD in networks today
  mDNS discovery of services on other links is not possible
  Multicast transmissions over wireless are very expensive
  Addressed with different ad hoc technologies
Of interest to: Homenet, Zero configuration, Enterprise-grade vendors of 802.11 infrastructure, Multi-link mesh networking
Updates [Nov 2016]
  Updated: Hybrid Multicast/Unicast DNS-Based Service Discovery, see https://datatracker.ietf.org/doc/draft-ietf-dnssd-hybrid/
  Updated: DNS Push Notifications, see https://datatracker.ietf.org/doc/draft-ietf-dnssd-push/
  New: Privacy Extensions for DNS-SD, see https://datatracker.ietf.org/doc/draft-ietf-dnssd-privacy/

## Slide 16: Of Interest: Network-Based Mobility Extensions (NETEXT)
NETEXT: http://datatracker.ietf.org/wg/netext/charter/
RFC 7561 published: Mapping PMIPv6 QoS Procedures with WLAN QoS Procedures, see http://datatracker.ietf.org/doc/rfc7561/
Abstract: This document provides guidelines for achieving end to end Quality- of-Service (QoS) in a Proxy Mobile IPv6 (PMIPv6) domain where the access network is based on IEEE 802.11. RFC 7222 describes QoS negotiation between a Mobility Access Gateway (MAG) and Local Mobility Anchor (LMA) in a PMIPv6 mobility domain. The negotiated QoS parameters can be used for QoS policing and marking of packets to enforce QoS differentiation on the path between the MAG and LMA. IEEE 802.11, Wi-Fi Multimedia - Admission Control (WMM-AC) describes methods for QoS negotiation between a Wi-Fi Station (MN in PMIPv6 terminology) and an Access Point. This document provides a mapping between the above two sets of QoS procedures and the associated QoS parameters. This document is intended to be used as a companion document to RFC 7222 to enable implementation of end to end QoS.

## Slide 17: Protocols for IP Multicast (PIM)
PIM: http://datatracker.ietf.org/wg/pim/charter/
  The Working Group charter includes: “Optimization approaches for IGMP and MLD to adapt to link conditions in wireless and mobile networks and be more robust to packet loss.”
  And a work item (April 2016) “submit solutions for IGMP and MLD to adapt to wireless link conditions”
  RFC 7761 published, Protocol Independent Multicast - Sparse Mode (PIM-SM): Protocol Specification (Revised), https://datatracker.ietf.org/doc/rfc7761/
Of interest:
  Updated: A YANG data model for Protocol-Independent Multicast (PIM), see https://datatracker.ietf.org/doc/draft-ietf-pim-yang/ and A YANG data model for Internet Group Management Protocol (IGMP) and Multicast Listener Discovery (MLD), see https://datatracker.ietf.org/doc/draft-ietf-pim-igmp-mld-yang/
  RFC 2236: Internet Group Management Protocol, Version 2 (IPv4), https://tools.ietf.org/html/rfc2236
  RFC 2710: Multicast Listener Discovery (MLD) for IPv6, https://www.ietf.org/rfc/rfc2710.txt

## Slide 18: Deterministic Networking (DETNET)
DETNET: https://datatracker.ietf.org/wg/detnet/charter/
  The Deterministic Networking (DetNet) Working Group focuses on deterministic data paths that operate over Layer 2 bridged and Layer 3 routed segments, where such paths can provide bounds on latency, loss, and packet delay variation (jitter), and high reliability.
  The Working Group addresses Layer 3 aspects in support of applications requiring deterministic networking.
  The Working Group collaborates with IEEE802.1 Time Sensitive Networking (TSN), which is responsible for Layer 2 operations, to define a common architecture for both Layer 2 and Layer 3.
  Example applications for deterministic networks include professional and home audio/video, multimedia in transportation, engine control systems, and other general industrial and vehicular applications being considered by the IEEE 802.1 TSN Task Group.
Of interest:
  New: DetNet Data Plane Protocol and Solution Alternatives, see https://datatracker.ietf.org/doc/draft-ietf-detnet-dp-alt/
  New: Deterministic Networking Architecture, see https://datatracker.ietf.org/doc/draft-ietf-detnet-architecture/
  Updated: Deterministic Networking Use Cases, see https://datatracker.ietf.org/doc/draft-ietf-detnet-use-cases/ (note 5.1.1, reference to WiFi)
  Updated: Deterministic Networking Problem Statement, see https://datatracker.ietf.org/doc/draft-ietf-detnet-problem-statement/
  Integrated Mobile Fronthaul and Backhaul, see https://datatracker.ietf.org/doc/draft-huang-detnet-xhaul/

## Slide 19: Active Queue Management (AQM)
Active Queue Management and Packet Scheduling Working Group website: http://datatracker.ietf.org/wg/aqm/charter/
IETF Recommendations Regarding Active Queue Management to update https://datatracker.ietf.org/doc/rfc2309/
Updates [Nov 2016]
  Updated: Controlled Delay Active Queue Management, see https://datatracker.ietf.org/doc/draft-ietf-aqm-codel/
  Draft “Guidelines for DiffServ to IEEE 802.11 Mapping”: https://tools.ietf.org/html/draft-ietf-tsvwg-ieee-802-11-00 . It is not intended to make any changes in priority mapping in 802.11 but does mention it extensively in Section 2. Also see https://www.ietf.org/proceedings/96/slides/slides-96-tsvwg-2.pdf .
  In RFC Editor queue: The Benefits and Pitfalls of using Explicit Congestion Notification (ECN), see http://datatracker.ietf.org/doc/draft-ietf-aqm-ecn-benefits/
  Published as RFC 7928: AQM Characterization Guidelines, see https://datatracker.ietf.org/doc/rfc7928/
  RFC 7567 published: IETF Recommendations Regarding Active Queue Management, see https://tools.ietf.org/html/rfc7567