## Slide 1: Proposed response to 3GPP ED request
Date: 2016-10-25
Authors:
Name | Company | Phone | email
Thomas Derham | Broadcom |  | thomas.derham@broadcom.com

## Slide 2: Context
IEEE 802 received an LS from 3GPP RAN1 in June 2016 as part of an ongoing discussion on coexistence of LAA and 802.11
  http://www.ieee802.org/Communications/16_06/R1-166040.zip
Along with responses to various concerns and questions raised by IEEE 802, this LS contains the following request:
  “RAN1 respectfully requests future IEEE 802.11 technologies to align the energy detection threshold used with other technologies operating in the same unlicensed band, e.g., -72 dBm. An energy detection threshold of -72 dBm has been chosen by 3GPP for Rel-13 LAA also with an interest in aligning with other technologies in the future.”
IEEE 802.11 WG created the “PDED ad hoc” to consider a potential response to this request

## Slide 3: Observations on 3GPP’s request
We assume the ED level “-72 dBm … chosen for Rel-13 LAA” referred to in RAN1’s request is actually short-hand for the sliding-scale ED threshold defined in LAA with the following upper and lower bounds:
  ED=-62 dBm at TxPower=+13 dBm
  ED=-72 dBm at TxPower=+23 dBm
We note 3GPP’s request refers to “future 802.11 technologies”, and assume it is limited to those future technologies that may operate in the same band as LAA
  i.e. 3GPP’s request relates to 802.11ax operating in 5 GHz band, but does not relate to 802.11 technologies operating in 2.4 GHz or other bands

## Slide 4: 802.11 coexistence mechanisms
802.11 devices are mandated to support Preamble Detect (PD) in addition to Energy Detect (ED)
PD is the primary coexistence mechanism between 802.11 devices
  PD is back-compatible across all generations of 802.11 technologies operating in 5 GHz band (11a, 11n, 11ac, and the under-development 11ax)
PD allows reliable detection of transmissions from coexisting devices at much higher sensitivity than is possible using ED
802.11 currently requires PD-based back-off at -82 dBm
  All 5 GHz 802.11 devices already detect and back-off to each other at a level that is between 10x and 100x more sensitive than the ED level requested by 3GPP
  Many current 802.11 devices actually back-off at even lower levels than required by the spec (e.g. <-90 dBm)
Per 802.11-2012 18.3.10.6, for OFDM transmissions (i.e. in 5 GHz band), CS/CCA shall detect a channel busy condition with a probability >90% within 4 us, for a receive level greater than or equal to -82 dBm for 20 MHz channel spacing

## Slide 5: 802.11ax coexistence mechanisms
802.11ax is still in early draft and is subject to significant change
802.11ax D0.5 includes optional Spatial Reuse feature OBSS_PD
  When an 11ax device detects an 802.11 transmission not in its own BSS, it may raise its PD level on a sliding scale with Tx Power
  The PD level allowed by the default sliding scale is basically 10 dB lower than the equivalent ED sliding scale in LAA
  Even with OBSS_PD, 11ax devices will by default back-off to other 802.11 transmissions at a level that is on average at least 10x more sensitive than the ED level requested by 3GPP
Chart: 
| 0 | 1 | 5 | 13 | 21 | 23 | 25 | 26
LAA | -62 | -62 | -62 | -62 | -70 | -72 | -72 | -72
11ax (Nss=1-2) | -62 | -62 | -66 | -74 | -82 | -82 | -82 | -82
11ax (Nss=3+) | -62 | -62 | -62 | -70 | -78 | -80 | -82 | -82
AP only
Transmit Power (dBm)
PD CCA (dBm)

## Slide 6: Optimizing 5 GHz band coexistence
We believe it is desirable for 5 GHz band technologies to evolve to optimize aggregate spectral efficiency while also protecting the ability of the band to be used in a wide range of use cases
  This means intelligent optimization of CCA levels to maximize spatial reuse when it is possible (e.g. in dense managed networks) while not causing undue impact to links that require protection from interference (e.g. weak signal strength links)
In that context, introducing a lower “blanket” ED level (-72 dBm at +23 dBm Tx Power) seems undesirable and counter-intuitive
  It may limit the spatial reuse gains that can be obtained by evolving technologies in scenarios that can support it
  It may still be insufficiently protective in other scenarios (as noted in the context of IEEE 802’s concerns about impact of -72 dBm ED on 802.11)
  It would have disproportionate impact on channel access by APs (operating at higher Tx Power), contrary to 802.11ax MAC efficiency enhancements that rely on coordination/scheduling by the AP (e.g. MU trigger frame based UL)

## Slide 7: Relationship with ETSI EN 301 893
It has been noted that future releases of ETSI EN 301 893 requirements for 5 GHz RLAN devices may incorporate ED-based CCA rules that are similar to those adopted by 3GPP LAA
However, we note that:
  ETSI adaptivity rules are subject to ongoing study and discussion, resulting in updated requirements on a regular basis.
  It can be imagined that future enhancements to these rules may address some of the issue described on the previous slide, with the objective of promoting more efficient use of the spectrum
  While ETSI requirements may be adopted by EU countries and potentially some other regulatory domains, there are also many other domains in which they will not apply.
  802.11-based device vendors may continue to ensure they abide by adaptivity requirements in each regulatory domain, irrespective of whether or not those requirements are mandated in the 802.11 specification

## Slide 8: Proposed response
IEEE 802 should respond to 3GPP stating the request is noted
IEEE 802 should reiterate its position that LAA adopting 802.11 PD and reservation signaling (e.g. CTS-to-self) is the best solution for coexistence in the 5 GHz band
  Better sensitivity, reliability and robustness (e.g. to noise) than ED; enables intelligent optimization of CCA thresholds over a broader range as technologies evolve
  Fully compatible with billions of legacy 802.11 devices (whereas any new ED would only apply to 11ax devices)
  Solves any imbalance between CCA levels of different coexisting technologies
  Simple and low-complexity to implement in devices
IEEE 802 and 3GPP may continue to study, communicate and collaborate towards optimizing coexistence between their respective technologies in the 5 GHz band