## Slide 1: MAC support of preamble puncture
Date: 2016-11-04
Authors:
Name | Affiliation | Address | Phone | Email
Zhou Lan | Broadcom |  |  | 
Matthew Fischer |  |  |  | mfischer@broadcom.com
Sriram Venkateswaran |  |  |  | 
Ron Porat |  |  |  | rporat@broadcom.com
Leo Montreuil |  |  |  | 
Andrew Blanksby |  |  |  | 
Vinko Erceg |  |  |  | 

## Slide 2: Authors (continued)
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Laurent Cariou |  |  |  | laurent.cariou@intel.com
Yaron Alpert |  |  |  | yaron.alpert@intel.com
Assaf Gurevitz |  |  |  | assaf.gurevitz@intel.com
Ilan Sutskover |  |  |  | ilan.sutskover@intel.com

## Slide 3: Authors (continued)
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Yakun Sun |  |  |  | yakunsun@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Bo Yu |  |  |  | boyu@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Xiayu Zheng |  |  |  | xzheng@marvell.com
Christian Berger |  |  |  | crberger@marvell.com
Niranjan Grandhe |  |  |  | ngrandhe@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 4: Authors (continued)
Name | Affiliation | Address | Phone | Email
Alice Chen | Qualcomm | 5775 Morehouse Dr. San Diego, CA, USA |  | alicel@qti.qualcomm.com
Albert Van Zelst |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Arjun Bharadwaj |  | 5775 Morehouse Dr. San Diego, CA, USA |  | arjunb@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Lin Yang |  | 5775 Morehouse Dr. San Diego, CA, USA |  | linyang@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Naveen Kakani |  | 2100 Lakeside Boulevard Suite 475, Richardson TX 75082, USA |  | nkakani@qti.qualcomm.com
Raja Banerjea |  | 1060 Rincon Circle San Jose CA 95131, USA |  | rajab@qit.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com

## Slide 5: Authors (continued)
Name | Affiliation | Address | Phone | Email
Rolf De Vegt | Qualcomm | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tao Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | ttian@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com

## Slide 6: Authors (continued)
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com
Name | Affiliation | Address | Phone | Email
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Chingwa Hu |  |  |  | chinghwa.yu@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
Thomas Pare | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Jianhan Liu |  |  |  | Jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com

## Slide 7: Authors (continued)
Name | Affiliation | Address | Phone | Email
Peter Loc | Huawei |  |  | peterloc@iwirelesstech.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Rob Sun |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Rob.Sun@huawei.com
David X. Yang |  | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com
Edward Au |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | edward.ks.au@huawei.com
Teyan Chen |  | F1-17, Huawei Base, Bantian, Shenzhen |  | chenteyan@huawei.com
Yunbo Li |  | F1-17, Huawei Base, Bantian, Shenzhen |  | liyunbo@huawei.com

## Slide 8: Authors (continued)
Name | Affiliation | Address | Phone | Email
Jinmin Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | Jinmin1230.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
JayH Park |  |  |  | Hyunh.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Thomas Derham | Orange |  |  | thomas.derham@orange.com
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com

## Slide 9: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan | +81 46 859 3135 | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  | +81 46 859 5097 | inoue.yasuhiko@lab.ntt.co.jp
Shoko Shinohara |  |  | +81 46 859 5107 | Shinohara.shoko@lab.ntt.co.jp
Yusuke Asai |  |  | +81 46 859 3494 | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  | +81 46 859 4233 | ishihara.koichi@lab.ntt.co.jp
Junichi Iwatani |  |  | +81 46 859 4222 | Iwatani.junichi@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan | +81 46 840 3759 | yamadaakira@nttdocomo.com

## Slide 10: Authors (continued)
Name | Affiliation | Address | Phone | Email
Masahito Mori | Sony Corp. |  |  | Masahito.Mori@jp.sony.com
Yusuke Tanaka |  |  |  | YusukeC.Tanaka@jp.sony.com
Yuichi Morioka |  |  |  | Yuichi.Morioka@jp.sony.com
Kazuyuki Sakoda |  |  |  | Kazuyuki.Sakoda@am.sony.com
William Carney |  |  |  | William.Carney@am.sony.com
Minho Cheong | Newracom, Inc. | 9008 Research Dr, Irvine, CA 92618 | +1-949-390-7146 | minho.cheong@newracom.com
Reza Hedayat |  |  |  | reza.hedayat@newracom.com
Young Hoon Kwon |  |  |  | younghoon.kwon@newracom.com
Yongho Seok |  |  |  | yongho.seok@newracom.com
Daewon Lee |  |  |  | daewon.lee@newracom.com
Yujin Noh |  |  |  | yujin.noh@newracom.com
Sigurd Schelstraete | Quantenna | 3450 W. Warren Ave, Fremont, CA 94538 |  | Sigurd@quantenna.com
Huizhao Wang |  |  |  | hwang@quanetnna.com

## Slide 11: Abstract
D0.5 supports dynamic channel bonding by defining preamble punctured HE MU PPDU
  The non-contiguous channel bonding will be supported in 802.11ax by:
    Transmitting using OFDMA PPDU format by nulling the tones of one or more secondary channels in 80 MHz and 160 (80+80) MHz;
    Modes for non-contiguous channel bonding are TBD;
    Non-contiguous channels within primary or secondary 80 MHz only exists at AP side.
MAC support on preamble puncture mode is not well defined
November, 2016
Slide 11
Zhou Lan, Broadcom et al

## Slide 12: Current rule settings
Spec framework r17:MU-RTS shall not be carried in an HE MU PPDU. The CTS response to an MU-RTS shall be carried in a non-HT or a non-HT duplicate PPDU
D0.5: The RU Allocation subfield in the User Info field addressed to the STA indicates either the primary 20 MHz channel, primary 40 MHz channel, primary 80 MHz channel, 160 MHz channel, or 80+80 MHz channel
D0.5: The CTS frame sent in response to an MU-RTS frame shall be carried in a non-HT or non-HT duplicate PPDU
Baseline (section 10.22.2.7): If a TXOP is protected by an RTS or CTS frame carried in a non-HT or a non-HT duplicate PPDU, the TXOP holder shall set the TXVECTOR parameter CH_BANDWIDTH of a PPDU as follows:
  To be the same or narrower than RXVECTOR parameter CH_BANDWIDTH_IN_NON_HT of the last received CTS frame in the same TXOP, if the RTS frame with a bandwidth signaling TA and TXVECTOR parameter DYN_BANDWIDTH_IN_NON_HT set to Dynamic has been sent by the TXOP holder in the last RTS/CTS exchange.
  Otherwise, to be the same or narrower than the TXVECTOR parameter CH_BANDWIDTH of the RTS frame that has been sent by the TXOP holder in the last RTS/CTS exchange in the same TXOP.
    Assuming MU-RTS will inherit the same rule here
Baseline (section 10.22.2.7): Note that when transmitting multiple frames in a TXOP using acknowledgment mechanisms other than Normal Ack, a protective mechanism should be used
November, 2016
Slide 12
Zhou Lan, Broadcom et al

## Slide 13: One example
MU-RTS
Simultaneous CTS
Simultaneous CTS
Simultaneous CTS
Channel1 (primary channel )
Channel2
Channel3
Channel4
Channel5
Channel6
Channel7
Channel8
STA 1, 2, 3, 4, 5, 6, 7, 8
STA 1, 2, 3, 4, 5, 6, 7, 8
STA 2 40 MHz
STA 1 20 MHz
DATA
BA
STA 1
STA 2
STA 8
STA 1
STA 2
STA 8
STA 6
STA 5
STA 6
STA 5
STA 4
STA 4
Non-HT PPDU
HE PPDU
NAV
SIFS
Simultaneous CTS
Simultaneous CTS
SIFS
SIFS
Current rule prevents data transmission on these secondary channels even if preamble punctured mode is introduced
Assumption:
  AP finds 160MHz channel are NOT clear (channel 3 and 5 are not clear according to the sensing results)
  AP attempts to schedule 8 users
    STA 1: channel 1, 242 RU, STA 2:channel 2, 242 RU, STA 3: channel 4, 106 RU, STA 4: channel 4, 106 RU, STA 5:channel 6, 106 RU, STA 6: channel 6, 106RU, STA7: channel 7, 242 RU, STA 8: channel 8, 242 RU
  STA 3 finds channel 4 is busy, STA 7 finds channel 7 is busy
Preamble puncture mode can not be used due to the rule setting on MU-RTS and EDCA TXOP multiple frame transmission rule
Even if we change the EDCA TXOP multiple frame transmission rule to allow MU-RTS solicit DL PPDU with bigger bandwidth, the DL data PPDU are not protected on secondary channels
Slide 13
Zhou Lan, Broadcom et al

## Slide 14: DL General protocol
MU-RTS
Simultaneous CTS
A-MPDU
BA
Extra protection from legacy STAs
160 MHz
Simultaneous CTS
Simultaneous CTS
Primary 20MHz channel
In legacy format non HT or non HT DUP
Channel information in scramble initial value or control wrapper
BQRP
In HE PPDU (preamble puncture mode)
Channel information in SIG-A SIG-B of MU RTS
Data transmissions
Bandwidth Query
Non-HT PPDU
HE PPDU
Define a Bandwidth Query operation procedure
The Bandwidth Query frame exchange may happen before the MU-RTS/CTS (in legacy format) exchange
BQR
Slide 14
Zhou Lan, Broadcom et al

## Slide 15: DL protocol example 1
Example 1:
  AP finds 160MHz channel are NOT clear (channel 3 and 5 are not clear according to the sensing results)
  AP attempts to schedule 8 users
    STA 1: channel 1, 242 RU, STA 2:channel 2, 242 RU, STA 3: channel 4, 106 RU, STA 4: channel 4, 106 RU, STA 5:channel 6, 106 RU, STA 6: channel 6, 106RU, STA7: channel 7, 242 RU, STA 8: channel 8, 242 RU
    Implementation choice: Use one 26 RU of the 80MHz to set a broadcast RU for a empty MU-RTS (A MU RTS frame with no STAs named)
      To mute all the HE STAs who is not participating this TXOP
  STA 3 finds channel 4 is busy, STA 7 finds channel 7 is busy
Define a new trigger variant (Bandwidth Query Report Poll) to solicit trigger based PPDU with a new A-control field (Bandwidth Query Report)
MU-RTS
Simultaneous CTS
Simultaneous CTS
Simultaneous CTS
Channel1 (primary channel )
Channel2
Channel3
Channel4
Channel5
Channel6
Channel7
Channel8
STA 1, 2, 3, 4, 5, 6, 7, 8
STA 1, 2, 3, 4, 5, 6, 7, 8
STA 2 40 MHz
STA 1 20 MHz
BQRP
STA 1
STA 2
STA 3
STA 7
STA 8
BQR
STA 1
STA 2
STA 3
STA 4
STA 6
STA 7
STA 8
DATA
BA
STA 1
STA 2
STA 8
STA 1
STA 2
STA 8
STA 5
STA 6
STA 5
STA 6
STA 5
STA 4
STA 4
STA 4
STA 5
STA 6
Non-HT PPDU
HE PPDU
NAV
Slide 15
Zhou Lan, Broadcom et al

## Slide 16: Straw poll
Do you support to update11ax draft specification D0.5 according to editor instruction in document 802.11-16/1383r1.
  A HE AP transmits a new trigger variant (Bandwidth Query Report Poll) to solicit bandwidth Query Report from one or multiple HE non AP STAs
  A HE non AP STA after receiving Bandwidth Query Report Poll from a HE AP responds with channel availability information in a new A-control field (Bandwidth Query Report)
  It is optional for a non AP STA to support the Bandwidth Query mechanism
  Yes
  No
  Abstain
Slide 16
Zhou Lan, Broadcom et al