## Slide 1: Power Efficient WUR AP Discovery
Date: 2016-11-07
Authors:

## Slide 2
Abstract
In this contribution, we discuss issues related to AP discovery using WUR when the AP is in the sleep mode.

## Slide 3: Introduction
Traditionally, an 802.11 STA may utilize two methods for AP discovery
  Passive scanning: by monitoring APs’ Beacons, Measurement Pilots, FILS Discovery frames, etc.
  Active scanning: by transmitting Probe Request frames to solicit Probe Response frames from APs
For APs equipped with WURs, APs’ primary connectivity radios may be in the sleep mode for an extended period of time with their WUR turned on [1]
  A STA may not be able to readily discover the presence of the desired AP
  A similar mechanism to active scanning may be desired for WUR STAs that require low latency, and hence speedy AP discovery and association

## Slide 4: Active Scanning for WUR (1)
A WUR STA can send a wake up frame to wake up one or more WUR APs to discover a suitable AP
  Such wake up frames can be either a unicast or a broadcast frame
Unicast wake up frame is power efficient
  Only one AP needs to evaluate the frame and turn on its primary connectivity radio if needed
However, unicast wake up frame for a specific AP is not always possible
  The initiating STA must know the BSSID/identifier of the desired AP
  Could be time consuming
  May be useful when the STA has pre-acquired knowledge of the presence of the AP, e.g.:
    From a previous association (and maybe some information, such as location)
    Directed by other APs

## Slide 5: Active Scanning for WUR (2)
Broadcast wake up frame may be very inefficient in power consumption
  All APs must decode the entire wake up frame
  Without specific information, it is hard for the receiving APs to decide individually whether they should turn on their primary connectivity radio
    The STA only needs to associate with one AP
    Wasteful for many APs to turn on their primary connectivity radios and transmit beacon/probe response
    Too many Beacon/Probe Responses frames already! [3]
  Malicious devices may want to wake up APs often to drain their batteries [3]
    APs could be obvious targets for attacks on the WLAN networks
Some optimization may be desired.

## Slide 6: Active Scanning for WUR (3)
Not all APs need to wake up when receiving a broadcast wake up frame meant for AP discovery
  If a STA desires APs with, e.g., a certain SSID, then an AP of a different SSID need not to wake up, i.e., turning on their primary connectivity radio
Otherwise, that AP just wastes power by:
  Turning on its primary connectivity radio
  Waiting for a Probe Request; or send a Beacon/Probe Response
  AP may turn off primary connectivity radio after receiving a Probe Request with no matching SSID, or after responding with a Probe Response and don’t hear from the STA after some timeout duration
  In summary, nothing is achieved but energy was wasted

## Slide 7: Active Scanning for WUR (4)
More power efficient to have the initiating STA including information on desired BSS’s or SS’s in the broadcast wake up frame
  APs with different BSSIDs/SSIDs can ignore the wake up frame
  Further optimization is possible for APs of the desired SSID
Other optimization may also be desired to avoid that APs needlessly turn on their primary connectivity radios

## Slide 8: Conclusion
A WUR AP discovery mechanism similar to active scanning for regular 802.11 STAs may be desirable for fast AP discovery and association
Broadcast wake up frame used for AP discovery can be very inefficient in power consumption, but may be necessary in some scenarios
Including one or more BSSID/SSID in the broadcast wake up frames used for AP discovery can provide power saving for WUR AP discovery

## Slide 9
References
[1] 11-16/1045r6, A Proposed PAR for Wake Up Radio, Sept. 2016
[2] 11-16/0939r1, WUR-based Power Save Operations for AP, July 2016
[3] 11-11-1413r3, Real air-time occupation by beacon and Probe, January 2012
[4] 11-16/0927r0, Securing the WUR, July 2016