## Slide 1: DL/UL indication in MU-RTS
Date: 2016-11-07
Authors:

## Slide 2: Abstract
In this contribution, we propose to define DL/UL indication in MU-RTS variant Trigger frame by using Cascade Indication field

## Slide 3: MU-RTS procedure for MU transmission
AP may send MU-RTS variant Trigger frame to protect both DL and UL MU transmission
  In DL MU, HE MU PPDU follows right after simultaneous CTS
  In UL MU, another basic variant Trigger frame follows after simultaneous CTS
In UL MU procedure, Trigger frame requires a large amount of processing load for UL STAs during SIFS
  CCA, A-MPDU packing within a given duration etc.
    Trigger frame MAC padding is proposed to allow additional processing time for UL STAs
  It is recommended to ease the processing load for STAs with low processing power
MU-RTS
S-CTS
HE MU PPDU
UL ACK
AP
STAs
MU-RTS
S-CTS
HE TRIG PPDU
DL ACK
AP
STAs
TF

## Slide 4: Recap: Cascade Indication in Trigger frame
Trigger frame contains Cascade Indication field
  1-bit indication in common info field
  Indicating the presence of a subsequent trigger frame
Currently used in a limited number of cases
  TWT operation, power save with UL OFDMA-based random access
  Reserved in other cases

## Slide 5: Exploiting Cascade Indication in MU-RTS
In MU-RTS procedure of UL MU, a standalone basic variant Trigger frame always follows subsequently after simultaneous CTS
  No subsequent standalone Trigger frame for DL MU
The Cascade Indication in MU-RTS can be used to distinguish whether the following procedure is DL MU or UL MU
In case of UL MU, UL STA might prepare the UL MU transmission prior to the following basic-variant Trigger frame

## Slide 6: Advantages of DL/UL indication
If the Cascade Indication subfield indicates the following procedure is UL MU;
  STAs solicited in the MU-RTS could have more additional time to prepare UL MU transmission
  STAs not supposed to participate in UL MU might get into sleep mode earlier
    E.g., UL MU disabled STAs, STAs with empty buffer
Straightforward and aligned with the current usages
  Having the same meaning with other Cascade Indications
    Subsequent Trigger frame
  No ambiguity with other Cascade Indications
    MU-RTS is always used with UL/DL MU procedure

## Slide 7: Conclusion
In this contribution, we have proposed to use the Cascade Indication in the MU-RTS variant Trigger frame as a DL/UL indication

## Slide 8: Strawpoll
Do you agree to instruct TGax Editor to make the following change:
TGax Editor: change the paragraph below of 9.3.1.23 (Trigger frame format) as follows:
If the Cascade Indication subfield is 1, then a subsequent Trigger frame as defined in 10.3.2.8a.2 (MU-RTS procedure) and in 25.7 (TWT operation) and in 25.15.2 (Power save with UL OFDMA-based random access) follows the current Trigger frame. Otherwise the Cascade Indication subfield is 0.
TGax Editor: insert the paragraph below of 9.3.1.23.4 (MU-RTS variant) as follows:
The Cascade Indication subfield is set to 1 when the following procedure is UL MU and set to 0 when the following procedure is DL MU.