## Slide 1: Overall MAC Procedure for WUR
Date: 2016-11-7
Authors:
Name | Affiliation | Address | Phone | Email
Kiseon Ryu | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | kiseon.ryu@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Jayh Park |  |  |  | hyunh.park@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com

## Slide 2: Abstract
This presentation introduces overall WUR MAC procedure that we can consider
  Mode transition between WUR and WLAN modes
  WLAN packet Tx to WUR STA
  WUR error recovery
  Consideration on wake-up packet
  WUR keep-alive check

## Slide 3: Overall MAC Procedure for WUR

## Slide 4: WUR Mode Signaling
After the association procedure or receiving DL data completely, a STA may request to enter WUR mode for low power operation
After receiving the confirmation (i.e., WUR mode response) from the AP, a STA enters the WUR mode
For this procedure, an explicit WUR mode signaling is needed
  If the STA does not inform its 802.11 main radio turning off, then WUR AP can send 802.11 frames to the STA without sending WUR packet and it can be lost
  WUR operating parameter can be negotiated during WUR mode signaling

## Slide 5: WLAN packet transmission to WUR STA
Whenever an AP wants to send a WLAN packet to a STA in WUR mode, WUR packet should be transmitted to wake up the station
  After transmitting a WUR packet, AP should wait for a specific time before sending a WLAN data frame. WLAN main radio turn-on time can take about a few millisecond.
  Before WLAN packet transmission, STA’s wake-up can be confirmed through the existing WLAN control signaling (e.g., RTS/CTS, PS-Poll)

## Slide 6: WUR Error Recovery
To handle the case that wakeup signaling fails, an error recovery mechanism shall be provided.
  When an AP sends data frame after WUR packet and does not receive ACK/BA, AP has to retransmit WUR packet or data frame.
  For the case of PS-Poll transmission in response to WUR packet, AP has to retransmit WUR packet if PS-Poll is not received within the certain period after sending WUR packet.
  Retransmission policy at AP should be defined to reduce power consumption and overhead

## Slide 7: Consideration on WUR packet
Multi-user WUR packet
  WUR packet should be able to wake up a single receiver or multiple receivers at the same time (Multi-user wake-up)
  Multi-user wake-up can reduce the contention or collision with WLAN/WUR packets in dense environment
  WUR packet can be sent for waking up all WUR receivers (e.g., DTIM traffic)
Address in WUR packet
  WUR packet minimizes the false alarm of wake-up to avoid unnecessary power consumption of the WUR receiver
  Using unique receiver address (e.g., MAC Address) may increase the length of WUR packet
Multi-user wake-up should be considered in WUR packet design
Reduction of overhead and false alarm need to be considered for designing WUR packet

## Slide 8: WUR Keep Alive Check
WUR STA needs to know whether or not it is still in the TX range of the WUR AP [1]
WUR keep-alive check
  If a STA in WUR mode does not receive any WUR packet from the WUR AP for a specific time duration, the STA needs to check if its transmitter is available or not.
    Passive method: The STA listens to any WLAN packet from its associated AP,
    Active method: The STA sends a WLAN frame (e.g., Probe Request, etc) for Keep alive checking.
  If the STA detects WLAN packet or receives response from its associated AP, the STA re-enters the WUR mode. Otherwise, STA may perform scanning procedure for discovering other BSS

## Slide 9: Conclusion
For defining WUR MAC protocol, the following MAC functionalities needs to be provided
  Mode transition between WUR and WLAN modes
  Reliable WUR/WLAN packet transmission to WUR STA
  WUR packet error recovery
  WUR packet design considering low overhead/false alarm probability
  WUR keep-alive check

## Slide 10: References
11-16/1217 WUR-based Broadcast Reference Signal