## Slide 1: WUR MAC Consideration
Date: 2016-11-06
Authors:
Name | Affiliation | Address | Phone | Email
Liwen Chu | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | liwenchu@marvell.com

## Slide 2: Overview
Some high-level MAC aspects of WUR are considered:
  Wakeup handshake approaches
  Single STA wake-up and multi-STA wake-up
  EDCA Discussion
  Beacon Discussion
  Security discussion

## Slide 3: Wakeup Handshake 1: Handshake through LP antenna and 802.11 antenna
Wakeup Req is the low power frames.
802.11 frame, e.g. PS-Poll, QoS Null, RTS is the acknowledgement of Wakeup Req.
  LP Wakeup Req and its acknowledgement frame are transmitted in different TXOP.
After receiving the acknowledgement from the STA, the AP transmits date frame to the STA.
  The AP shall be ready to transmit the data frame after receiving the acknowledgement frame.
It is difficult to predict whether the STA receives wakeup request correctly.
LP Wakeup Req
.11PHY Header
Lower Power PPDU
.11PHY Header
Data MPDU
.11PHY Header
Ack
WUR AP
WUR STA
TXOP
.11PHY Header
PS-Poll
TXOP

## Slide 4: Wakeup Handshake 2: Handshake Through Lower Power Antenna only
Wakeup Req, Wakeup Res is the low power frames (LP frame).
The handshake exchange and the following data frame exchange is in same TXOP.
  EIFS protection is used here.
If the preparing procedure of 11 antenna at STA side needs long time, the wakeup stage and frame exchange stage can be in different TXOPs.
.
  .
LP Wakeup Res
LP Wakeup Req
.11PHY Header
Lower Power PPDU
EIFS Timer
EIFS Timer
.11PHY Header
Data MPDU
.11PHY Header
Ack
WUR AP
WUR STA
WUR AP’s Neighbor
WUR STA’s Neighbor
TXOP
X
Reset EIFS timer

## Slide 5: Single STA Wakeup and Multiple STA Wakeup
The Wakeup Request should at least include AP’s identifier, identifier of the STA(s).
AP’s identifier can be the BSS color announced in AP’s Beacon or AP’s MAC address.
An AP may wakeup one STA at a time for unicast frame exchange.
  The STA’s identifier in WakeUp Request frame can be STA’s AID.
An AP may wakeup one STA at a time for broadcast frame exchange.
  The STA’s identifier in WakeUp Request frame can be a specific AID, e.g. AID 0, AID of virtual AP defined by TIM, AID 2047 for STAs associated with multiple virtual APs.
An AP may wakeup multiple STAs at a time for multicast frame exchange.
  A multicast identifier can be defined or broadcast identifier can be used.
Broadcast Wakeup Request can also be used for Beacon transmission announcement.
  With this the discovery of Beacon can use less power.

## Slide 6: EDCA for Wakeup STA
If the wakeup STAs use normal EDCA parameters to transmit PS-Poll frame, the STA may waste its energy.
The AP can defines a new EDCA parameter set for wakeup STA’s medium access whose default values have higher priority.
  The AP can broadcast the EDCA parameter set for wakeup STA’s medium access.
LP Wakeup Req
.11PHY Header
Lower Power PPDU
.11PHY Header
Data MPDU
.11PHY Header
Ack
WUR AP
WUR STA
TXOP
.11PHY Header
PS-Poll
TXOP

## Slide 7: Beacon Discussion
Since the STA will not periodically wakeup to receive the beacons.
  The information in the beacon for associated STAs is not needed. E.g. TIM, channel switch etc.
The Beacons are only used for AP/BSS discovery, e.g.
  EDCA parameters, AP’s Capabilities (supported Rate/MCS etc.), Operation parameters (primary channel, BSS bandwidth etc.), Security.

## Slide 8: Security for handshaking
If another STA keeps Sending wakeup signal to a WUR STA, WUR STA will waste its energy.
One solution is to encrypt the LP Wakeup Req.
Another solution could be Wakeup Request frame carries secret information that both AP and destined STA aware.