## Slide 1: Wake-up and Data Exchange Sequences
Date: 2016-11-08
Authors:

## Slide 2: Introduction
In WUR PAR proposal [1], requirements for latency is defined
  In scenarios where low latency is a requirement, the WUR should decrease overall power consumption of the STA without significant increase in latency (relative to the current maximum latency of the nominal duration of one beacon interval, 102.4 ms) in transferring user data packets.
Typical WUR sequence would be composed of
  Wake-up packet reception
  Wake-up delay (internal power state transition time of 802.11 transceiver)
  802.11 User Data exchange
In this submission, we discuss several WUR sequences comparing the recovery latency after the failed wake-up packet transmission
Wake-up Delay
Backoff
802.11
WUR
802.11
Wake-up packet
User
Data Exchange
Deep sleep
Deep sleep
wake-up signal

## Slide 3: Wake-up delay defined in 11ax
Sleep States and their Transition times defined in 11ax simulation scenario [2]
  Shallow Sleep power state of a wireless module is defined as a sleep state with baseband and MAC processors turned on, but RF is switched off.
  Deep Sleep power state of a wireless module is defined as a sleep state with the wireless radio turned off, i.e., RF, baseband and MAC processors are all switched off. The only power consumed by the wireless module is leakage power.
  WUR-based sleep state would be similar to the Deep sleep state minimizing power consumption
We can assume the wake-up delay (sleep to listen state transition time) would be several milliseconds
Power Transition parameters | 
State Transitions | Transition Time
Shallow Sleep  Listen | 0.5 ms
Deep Sleep  Listen | 10 ms

## Slide 4: WUR sequence 1 : DL Data
WUR sequence
  AP transmits wake-up packet to WUR STA
  After STA’s wake-up delay, AP transmits downlink data to STA
Recovery from the failed WUP
  If the first data transmission is not acknowledged, AP should assume the previous wake-up packet transmission was failed
  AP should retransmit the wake-up packet
Latency
  The failed wake-up packet transmission is indicated only after
    Wake-up delay + Channel access + DL Data + SIFS
DL Data
Backoff
Wake-up Delay
Backoff
802.11
WUR
802.11
Wake-up packet
Deep sleep
wake-up signal
Ack
indicator for the successful WUP transmission

## Slide 5: WUR sequence 2: UL Poll
WUR sequence
  AP transmits wake-up packet to WUR STA
  After STA’s wake-up delay, STA transmits uplink Poll to AP
  AP transmits downlink data to STA
Recovery from the failed WUP
  If AP does not receive the uplink Poll within a timeout period, AP should retransmit the wake-up packet
Latency
  The failed wake-up packet transmission is indicated only after
    Timeout = Wake-up delay + Channel access + UL Poll + (some margin)
Wake-up Delay
Backoff
802.11
WUR
802.11
Wake-up packet
Deep sleep
wake-up signal
Ack
DL Data
Backoff
Poll
Ack
Backoff
Timeout
indicator for the successful WUP transmission

## Slide 6: WUR sequence 3: WUR Ack
WUR sequence
  AP transmits wake-up packet to WUR STA
  STA responses with WUR Ack
  After STA’s wake-up delay, AP transmits downlink data to STA
Recovery from the failed WUP
  If AP does not receive the WUR Ack, AP should retransmit the wake-up packet
Latency
  The failed wake-up packet transmission is indicated after SIFS
Discussions
  STA’s wake-up radio should have capability to send WUR Ack packet
  AP’s WUR or 802.11 should have capability to receive WUR Ack packet
  WUR Ack packet may not have legacy preamble
Backoff
Wake-up Delay
Backoff
802.11
WUR
802.11
Wake-up packet
Deep sleep
wake-up signal
Ack
WUR
Ack
WUR
DL Data
indicator for the successful WUP transmission

## Slide 7: Recovery from Wake-up packet failures
The wake-up delay (internal state transition time) can be quite large, i.e. several milliseconds, considering the current 802.11 transceiver implementations
After the failed wake-up packet transmission, it’d be better to have immediate recovery sequence to minimize the overall data delivery latency
Wake-up Packet
Transmission
802.11 Data
Exchange
wake-up delay
Immediate
Recovery Procedure
Late
Recovery Procedure

## Slide 8: Conclusions
For low latency required scenarios, WUR sequence design should minimize the overall latency in transferring user data to STA
We discussed several wake-up and data exchange sequences, and compared their recovery latencies when wake-up packet transmission is failed
Due to the long wake-up delay, we propose that WUR design should consider an immediate acknowledgement mechanism after wake-up packet reception

## Slide 9: References
  [1] 11-16/1045r6, A Par Proposal for Wake-up Radio
  [2] 11-14/0980r16, TGax Simulation Scenarios
  [3] 11-16/0341r0, LP-WUR (Low-Power Wake-Up Receiver) Follow-Up