## Slide 1: Rate 7/8 LDPC Code for 11ay
Date: 2016-11-10
Authors:

## Slide 2: Introduction
An LDPC code of rate 7/8 [1] was adopted in 802.11REVmc [2]
- to further increase the data rate of 802.11ad. By combining the 64QAM modulation, the peak data rate of DMG single carrier can be up to 8Gbps;
- to fill a gap between MCS9 (QPSK, code rate 13/16) and MCS10 (16QAM, code rate 5/8) in 802.11ad. Currently the gap is about 4 dB;
- to fill a gap between the MCS of16QAM and the highest rate and the MCS of 64QAM and the lower rates.
The proposed rate 7/8 LDPC code [1] is generated by puncturing the first 48 parity bits from rate 13/16 LDPC code words. The LDPC code of rate 13/16 is specified in 802.11ad.
Since the punctured rate 7/8 code has not been optimized, its performance may require to improve.
Since the new rate 7/8 LDPC code is obtained by puncturing the rate 13/16 11ad LDPC code, the codeword length is 624 (no longer to be 672). This will impact on the implementation of the bit-symbol mapping at the transmitter and the decoding at the receiver.
Another rate 7/8 LDPC code which keeps the codeword length 672 unchanged. Its parity check matrix is generated by removing the first row of the parity-check matrix of rate 13/16 LDPC specified in 11ad [3].

## Slide 3: Rate 3/4 and 13/16 LDPC Codes in 11ad [4]
Rate-3/4 LDPC code matrix H = 168 rows x 672 columns, Z = 42
Rate-13/16 LDPC code matrix H = 126 rows x 672 columns, Z = 42

## Slide 4: Rate 7/8 LDPC Code in 802.11REVmc [1][2]
Rate 7/8 LDPC introduced in [2] is generated by puncturing the first 48 parity bits from rate 13/16 code words
It uses existing LDPC matrix of rate 13/16.
Transmitter does not transmit the punctured bits; receiver puts equal likelihood for 1/0 for these bits.
The lengths of a source word and a codeword of the rate 7/8 code are 546 and 624. The codeword length is different from 672 as other LDPC codes of different rates in 802.11ad.

## Slide 5: SC Blocking in 11ad and in 11REVmc [1]
SC QPSK Blocking in 802.11ad
Source
word1
Codeword1
672
(bits)
encoding
Bit-to-symbol mapping
blocking
BLK 1
BLK 2
BLK 3
448
448
448
(symbols)
Codeword2
Codeword3
Codeword4
672
672
672
Codeword1
336
(symbols)
Codeword2
Codeword3
Codeword4
336
336
336
Source
word2
Source
word3
Source
word4
SC QPSK Blocking (rate 7/8) in 802.11REVmc
Source
word1
Codeword1
624
(bits)
encoding
Bit-to-symbol mapping
blocking
BLK 1
448
448
448
(symbols)
Codeword2
…
Codeword56
624
624
Codeword1
312
(symbols)
Codeword2
…
Codeword56
312
312
Source
word2
…
Source
word56
Note: Every three blocks are constructed from four codewords
(Each block is constructed from two codewords.)
Note: Every 39 blocks are constructed from 56 codewords
(Each block is constructed from two or three codewords.)
BLK 2
…
BLK 39

## Slide 6: SC Blocking in 11ad and in 11REVmc [1]
Note: Every three blocks are constructed from seven codewords.
(each block is constructed from three or four codewords)
Note: Every 39 blocks are constructed from 112 codewords.
(each block is constructed from three or four codewords.)
SC 16QAM Blocking in 802.11ad
Source
word1
Codeword1
672
(bits)
encoding
Bit-to-symbol mapping
blocking
BLK 1
BLK 2
BLK 3
448
448
448
(symbols)
Codeword2
…
Codeword7
672
672
Codeword1
168
(symbols)
Codeword2
…
Codeword7
168
168
Source
word2
…
Source
word7
SC 16QAM Blocking (rate 7/8) in 802.11REVmc
Source
word1
Codeword1
624
(bits)
encoding
Bit-to-symbol mapping
blocking
448
448
448
(symbols)
Codeword2
…
Codeword112
624
624
Codeword1
156
(symbols)
Codeword2
…
Codeword112
156
156
Source
word2
…
Source
word112
BLK 1
BLK 2
…
BLK 39

## Slide 7: SC Blocking for 7/8 LDPC (n=672, k=588) and 802.11REVmc [1]
Expected SC 64QAM Blocking
(rate 7/8, codeword length=672)
Source
word1
Codeword1
672
(bits)
encoding
Bit-to-symbol mapping
blocking
BLK 1
448
(symbols)
Codeword2
Codeword3
Codeword4
672
672
672
Codeword1
112
(symbols)
Codeword2
Codeword3
Codeword4
112
112
112
Source
word2
Source
word3
Source
word4
SC 64QAM Blocking (rate 7/8) in 802.11REVmc
Source
word1
Codeword1
624
(bits)
encoding
Bit-to-symbol mapping
blocking
448
448
448
(symbols)
Codeword2
…
Codeword56
624
624
Codeword1
104
(symbols)
Codeword2
…
Codeword56
104
104
Source
word2
…
Source
word56
Note: Each block is constructed from four codewords.
Note: Every 13 blocks are constructed from 56 codewords
(each block is constructed from five or six codewords )
BLK 1
BLK 2
…
BLK 13

## Slide 8: Rate 7/8 LDPC (n=672, k=588) [3] – Obtained by Modifying the Parity-Check Matrix of 13/16 LDPC
The rate 13/16 code of the 802.11ay standard is modified by eliminating its first row of its parity-check matrix to generate the parity-check matrix of the rate 7/8 LDPC., i.e., a matrix with H = 84 rows x 672 columns. The codeword length 672 is preserved.
-
However, as shown in [2] the performance of this proposal is not satisfactory.

## Slide 9: New rate 7/8 LDPC codes (n=672, k=588) based on the 11ad 3/4 LDPC
A new 7/8 code with parameters (n=672, k=588) with the block cyclic structure of the 802.11ad standard codes.
Code design based on the rate ¾ LDPC in 11ad
Parity-check matrix of the 7/8 code obtained by adding 1st with 3rd row and 2nd with 4th row of the parity-check matrix of the LDPC in 802.11ad
Example of cyclic-permutation matrices (Z=4)

## Slide 10: Simulation Assumptions (I)
SC modulations: QPSK, 16QAM and 64QAM;
frame size 8192 bytes;
AWGN channel;
no hardware impairments taken into account;
rate 7/8 LDPC code; a layered LDPC decoder using 8 iterations.

## Slide 11: FER Performance (I-a)
R=7/8, QPSK, AWGN
For the case of QPSK under AWGN, the Huawei’s rate 7/8 LDPC code yields about 0.38dB gain w.r.t. punctured 13/16 LDPC code [2] at 1% FER.

## Slide 12: FER Performance (I-b)
    For the case of 16QAM, the Huawei’s 7/8 Rate LDPC yields about 0.45dB gain w.r.t. the punctured 13/16 LDPC code [2] at 1% FER.
R=7/8, 16QAM, AWGN

## Slide 13: FER Performance (I-c)
    For the case of 64QAM, the Huawei’s 7/8 Rate LDPC yields about 0.52dB gain w.r.t. the punctured 13/16 LDPC code [2] at 1% FER.
R=7/8, 64QAM, AWGN

## Slide 14: Simulation Assumptions (II)
SC modulations: QPSK, 16QAM and 64QAM;
frame size 8192 bytes;
AWGN channel;
hardware impairments: phase noise, frequency offset;
rate 7/8 LDPC code; a layered LDPC decoder using 8 iterations.

## Slide 15: FER Performance (II-a)
R=7/8, QPSK, AWGN + PN + Frequency offset
For the case of QPSK, the Huawei’s rate 7/8 LDPC code yields about 0.42dB gain w.r.t. punctured 13/16 LDPC code [2] at 1% FER.

## Slide 16: FER Performance (II-b)
    For the case of 16QAM, the Huawei’s 7/8 Rate LDPC yields about 0.48dB gain w.r.t. the punctured 13/16 LDPC code [2] at 1% FER.
R=7/8, 16QAM, AWGN + PN + Frequency offset

## Slide 17: FER Performance (II-c)
    For the case of 64QAM, the Huawei’s 7/8 Rate LDPC yields about 0.61dB gain w.r.t. the punctured 13/16 LDPC code [2] at 1% FER.
R=7/8, 64QAM, AWGN + PN + Frequency offset

## Slide 18: Simulation Assumptions (III)
SC modulations: QPSK, 16QAM and 64QAM;
frame size 8192 bytes;
11ad conference room channel model;
hardware impairments: phase noise, frequency offset
rate 7/8 LDPC code; a layered LDPC decoder using 8 iterations.

## Slide 19: FER Performance (III-a)
For the case of QPSK under the 11ad conference room scenario with impairments of phase noise and frequency offset, the Huawei’s rate 7/8 LDPC code yields about 0.2dB gain w.r.t. the punctured 13/16 LDPC code [2] at 1% FER.
R=7/8, QPSK, 11ad conference room

## Slide 20: FER Performance (III-b)
For the case of 16QAM under the 11ad conference room scenario with impairments of phase noise and frequency offset, the Huawei’s rate 7/8 LDPC code yields about 0.3dB gain w.r.t. the punctured 13/16 LDPC code [2] at 1% FER.
R=7/8, 16QAM, 11ad conference room

## Slide 21: FER Performance (III-c)
R=7/8, 64QAM, 11ad conference room
For the case of 64QAM under the 11ad conference room scenario with impairments of phase noise and frequency offset, the Huawei’s rate 7/8 LDPC code yields about 0.3dB gain w.r.t. the punctured 13/16 LDPC code [2] at 1% FER.

## Slide 22: Summary of Performance Gains
The performance gains (in dB) of the 7/8 LDPC code proposed in this contribution against the punctured 13/16 LDPC code [2] at 1% FER are summarized below.
 | Assumption I | Assumption II | Assumption III
QPSK | 0.38 | 0.42 | 0.2
16QAM | 0.45 | 0.48 | 0.3
64QAM | 0.52 | 0.61 | 0.3

## Slide 23: LDPC Decoder Complexity
The presence of superimposed layers in the parity-check matrix of the proposed new codes has a minor impact in the implementation of the LDPC decoder, which is assumed to have a layered architecture.
In a layered architecture of the LDPC decoder, Z (=42 in this case) parallel check node processors process sequentially the messages of the edges (16 in this case) relative to a block of Z rows of the parity-check matrix. The cyclic shift structure simplifies the decoder architecture allowing to feed the parallel processors with a simple barrel shifter. When the processing of a layer is terminated, the parity-check processors are re-initialized and the next layer is processed.
When two rows are superimposed the parity-check node processors are not initialized after the end of the first layer but rather they continue processing the next 16 edges of the superimposed block-row. The decoding complexity thus remains the same as the one of the original code and also the original hardware architecture can be reused.

## Slide 24: Summary
New 7/8 LDPC codes (N=672, k=588) have been obtained based the LDPC codes in 802.11ad .
The new codes can outperform previously proposed 7/8 LDPC code generated by puncturing the 13/16 LDPC codewords in 802.11ad in both AWGN and 11ad conference room channels.
The new codes remain the codeword length unchanged as other LDPC codes in 802.11ad, which simplify the implementation.

## Slide 25: References
[1] IEEE 802.11-16/0233, Additional SC MCSs in clause 20 (DMG PHY).
[2] 2016-TECH-Broadcom-0001-00-On SNR Granularity.
[3] 2015-TECH-Intel-0039-00-SC 64 QAM NG60
[4] IEEE Std 802.11ad™-2012.
[5] L. Dinoi, F. Sottile and S. Benedetto, ”Design of versatile eIRA codes for parallel decoders”, IEEE Transactions on Communications, vol. 56, December 2008, pp. 2060-2069.

## Slide 26: Straw Poll/Motion
Do you agree to include the parity check matrix shown in Slide 9 for the rate 7/8 LDPC code of length 672 in the IEEE 802.11ay SFD?
Yes:
No:
Abstain: