## Slide 1: Channel issue in WUR
Date: 2017-01-16
Authors:
Name | Affiliation | Address | Phone | Email
Suhwook Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | suhwook.kim@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Jayh Park |  |  |  | hyunh.park@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com

## Slide 2: Introduction
SG WUR have discussed various topics in PHY and MAC
  However, channel related issue hasn’t been discussed a lot
  In submission [1], it proposed using narrow band in 2.4 GHz band for WU frame design
This presentation will address channel issues in TGba and study all possible cases

## Slide 3: Channel in WUR and WLAN
WLAN channel
  Used for WLAN communication (Association, Data exchange, Beaconing, etc...)
  A device will operate at WLAN channel in WUR off state
  It may be 20, 40, 80, or 160 MHz bandwidth
WUR channel
  Used for WUR communication (Wake-Up(WU) signal)
  A device will operate at WUR channel in WUR on state
  It will be 20 MHz or smaller than 20 MHz

## Slide 4: Channel issues
Issue 1: Does WUR channel need to be equal to WLAN channel?
  Issue 1a: If WUR channel is not equal to WLAN channel, what channel is adequate for WUR operation?
  Issue 1b: Does WUR channel need to be changed whenever WLAN channel is changed?
Issue 2: How can we design an efficient procedure about WUR channel information
Issue 3: Can WUR channel bandwidth be smaller than 20 MHz?

## Slide 5: Possible cases for Issue 1 and 2
WUR channel is dependent on WLAN channel
  Case 1: WUR channel is identical with primary channel of WLAN
  Case 2: WUR channel is one of secondary channel of WLAN
  Case 3: WUR channel is different with WLAN channel
WUR channel is independent
  Case 4: WUR channel is systematic fixed to specific channel (for example, channel 6 in 2.4 GHz band)
*Assume that WUR channel is 20 MHz bandwidth

## Slide 6: Case 1 – Issue 1&2
WUR channel is identical with primary channel of WLAN
  PROS
    AP/STA do not have to change operating channel
    Signaling about WUR channel information can be simple
    AP doesn’t have to manage WUR channel independently
  CONS
    Latency of WU signal can be increased in high density network

## Slide 7: Case 2 – Issue 1&2
WUR channel is one of secondary channel of WLAN
  PROS
    AP/STA do not have to change operating channel
    Signaling about WUR channel information can be simple
    AP doesn’t have to manage WUR channel independently
    Long latency problem can be mitigated a bit because secondary channel would be relatively under utilized than primary channel
  CONS
    It can be complex to design WU signaling procedure
      Transmission on secondary channel only

## Slide 8: Case 3 – Issue 1&2
WUR channel is different with WLAN channel
  PROS
    AP can select the best channel for WUR regardless of WLAN channel
  CONS
    AP/STA have to change operating channel
    WUR channel should be managed independently
    Transmission range should be matched if WUR channel is selected in different frequency band

## Slide 9: Case 4 – Issue 1&2
WUR channel is systematic fixed to specific channel
  PROS
    AP doesn’t have to indicate WUR channel
  CONS
    AP/STA have to change operating channel
    False alarm problem can arise if we use short address in WU signaling
    Pre-fixed WUR channel can be crowded by OBSS WUR transmission
    Transmission range should be matched if WLAN operates in different frequency band

## Slide 10: Discussion on Issue 1 and 2
Case 1 may be the most preferred option in term of implementation
  AP/STA don’t have to change its operating channel
  We can minimize signaling overhead about WUR channel information
  Some solutions may be needed to address long latency problem
Case 2 is similar with case 1 but WU signaling will be complicate so it isn’t preferable
Case 3&4 cause channel hopping and channel management overhead

## Slide 11: Issue 3 (Bandwidth)
Some submissions([2][3]) addressed smaller than 20 MHz bandwidth channel for WUR (4, 5, 8, 10 MHz)
  If we use smaller than 20 MHz bandwidth channel for WUR, receiver power consumption and PER performance can be enhanced
There are three cases when we use smaller than 20 MHz bandwidth channel for WUR
  Case 1: Define 1 WUR channel in 20 MHz, use WUR channel
  Case 2: Define 2 ~ 4 WUR channels in 20 MHz, use 1 WUR channel
  Case 3: Define 2 ~ 4 WUR channels in 20 MHz, use all channels

## Slide 12: Case 1 – Issue 3
Define 1 WUR channel in 20 MHz, use 1 WUR channel
  PER enhancement (TX power gain)
  No additional WUR channel indication
  OBSS inference by WUR should be considered

## Slide 13: Case 2 – Issue 3
Define 2 ~ 4 WUR channels in 20 MHz, use 1 WUR channel
  PER enhancement
  OBSS inference by WUR can be mitigated
  WUR channel indication can be used
  for station grouping [4]
  WUR channel of each STA
  should be indicated in advance

## Slide 14: Case 3 – Issue 3
Define 2 ~ 4 WUR channels in 20 MHz, use all channels
  It can support multi-user wake up signaling easily
  Cost increases at receiver side due to sharp filter
  No PER enhancement (No TX power gain)
  WUR channel indication can be used
  for station grouping

## Slide 15: Discussion on Issue 3
Case 1 may be the most preferred option in term of implementation
  Case 1 is simple and no additional channel indication
  However, if 802.11ba supports group wake-up procedure, case 2 and 3 will be considerable [4]

## Slide 16: Summary
In this submission, we address some issues about WUR channel
  To easy implementation, following options can be preferred
    WUR channel is identical with primary channel of WLAN channel
    Define one WUR channel in 20 MHz even though bandwidth of WUR channel is lower than 20 MHz
  However, other options might be considerable when we enhance MAC protocol

## Slide 17: References
[1] 11-16-1147-01-0wur-wur-and-efficiency-tradeoff
[2] 11-17-0030-00-00ba-on-the-performance-of-timing-synchronization-and-ook-pulse-bandwidth
[3] 11-17-0036-00-00ba-WUR-PHY-Structure-for-WUR-signal
[4] 11-17-0054-00-00ba-WUR-MAC-issues