## Slide 1: Power Efficient WUR AP Discovery - A Follow Up
Date: 2017-01-16
Authors:

## Slide 2
Abstract
In this contribution, we continue the discussion related to power efficient WUR AP discovery.

## Slide 3: Introduction
In [1], we discussed that a WUR AP discovery procedure similar to active scanning may be desirable for fast WUR AP discovery when the AP is asleep
  Broadcast Wake Up frame used for AP discovery may be very energy inefficient
  Including one or more BSSID/SSI in broadcast Wake up frames used for AP discovery may provide energy efficiency for WUR AP discovery
In this presentation, we discuss scenarios in which such an active WUR AP discovery procedure is beneficial
We also discuss the trade off between active and passive discovery of WUR AP for optimal power usage
  Active and passive WUR AP discovery mechanisms are complimentary to each other

## Slide 4: Why would an AP sleep? (1)
An AP may sleep to conserve energy due to one or more of the following reasons:
Power source: An AP may not be plugged in:
  Mobile
  Ease of deployment
  Environmental requirements
  Regulation requirements
Traffic Requirement: AP’s Primary Connectivity Radio may not be (fully) turned on all the time
  Associated STAs transmit once in a long time: e.g., sensors/meters
  Status query only once in a long time: e.g., sensors/meters
  Associated STAs may only need to transmit in emergencies: e.g., fire/intrusion

## Slide 5: Why would an AP sleep? (2)
A number of usage scenarios in which AP may want to sleep and turn on its WUR:
Quick Emergency Report Scenario [3]
  Mobile gateways sleep for a long period of time until it receives a wakeup packet
Outdoor Cattle Farms [2]:
  Mobile APs may go to the sleep state and turn on their WUR if only very sparse transmissions are expected between APs and STAs, e.g.:
    4 times a day status query
    1 time a week emergency report
Warehouse [2]:
  Warehouse APs may go to the sleep state and turn on their WUR if only sparse transmissions are expected between APs and STAs, e.g.:
    When there is not much change in inventory or other transmissions

## Slide 6: WUR AP Discovery (1)
An active WUR AP Discovery mechanism may be needed:
  APs may be in the sleep state with its WUR turned on
  A STA may need to discover and associate with a new AP that is in the sleep state with its WUR turned on, e.g.:
    Cattle may have walked to the coverage area of another AP
    Goods may have moved to a different part of the warehouse
Is a passive WUR AP Discovery mechanism sufficient?
  Regular/WUR passive AP discovery is done by STAs, by detecting regular/WUR beacons, FILS Discovery frame, etc., that are transmitted by the AP
  Passive AP Discovery mechanism is sufficient and power efficient, in the right circumstances
    AP transmits one frame to provide sufficient information for a number of STAs
    When transmitting regular/WUR beacons etc. doesn’t cost too much energy

## Slide 7: WUR AP Discovery (2)
When is passive AP discovery power efficient?
  When latency requirement is not very stringent so that regular/WUR beacon(s), etc., doesn’t need to be transmitted too frequently
  When AP is in the awake state most of the time in order to support existing traffic to transmit
When is passive AP discovery not optimal?
  When traffic is very sparse and the AP doesn’t need to be awake most of the time
    Outdoor cattle farm, warehouse, quick emergency report, etc.
  When latency requirement is high
    Emergency report/handling
Trade off of power consumption and support for low latency for passive AP discovery

## Slide 8: WUR AP Discovery (3)
An active WUR AP discovery mechanism may fill in the gap for passive AP discovery
  Enabling WUR AP to transmit as less frequent as possible and therefore reduce power usage
    When associated STAs transmit/receive very little data and don’t (always) listen to beacons [5]
  Allowing STAs that have low latency data to discover and associate with APs as soon as possible
Passive and active WUR AP discovery are complementary
  Particularly in a number of IoT usage scenarios
An active WUR AP discovery mechanism is desirable depending on the usage scenarios and traffic requirements

## Slide 9: Conclusion
A WUR AP discovery mechanism similar to active scanning for regular 802.11 STAs may be desirable for fast AP discovery and association in a number of WUR usage scenarios
Allowing for both active and passive WUR discovery mechanisms will enable the ability to optimize latency and power consumption performance in many WUR usage scenarios

## Slide 10
References
[1] 11-16/1400r0, Power Efficient Discovery WUR AP Discovery, Nov. 2016
[2] 11-16/1465r0, WUR Usage Model, Nov. 2016
[3] 11-16/0974r0, Wake-up Receiver Usage Scenarios and Applications, Jul. 2016
[4] 11-16/1045r6, A Proposed PAR for Wake Up Radio, Sept. 2016
[5] 11-16/1460r1, WUR MAC Consideration, Nov. 2016