## Slide 1: WUR Signaling Field
Date: 2017-01-16
Authors:

## Slide 2: Introduction
WUR considers IoT scenarios where a large number of STAs are operating in a WUR BSS
At a certain time, even though most WUR STAs would be in sleep mode, there still can be many WUR STAs in awake mode
WUR PPDU design should minimize energy consumption of WUR STAs in both sleep and awake modes
WUR STA
(sleep)
WUR STA
(awake)
WUR PPDU
Backoff
802.11
WUR
802.11
WUR part
sleep
wake-up
WUR
802.11
OFDM decoding
Legacy
Part
Legacy
Part
WUR part
energy consumption
sleep

## Slide 3: WUR PPDU format
Currently discussed WUR PPDU format
  Legacy Part for coexistence with legacy STAs, at least L-Preamble (L-STF/L-LTF/L-SIG) is included [1]
  WUR Part for signaling to WUR STAs in sleep mode
Problem: Network-wide energy consumption of WUR PPDU decoding
  If a WUR STA is awake, it will enable its Primary Radio only (suspending Wake-up Radio)
  WUR STAs in awake mode cannot detect WUR PPDU, thus wasting energy for decoding WUR PPDU’s WUR Part (regarding it as non-HT PPDU)
Problem: Forward compatibility of WUR PPDU
  For STAs based on the future 802.11 amendments, but do not have Wake-up Radio
  Those STAs would always try to decode WUR PPDU (regarding it as non-HT PPDU)
By including WUR information in Legacy Part, we can enable STAs in awake mode to reduce energy consumption
Legacy Part
WUR Part
OFDM Symbols
OOK Symbols
WUR PPDU

## Slide 4: 1. WUR PPDU indication in Legacy Part
Option 1
  Include a simple indication that it is WUR PPDU in Legacy Part
For WUR STAs in awake mode,
  if WUR PPDU is detected, they may stop decoding the remaining WUR Part since they are already in awake mode,
  but still protecting the WUR PPDU until the PPDU Length
For the future 802.11 STAs without Wake-up radio,
  if WUR PPDU is detected, they may stop decoding the PPDU,
  but still protecting the WUR PPDU until the PPDU Length
For legacy STAs,
  the added WUR PPDU indication information should not affect legacy STAs from detecting it as non-HT PPDU
Legacy Part
+ WUR PPDU indication
WUR Part
OFDM Symbols
OOK Symbols

## Slide 5: 2. BSS info in Legacy Part
Option 2
  Include a BSS color or other BSS identification information in Legacy Part
For WUR STAs in awake mode,
  if the received PPDU is from MYBSS, they may enter Intra-PPDU power save mode
    Intra-PPDU PS on WUR PPDU can be beneficial since the WUR Part can be relatively long considering the OOK overhead [2]
  if the received PPDU is from OBSS, they may stop decoding the PPDU
For legacy STAs,
  the added BSS information should not affect legacy STAs from detecting it as non-HT PPDU
Legacy Part
+ BSS Info
WUR Part
OFDM Symbols
OOK Symbols

## Slide 6: 3. Receiver info in Legacy Part
Problem
  An WUR AP may not know the current power state of the target WUR STA [3][4]
  If a WUR PPDU is sent to a WUR STA in awake mode, the STA does not even recognize whether it has received a WUR PPDU
  Therefore, the WUR AP/STA would wait until the AP initiates data exchange in Primary Radio after wake-up delay of the STA
Option 3
  Include a receiver identification information in Legacy Part
For WUR STAs in awake mode,
  if the received WUR PPDU is destined to it (by decoding the receiver info in Legacy part), the STA transmits immediate acknowledgement to WUR AP
  thus reducing data exchange delay, and removing requirements on WUR AP for keeping track of power states of WUR STAs
  Non-receiver STAs may stop decoding the PPDU
Legacy Part
+ Receiver Info
WUR Part
OFDM Symbols
OOK Symbols

## Slide 7: Summary
TGba needs to define WUR PPDU format
The previously discussed format has Legacy Part and WUR Part where the first part includes L-Preamble (L-STF/L-LTF/L-SIG) for coexistence with legacy STAs
However, WUR STAs in awake mode may not identify WUR PPDU format thus wasting energy to decode it like non-HT PPDU
We propose to include WUR related information in Legacy Part of WUR PPDU for network-wide energy efficiency of WUR BSS
The type of information to include and how to include it in Legacy Part is open for discussions

## Slide 8: Straw poll
Do you agree that IEEE 802.11ba provide mechanisms to include WUR related information in Legacy part (OFDM-modulated) of WUR PPDU?
  Y/N/A

## Slide 9: References
  [1] 11-16/0341r0, LP-WUR (Low-Power Wake-Up Receiver) Follow-Up
  [2] 11-16/0865r1, Performance Investigation on Wake-Up Receiver
  [3] 11-16/1470r0, Wake-up and Data exchange Sequences
  [4] 11-17/0055r0, Considerations on post wake-up sequences