## Slide 1: UL Training Protocol for DL MU-MIMO in 802.11ay
Date:
Authors:

## Slide 2: Introduction
DL MU-MIMO is included in 11ay
An essential part of DL MU-MIMO operation is the obtaining of channel information (at the AP) for proper user pairing and precoding
Depending on the scenario, UL training may be more efficient (lower overhead etc.) than explicit (DL) training
  And vice versa
  Other 5G communities are adopting UL training for mmWave

## Slide 3: Hardware Model
AP
…
antennas
…
RF chains
STA
…
antennas
…
RF chains
We consider a hybrid scenario (not fully digital)
Due to this, we need to find good analog beams (SLS, BRP, etc.) before doing any digital precoding
The proposed UL training mechanism is useful for both

## Slide 4: Generating Transmit Beams in Hybrid Mode
Transmitting a beam (a.k.a. sector):
RF
RF
+
+
+
+
Typically

## Slide 5: Example: Classic Hybrid Structure Transmission
…
RF
…
RF
Transmit beams/sectors corresponding to classic hybrid structure
…
RF
…
RF

## Slide 6: Example: Classic Hybrid Structure Transmission Implementation
A way to implement the classic hybrid transmission
RF
RF
+
+
+
+
RF
RF
+
+
+
+

## Slide 7: Generating Receive Beams in Hybrid Mode
Receiving simultaneously with beams/sectors
RF
RF
+
+

## Slide 8: Example: Hybrid Structure Reception
RF
RF
+
+

## Slide 9: Main Observations: Enhanced SLS Example
Consider an AP (2 RF chains) that transmits 4 sectors to a single STA (1 RF chain) with 2 receive sectors during enhanced SLS [1]
AP
STA
TRN-R
TRN-R
TRN-R
TRN-R
It takes in total 4×2 = 8 TRN-R subfield slots
RF
RF
RF

## Slide 10: Main Observations: Enhanced SLS Example in UL
By reversing the previous procedure, the AP can listen to 2 sectors simultaneously (since it has 2 RF chains)
AP
STA
TRN-R
TRN-R
It takes in total 2×4/2 = 4 TNR-R subfield slots (half the overhead compared to DL)
RF
RF
RF

## Slide 11: BRP DL
The previous reversal to UL training can as well be applied to the BRP procedure
STA
RF
BRP
BRP
BRP
It takes in total 4×4 = 16 BRP subfield slots
BRP
AP
RF
RF

## Slide 12: BRP UL
We now reverse the DL BRP, so that it becomes UL BRP
STA
AP
RF
RF
RF
It takes in total 4×4/2 = 8 BRP subfield slots (half the overhead compared to BRP DL)
BRP
BRP
BRP
BRP

## Slide 13: DL/UL Overhead Comparison

## Slide 14: DL/UL Overhead Comparison (Detailed)
Previous presentation showed:
Hardware & scenario
dependent (shaded boxes)
Implementation
dependent
Clearly, if , DL training overhead is larger
  Independent of the feedback packet duration
  In general, the larger the , the larger the DL training overhead

## Slide 15: DL/UL Training Duality
Both training methods can provide the same information about
  The DL training provides estimates of - can be fed back to AP in full form or just by indicating best beams
  The UL training provides estimates of - directly available at AP, no feedback needed
  If and (this is where calibration comes in), DL and UL training produce equivalent channel information
  Calibration at AP is enough to remove inter-user interference

## Slide 16: Impact of Channel Characteristics
If complete (or almost complete) channel estimate is required, the overhead can be reduced significantly with UL training
There are indoor mmWave (58.7 GHz) channels that contain significant multipaths [2] – might require more than LOS estimate

## Slide 17: UL Training Protocol
AP sends out a trigger frame for UL training
AP
Trigger frame
STA 1
STA 2
AP
STA 1
STA 2
Pilot packet
Pilot packet
STAs transmit (directional or omni) in UL (simultaneous or sequential) and AP listens to different sectors
is orthogonal to

## Slide 18: Benefits of UL Training
Significantly less training overhead (for same channel information) in many scenarios
Requires no feedback
  The AP can estimate the best analog Tx-Rx beam configuration itself
  The AP also obtains digital CEF for the best analog Tx-Rx beam configuration (no STA feedback needed)
  The AP only informs STAs (during DL packet) which analog beams that they transmitted were best (so these are used as receiving beams at STAs)

## Slide 19: References
[1] IEEE 802.11-17/0067r1
[2] J. Medbo, N. Seifi, H. Asplund, ”Frequency Dependency of Measured Highly Resolved Directional Propagation Channel Characteristics”, European Wireless 2016 (invited paper)

## Slide 20: Straw Poll
Do you support including the principles of Uplink training (as outlined on page 17 of this presentation) into the 802.11ay draft?
Note: Inclusion into the draft is subject to the availability of normative text
Yes
No
Further studies wanted