## Slide 1: Discussion for CR on 10.22.2.8 TXOP limits
Date: 2017-01-18
Authors:

## Slide 2: Abstract
This contribution contains the discussion regarding comment resolution of CID 6189, 7040, 9412
Proposing to change the TXOP limit exception rules so as to be applied to HE fragmentation appropriately

## Slide 3: Baseline (static) fragmentation and TXOP limit background
With non-zero TXOP limit value, a TXOP holder shall not transmit data that causes the TXOP limit to be exceeded
  Not allowed to aggregate MPDUs beyond the limit
If an AP sets a very low TXOP limit value or the size of a single MSDU is large, then the transmission of the MSDU might be longer than the limit value
  If the MSDU is under an HT-immediate BlockAck agreement, it cannot be fragmented
  When it is transmitted in a VHT single MPDU (S-MPDU context), it shall be fragmented, and be subject to the TXOP limit

## Slide 4: TXOP limit exceptions regarding static fragmentation
The baseline allows a transmission exceeding the TXOP limit if the TXOP holder transmits a single MPDU and has no control over the size of the transmitting data
The baseline spec also defines a few exceptions allowing a transmission of a fragment to exceed the TXOP limit
  Derived from the nature of static fragmentation
    Once the size of the first fragment is defined, the sizes of all other fragments in the same MSDU are also defined
    The maximum number of fragments is 16

## Slide 5: 10.22.2.8 TXOP limits

## Slide 6: Rationale for the exception rules
1) Initial transmission of a fragment of an MSDU or MMPDU, if a previous fragment of that MSDU or MMPDU was retransmitted
  The baseline allows a retransmission of a single MPDU to exceed the TXOP limit
    Initial transmission must be fit into the TXOP limit
    But, the transmitter may set a lower MCS for the retransmission in terms of reliability, in which case TXOP might be exceeded
  Once any fragment experienced retransmission, the subsequent fragment with the same size might necessarily be transmitted with lower MCS
    The originator has no control to change the subsequent fragment size
2) Transmission of a fragment of an MSDU or MMPDU fragmented into 16 fragments
  The originator has no control over the size of the fragment that is already maximally fragmented

## Slide 7: Changes in dynamic fragmentation
Dynamic fragmentation has different rules on generating fragments
  No constraint on size except for the first fragment
    greater than or equal to the minimum fragment size specified by the receiver STA in the Minimum Fragment Size subfield of the HE Capabilities element
An HE STA might transmit a dynamic fragment with S-MPDU context as well
  The STA obtains a TXOP as a TXOP holder
  Subject to the TXOP limit rule
The current TXOP limit exception rules are not applied to dynamic fragments very well

## Slide 8: Proposed change (1)
1) Initial transmission of a fragment of an MSDU or MMPDU, if a previous fragment of that MSDU or MMPDU was retransmitted
  Initial transmission of a dynamic fragment doesn’t have to exceed the TXOP limit regardless of transmission result of the previous fragment
  The originator may change the size of the fragment so as to fit into the TXOP limit even with a lower MCS
  This rule is irrelevant to dynamic fragments
2) Transmission of a fragment of an MSDU or MMPDU fragmented into 16 fragments
  An originator of dynamic fragments has no control over the size of fragment that is already fragmented maximally
  This rule is still valid for dynamic fragments

## Slide 9: Proposed change (2)
Transmission of the first dynamic fragment may exceed the TXOP limit
  Only when the minimum fragment size specified by the receiver requires the transmission of the first dynamic fragment that exceeds the TXOP limit
    TXOP limit value in EDCA parameter set element is in 32us unit
    The minimum fragment size can be up to 512 octets
  In which case, the size of the first fragment shall be set to the minimum fragment size
Any fragments of an A-MSDU shall not cause the TXOP limit to be exceeded
  Fragment of A-MSDU must be exempted from the exception rules

## Slide 10: Proposed text
Add the following paragraph in D1.0, 10.22.2.8
  with underlined insertions
The TXOP holder may exceed the TXOP limit only if it does not transmit more than one Data or Management frame in the TXOP, and only for:
  Retransmission of an MPDU, not in an A-MPDU consisting of more than one MPDU
  Initial transmission of an MSDU under a block ack agreement, where the MSDU is not in an A-MPDU consisting of more than one MPDU and the MSDU is not in an A-MSDU
  Transmission of a Control MPDU or a QoS Null MPDU, not in an A-MPDU consisting of more than one MPDU
  Initial transmission of a static fragment of an MSDU or MMPDU, if a previous fragment of that MSDU or MMPDU was retransmitted
  Transmission of a fragment of an MSDU or MMPDU fragmented into 16 fragments
  Transmission of an A-MPDU consisting of the initial transmission of a single MPDU not containing an MSDU and that is not an individually addressed Management frame
  Transmission of a group addressed MPDU, not in an A-MPDU consisting of more than one MPDU
  Transmission of a null data packet (NDP)
  Transmission of a VHT NDP Announcement frame and NDP or transmission of a Beamforming
  Report Poll frame, where these fit within the TXOP limit and it is only the response and the immediately preceding SIFS that cause the TXOP limit to be exceeded.
  Transmission of the first dynamic fragment of an MSDU or MMPDU, if the minimum fragment size specified by the receiver STA causes TXOP limit to be exceeded. The size of the fragment shall be set to the minimum fragment size.