## Slide 1: TX Sector Sweeps
Date: 2017-01-16
Authors:

## Slide 2: Abstract
Extending the TX Sector Sweep protocol for EDMG devices to support both SISO and MIMO

## Slide 3: Background
802.11ay will provide support for SISO, SU-MIMO and downlink MU-MIMO
  Up to 8 spatial streams
SFD and Draft 0.1 have defined many MIMO features
  PPDU structure
  CE sequences
  TRN sequences
SFD mandates simultaneous BF training of transmit DMG antennas
Sector sweep can be improved to support all implementations

## Slide 4: Separate / Simultaneous TX Sector Sweep (1)
STAs with MIMO capability need two options for TX sector sweep
  Separate – slower, but more allows the receiving STA to determine optimum sector of each antenna
  Simultaneous – significantly faster
STA
TX0 Sector i
TX1 Sector j
STA

## Slide 5: Separate / Simultaneous TX Sector Sweep (2)
Sector sweeps are necessary, but sweeping over many sectors is slow
  Minimum length SSW frame is 26 bytes (Beacon is longer)
  DMG Control preamble is 7552 Tc = 4.29 us
  Header + Data = 248 bits; 2 LDPC Codewords
  336 + 160 + 168 = 664 coded bits x 32 Tc = 12.07 us
  SBIFS = 1 us
  Total = 17.36 us per sector minimum
For NxN MIMO, the sector sweep time increases linearly with N

## Slide 6: Separate / Simultaneous TX Sector Sweep (3)
802.11ay should allow both separate (1 antenna array at a time) and simultaneous TX sector sweeps
Choice of employing separate, simultaneous, or both techniques should be left to equipment vendors
802.11ay will provide mechanisms to enable interoperability

## Slide 7: Separate / Simultaneous TX Sector Sweep (4)
In some cases, it may be beneficial to run more than one sector sweep
  An initial sector sweep to determine possible starting points for a combination of antennas
  After feedback from the receiver, a second sector sweep to determine a unique starting point

## Slide 8: Simultaneous Sector Sweep
Simultaneous Sector Sweep transmission from multiple antennas can employ time shifts as defined in Draft 0.1 29.3.4.26.5:
  Agreed upon method for transmitting non-EDMG portions of MIMO packets
  0, 4Tc, 8Tc, … 4(N-1)Tc for N antennas
  Provides sufficient diversity that receiver can accurately determine total power even if the path from each TX antenna to the RX antenna is almost the same

## Slide 9: Legacy 802.11ad SSW Field
3 octets total
Single sector and DMG Antenna ID settings (1 octet)

## Slide 10: Proposed EDMG SSW element (1)
Suitable for SISO and MIMO
  Enable up to 8 antennas
  Enable up to 256 sectors / antenna
Possible to have 8 Sector IDs in the SSW Field, but that would be inefficient
  Most applications would only use 2 fields
Instead, STAs can employ a Beam ID
  Unique 16 bit description of antenna and sector settings
  Implementations choose their own mapping from antenna and sector to Beam ID

## Slide 11: EDMG SSW element (2)
The Beam ID field contains the descriptor for the combination of antennas and actual sectors used to transmit the packet
Final Sweep is set to one for packets sent on the last sweep
Direction
CDOWN
Beam ID
RXSS Length
Bits:
1
9
16
6
Reserved
7
Final Sweep
1

## Slide 12: EDMG SSW Feedback (1)
SSW Feedback provides a Best Beam ID with the corresponding SNR
It also provides a bit map of the CDOWN on all successfully received SSW packets
SNR Report
Poll Required
Reserved
Bits:
8
CDOWN MAP
Bits:
(TBD – Suggest 32)
1
7
Best Beam ID
16

## Slide 13: EDMG SSW Feedback (2)
Need to limit CDOWN map to a reasonable size
  Suggest 32 since that is probably the maximum length of a sector sweep
  We want flexibility but do not want unnecessarily long SSW packets

## Slide 14: Multiple Sector Sweep Example
Employ sector sweeps to quickly determine an initial MIMO Beam ID for each side
  FB and ACK
Initiator
Responder
SSW
SSW
…
SSW
SSW
SSW
SSW
SSW
SSW
FB
ACK
…
…
…

## Slide 15: Constraints on EDMG Sector Sweeps
EDMG SSW Feedback is provided on all sweeps except the first
Sweep starts with Best Beam ID received in EDMG SSW Feedback element, if available
  For 2nd sweep or later
Total number of iterations needs to be limited
  Suggest 3 in each direction, however a larger limit may be useful for many antenna arrays

## Slide 16: Summary
Proposed EDMG SSW and EDMG Feedback elements are defined that allows both separate and simultaneous antenna sector sweeps
Allowing multiple sector sweeps before beam refinement can yield to a better choice of antenna sector selection
Only small protocol changes are needed from 802.11ad