## Slide 1: False Radar Pulse Detection on WUR Signal
Date: 2017-03-01
Authors:

## Slide 2: Overview
WLAN system is not the primary user of the DFS channels
  WLAN systems are required by law to vacate the channel for 30 minutes upon detecting radar signals
While radar ‘detection’ performance is important to abide by the law, ‘false detection’ performance is also crucial for the WLAN industry
  Spectrum is a valuable resource
  WLAN industry need to be able to demonstrate to Regulators that the industry can make efficient use of the DFS channels so that more spectrum may be made available
    WLAN systems often vacating DFS channels due to false alarm will not motivate Regulatory bodies to assign more DFS channels to WLAN

## Slide 3: Challenges in Radar Detection
Radars have very wide range of ‘characteristics’, making their detection challenging
  Difficult to set the pattern matching criteria very tight in practice
  Some regulatory bodies are considering to increase the ‘range’ of radar patterns, making reliance on pattern matching alone to be even harder
    E.g., the Japan Meteorological Agency (JMA) was considering radar pulses with 500 usec duration, thus filtering pulses out based on pulse duration would become quite difficult
One key distinction between WLAN signals and radars has been the BW of the signal
  WLAN signals in 5 GHz (11a/n/ac) have been at least 20 MHz wide
  Radar signal is a ‘tone’
    Chirping radars have time varying tone frequency. But at a given time, chirping radars are also narrow band signals.
  This distinction can greatly reduce the probability of declaring a (potential) radar pulse for a WLAN signal

## Slide 4: WUR Signal
OOK is being considered as the modulation scheme for WUR
  OOK signal has many rising/falling edges similar to radar pulses
For power efficiency and adjacent channel rejection performance consideration, WUR signal BW is most likely narrower than 20 MHz
  E.g. a 4 MHz BW has been proposed
In this presentation we examine the DFS channel false radar pulse detection performance of some legacy devices with respect to an example WUR signal

## Slide 5: Simulation Setup
1x1
80 MHz channel bandwidth
Primary20 on second subchannel from the left
WUR signal from OBSS on third subchannel from left
  WUR signal:
    has a 20 MHz 11a preamble with L-SIG rate at 6 Mbps and a length spoofing equivalent to 1 ms
    has a 1 ms On-Off Keying (OOK) payload with a bandwidth of 4 MHz, and 8 us symbols with a 4 us On and 4 us Off period or vice versa
WUR signal is received at -60 dBm
Radar detection enabled

## Slide 6: WUR Signal
Zoomed in at first 125 µs

## Slide 7: Simulation Results
In AWGN we see 94% false radar pulse detects
In D-NLOS we see 100% false radar pulse detects
From experience we can say that such high false pulse detect rates sooner or later result in false pattern recognitions, leading to false radar detects
  Any false radar detect will force the WLAN network to vacate the DFS channel for 30 minutes

## Slide 8: Problem + Potential Solution
Since the WUR signal is received on a secondary20 subchannel, the issue is that the L-SIG is not demodulated, an thus its length field is not honored, while the WUR OOK is rather narrowband and has many rising edges, which easily triggers the radar detector
Potential solution
  Limit the operation of WUR to non-DFS channel
    2.4 GHz band has better range
    Client with WUR receiver is also relieved from the burden of potential frequent channel switching due to DFS master’s radar detection outcome