## Slide 1: SFD MAC proposal
Date: 2017-03-13
Authors:
Name | Affiliation | Address | Phone | Email
Suhwook Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | suhwook.kim@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
TGba decided to build Specification Framework Document (SFD) in January meeting
We have submitted WUR MAC procedure presentations
  They were about WUR mode signaling, WUR general operation, WUR retransmission, and channel issue
So now we propose SFD text based on previous WUR MAC submissions

## Slide 3: WUR Mode Signaling [1]
After the association procedure or receiving DL data completely, a STA may request to enter WUR mode for low power operation
For this procedure, an explicit WUR mode initiation procedure is needed
  If the STA does not inform its 802.11 main radio turning off, then WUR AP can send 802.11 frames to the STA without sending WUR packet and it can be lost

## Slide 4: WUR Mode Signaling [1]
After receiving the confirmation (i.e., ACK, WUR mode response) from the AP, a STA enters the WUR mode

## Slide 5: WUR Mode Signaling [1]
To reduce MAC signaling overhead, WUR negotiation and Mode initiation procedure can be integrated

## Slide 6: WUR Mode Signaling [1]
Following WUR operating parameter can be negotiated during WUR negotiation procedure and/or WUR mode initiation procedure
  WUR Beacon information (timestamp, WUR-TBTT, period)
  WUR channel information (if 11ba supports multi-channel)
  Duty cycle operation information
  Wake-up packet information (data rate, BW, etc)
  Identification (individual or group)
  Mode transition delay (WUR -> WLAN)

## Slide 7: WLAN packet transmission to WUR STA [1]
Whenever an AP wants to send a WLAN packet to a STA in WUR mode, WUR packet should be transmitted to wake up the station
  After transmitting a WUR packet, AP should wait for a specific time before sending a WLAN data frame. WLAN main radio turn-on time can take about a few millisecond.

## Slide 8: WLAN packet transmission to WUR STA [1]
Before WLAN packet transmission, STA’s wake-up can be confirmed through the existing WLAN control signaling (e.g., PS-Poll)

## Slide 9: WUR Error Recovery [1]
To handle the case that wakeup signaling fails, an error recovery mechanism shall be provided.
  When an AP sends data frame after WUR packet and does not receive ACK/BA, AP has to retransmit WUR packet or data frame.
  Retransmission policy at AP should be defined to reduce power consumption and overhead

## Slide 10: WUR Error Recovery [1]
For the case of PS-Poll transmission in response to WUR packet, AP can retransmit WLAN data frame

## Slide 11: WUR channelization [2]
The channel where wake-up signal is sent is located within the primary 20MHz channel of primary connectivity radio
  PROS
    AP/STA do not have to change operating channel
    Signaling about WUR channel information can be simple
    AP doesn’t have to manage WUR channel independently
  CONS
    Latency of Wake-Up signal can be increased in high density network because primary channel is relatively high utilized

## Slide 12: Summary
In this submission, we proposed MAC description texts for Specification Framework Document
  The texts are based on previous technical submissions which are addressed overall MAC procedure and channel issue in WUR

## Slide 13: Straw poll 1 (WUR Mode signaling)
Do you support following sentences?
  Explicit Wake-Up mode initiation signaling shall be defined for the WUR STA to enter WUR mode
  Wake-Up operating parameter may be negotiated during Wake-Up mode initiation signaling
    Detail parameters are TBD
  Y/N/A: 12 / 2 / 11

## Slide 14: Straw poll 2 (WUR channelization)
Do you support following sentence?
  The channel where wake-up signal is sent is located within the primary 20MHz channel of primary connectivity radio
  Y / N / A : 8 / 4 / 13

## Slide 15: References
[1] 11-16-1445-01-0wur-overall-mac-procedure-for-wur
[2] 11-17-0031-00-00ba-channel-issue-in-wur