## Slide 1: WUR channel switch
Date: 2017-03-16
Authors:
Name | Affiliation | Address | Phone | Email
Suhwook Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | suhwook.kim@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
In last meeting, we addressed channel issue in WUR [1]
  To easy implementation, we preferred that WUR channel is identical with primary channel of WLAN channel
However, WLAN AP can change its primary channel
  AP has to indicate channel switching information to WUR STAs which are operating in power save mode

## Slide 3: Problem statement
Common AP has a capability of automatic channel switching
  Some AP changes its primary channel periodic for better performance
  There may be a Wi-Fi controller which can control all APs in Enterprise, and the Wi-Fi controller can change operating channel of some APs to handle OBSS interference
If an AP want to change its primary channel, channel switch information should be distributed to all associated STAs including power saving STAs

## Slide 4: Possible solutions
Channel Switch Announcement(CSA) element is defined in IEEE 802.11-2016
There are two ways to reuse CSA element
  Transmission on WLAN interface
  Transmission on WUR interface

## Slide 5: CSA information on WLAN interface
CSA information is delivered on WLAN interface
  AP transmits Wake-Up frame for WUR STA to wake up
  When WUR STA wakes up, AP transmits CSA information on WLAN interface
  When WUR STA received CSA information, it will change WUR channel as indicated

## Slide 6: CSA information on WLAN interface
Advantage
  Reliability is guaranteed by ACK frame
  No additional information in Wake-Up frame
Disadvantage
  WUR STA has to waste its power

## Slide 7: CSA information on WUR interface
CSA information is delivered on WUR interface
  AP transmits Wake-Up frame including CSA information
  When WUR STA received WUR frame including CSA information, it will change WUR channel as indicated in CSA information

## Slide 8: CSA information on WUR interface
Advantage
  Power consumption can be minimized
Disadvantage
  Reliability is not guaranteed
  Addition overhead in Wake-Up frame

## Slide 9: CSA information on WUR interface
Reliability of CSA information in WUR frame can increase by consecutive WUR transmission
CSA information can be compressed into two byte
  New channel number (1 octet) and Channel switch count (1 octet) are only meaningful sub-element

## Slide 10: Summary
In this submission, we addressed channel switch issue in WUR
  Common AP has a capability of automatic channel switching
  AP has to indicate channel switching information to WUR STAs which are operating in power saving mode
We proposed two solutions
  Transmission CSA element on WLAN interface
  Transmission CSA element on WUR interface

## Slide 11: Straw poll 1
Do you support following sentences?
  11ba spec shall define a mechanism to indicate channel switch information for WUR STA

## Slide 12: Straw poll 2
Do you support following sentences?
  11ba spec shall define a mechanism to indicate channel switch information for WUR STA and that channel switch information can be delivered on primary connectivity radio

## Slide 13: Straw poll 3
Do you support following sentences?
  11ba spec shall define a mechanism to indicate channel switch information for WUR STA and that channel switch information can be delivered in Wake-Up frame

## Slide 14: References
[1] 11-17-0031-00-00ba-channel-issue-in-wur