## Slide 1: WUR channel switch
Date: 2018-01-15
Authors:
Name | Affiliation | Address | Phone | Email
Suhwook Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | suhwook.kim@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
In previous meeting, we have addressed channel switch issue for WUR [1][2]
  However, we had so many unclarified issues on WUR channel before handling channel switch

## Slide 3: WUR channel
We have several passed motions on WUR channelization
  The operation in DFS channel is disallowed (R.3.3.A/B)
  When a single band is used for transmission of WUR PPDU, the OOK waveform of WUR PPDU is generated by using contiguous 13 subcarriers with the subcarrier spacing of 312.5 kHz (R.3.3.C)
  AP decides the WUR operating channel in the band(s) supported by the associated non-AP STA operating in WUR Mode (R.4.2.G)

## Slide 4: WUR channel
As defined in the current SFD document,
  WUR channel can be selected in one of PCR channels
    In this case, WUR and PCR simultaneously operate in same channel
    The selected PCR channel shall not be non-DFS channel
  Or WUR channel can be selected from non-DFS channels that are not in use for PCR
    PCR channels can be DFS channel

## Slide 5: Channel Switch Scenarios
Scenario 1: PCR channel has been changed
  PCR channel can be changed by AP because of several reasons
    OBSS interference mitigation
    Coverage enhancement (5 GHz → 2.4 GHz)
    Throughput enhancement (2.4 GHz → 5 GHz)
    Security
  If WUR channel is selected in one of PCR channels, WUR channel may be changed whenever PCR channel is changed

## Slide 6: Channel Switch Scenarios
Scenario 2: Poor performance on WUR channel
  Current WUR channel has poor performance by following factors
    Dense environment
    OBSS interference
    Poor channel quality
  An AP may can change current WUR channel when it determines that the current WUR channel is not appropriate for WUR operation

## Slide 7: Channel Switch Scenarios
Scenario 3: New WUR STA cannot support current WUR channel
  A newly associated WUR STA that wants to operate in WUR mode may not support current WUR channel
  If an AP wants to support WUR operation on the WUR STA, current WUR channel shall be changed

## Slide 8: WUR channel switch
An AP shall have a capability of WUR channel switch and have to notify the channel switch information to WUR STAs
WUR channel switch information may be transmitted through PCR channel because that information needs robustness and acknowledgement
  We may reuse CSA information element
  WUR mode signaling can be used for channel switch

## Slide 9: Summary
In this submission, we address channel switch issue in WUR
An AP may have to change its WUR channel in some cases, and then it has to notify channel switch information to WUR STAs
  Channel switch information will be transmitted through PCR

## Slide 10: Straw poll 1
Do you support following sentences?
  11ba spec shall define a mechanism to indicate channel switch information for WUR STA

## Slide 11: Straw poll 2
Do you support following sentences?
  11ba spec shall define a mechanism to indicate channel switch information for WUR STA and that channel switch information can be delivered on primary connectivity radio

## Slide 12: References
[1] 11-17-0031-00-00ba-channel-issue-in-wur
[2] 11-17-1651-00-00ba-WUR-channel-issue