## Slide 1
WUR Wakeup Channel Access
Date: 2017-03-11
Authors:

## Slide 2: Overview
WUR Wake up procedure is initiated after wakeup delay
STAs’ presence check may be required depending on situation/capability
PS-Poll/Data transmission can be used for presence check
At wakeup time, channel access should be defined
In this contribution, considerations on WUR wakeup channel access are presented

## Slide 3: WUR Wakeup Procedure
WUR Procedure: Single User Case
  Case 1: Without Presence Check
    STA can save power without transmitting presence indication (PS-Poll/Data)
    No special 802.11 procedure for WUR wakeup
    Error recovery procedure for data TX failure is required
  Case 2: With Presence Check with 802.11 PS-Poll /Data frame
    Conventional PS-Poll transmission procedure needs to be modified or Data frame transmission procedure needs to be defined
    Data transmission failure case can be handled by normal 802.11 procedure

## Slide 4: WUR Wakeup Procedure
WUR Procedure: Multi User Case
  Case 1: Without Presence Check
    No special 802.11 procedure for WUR wakeup
    Error recovery procedure for data TX failure may be required
  Case 2: With Presence Check with 802.11 PS-Poll Frame/Data frame
    STAs need to wait for Trigger frame
    A new EDCA parameter set for MU wakeup can be used to delay SU PS-Poll /Data frame transmission

## Slide 5: Presence check indication in WUR packet
Presence check should be optionally enabled, depending on situations or STAs’ capability.
  Enable (example cases)
    STAs without power consumption constraint
    Large amount of data transmission
    number of STAs in WUR packet <= maximum number of MU transmission STAs
  Disable (example cases)
    STAs with strict power consumption constraint
    number of STAs in WUR packet > maximum number of MU transmission STAs (e.g., broadcast or multicast packet transmission)

## Slide 6: Presence check indication in WUR packet
Single User
Multi User
Channel Access for PS-Poll/Data needs to be considered
Channel Access for PS-Poll/Data needs to be considered

## Slide 7: Channel access for PS-Poll/Data frame transmission
Single User
  A normal EDCA parameter set or a high priority EDCA parameter set
Multi-User
  Trigger Indication = 0
    Same as Single User case
  Trigger Indication = 1
    A low priority EDCA parameter set
      Trigger frame has higher priority
      In case of channel idle, DIFS applies causing collision
    Fixed MU delay time to wait for Trigger frame
      Until the indicated delay time, STAs are prohibited from data transmission (NAV-Virtual carrier sensing)

## Slide 8: WUR MU Wakeup Channel Access
A Low Priority EDCA Parameter Set
Fixed MU delay time to wait for Trigger frame
  Virtual Carrier Sensing: NAV is set until the indicated time
  AP makes the channel busy

## Slide 9: Conclusion
WUR wakeup procedures for both SU and MU cases were discussed
  Presence check should be optionally enabled, depending on situations or STAs’ capability.
Channel access procedure for presence check (PS-Poll/Data transmission) needs to be further investigated
  EDCA parameters for WUR wakeup
  Virtual carrier sensing (NAV) for MU

## Slide 10: Straw Poll
Do you agree with the following
  WUR presence check with a STA’s uplink packet (e.g., PS-Poll or Data or TBD frame) transmission prior to data transmission is optionally turned on and off.