## Slide 1: Training Protocols for DL MU-MIMO in 802.11ay
Date:
Authors:

## Slide 2: Introduction
DL MU-MIMO is included in 11ay
An essential part of DL MU-MIMO operation is the obtaining of channel information (at the AP) for proper user pairing and digital precoding
Depending on the scenario, UL training may be more efficient (lower overhead etc.) than explicit (DL) training
  And vice versa
  Other 5G communities are adopting UL training for mmWave

## Slide 3: Introduction
In this presentation, we will present different training mechanisms
  In principle, one is DL based and the other UL based
  The methods are based on principles from 11ad/ay
  We will look at training with an SLS phase and without SLS
  Concerns raised during last f2f meeting regarding UL trigger frame are addressed

## Slide 4: Hardware Model
AP
…
antennas
…
RF chains
STA
…
antennas
…
RF chains
We consider a hybrid scenario (not fully digital)
Due to this, one needs to find good analog beams (SLS, BRP, etc.) before doing any digital precoding
The proposed UL training mechanism is useful for the digital precoding

## Slide 5: Example Scenario
In our presentation, we will (for simplicity) assume that
  AP has 4 RF chains
  Each STA has 1 RF chain

## Slide 6: Envisioned DL Training Mechanisms With SLS

## Slide 7: Envisioned DL training with SLS
STA
RF
Step 1 (SLS): Find best transmit and receive beams (with TRN-R) for MU-MIMO STAs
TRN-R
TRN-R
TRN-R
TRN-R
1
2
3
4
STA
RF
AP
RF
RF
RF
RF

## Slide 8: Envisioned DL training with SLS
Step 2-1: Each STA feedbacks best transmit direction (along its best TRN-R beam, assuming reciprocity [1]) via scheduling during step 1. AP is receiving in omni mode
STA
RF
2
STA
RF
3
AP
RF
RF
RF
RF

## Slide 9: Envisioned DL training with SLS
Step 2-2: Omni reception at AP could be replaced by directional reception, as introduced in [1]
STA
RF
STA
RF
1
1
2
2
3
3
4
4
AP
RF
RF
RF
RF

## Slide 10: Envisioned DL training with SLS
Step 3-1: AP transmits DL training packet in each reported direction
2
TRN-TR
STA
RF
STA
RF
CSI
3
TRN-TR
CSI
2
3
AP
RF
RF
RF
RF

## Slide 11: Envisioned DL training with SLS
Step 3-2: AP transmits DL training packet (or several training packets) in one joint direction and polls for CSI
2+3
TRN-TR
STA
RF
STA
RF
CSI
CSI
Poll
2
Poll
3
2
3
+
AP
RF
RF
RF
RF

## Slide 12: Envisioned DL training with SLS
Step 3-3: AP transmits DL training packet (or several training packets) in one direction and awaits CSI according to scheduling during step 1
2+3
TRN-TR
STA
RF
STA
RF
CSI
CSI
2
3
+
AP
RF
RF
RF
RF

## Slide 13: Envisioned UL Training With SLS

## Slide 14: Envisioned UL training with SLS
STA
RF
Step 1 (SLS): Find best transmit and receive beams (with TRN-R) for MU-MIMO STAs
TRN-R
TRN-R
TRN-R
TRN-R
1
2
3
4
STA
RF
AP
RF
RF
RF
RF

## Slide 15: Envisioned UL training with SLS
Step 2-1: Each STA feedbacks best transmit direction (along its best TRN-R beam, assuming reciprocity [1]) via scheduling during step 1
STA
RF
2
STA
RF
3
AP
RF
RF
RF
RF

## Slide 16: Envisioned UL training with SLS
Step 2-2: Omni reception at AP could be replaced by directional reception, as introduced in [1]
STA
RF
STA
RF
1
1
2
2
3
3
4
4
AP
RF
RF
RF
RF

## Slide 17: Envisioned UL training with SLS
Step 3-1: AP polls each STA to transmit training packet
STA
RF
STA
RF
Poll
2
2
Poll
3
3
AP
RF
RF
RF
RF

## Slide 18: Envisioned UL training with SLS
Step 3-2: AP transmits a joint poll (or several polls), acting as a trigger frame, that schedules all STAs
STA
RF
STA
RF
Poll
2+3
2
3
AP
RF
RF
RF
RF
+

## Slide 19: Envisioned UL training with SLS
Step 3-3: No polling due to scheduling during step 1 (SLS)
STA
RF
STA
RF
2
3
AP
RF
RF
RF
RF

## Slide 20: Envisioned Training With BRP

## Slide 21: Envisioned DL training with BRP
AP appends BRP field after DTI in MU-MIMO packet
  Polling could be replaced by scheduling
TRN-TR
STA
RF
STA
RF
CSI
CSI
Poll
2
Poll
3
AP
RF
RF
RF
RF

## Slide 22: Envisioned UL training with BRP
Step 3: AP appends a ”BRP poll” field after DTI in MU-MIMO packet, acting as a trigger frame, that schedules all STAs
STA
RF
STA
RF
Poll
2
3
AP
RF
RF
RF
RF

## Slide 23: Benefits of UL Training
Significantly less training overhead (for same channel information) in many scenarios
  Faster access to CSI estimates => more time for data transmission
Requires no CSI feedback and quantization
  The AP directly estimates digital CEF (no STA feedback needed)

## Slide 24: Straw Poll 1
Do you agree on including the BRP UL training as an optional mechanism into the 11ay SFD draft?
  Y/N/A:

## Slide 25: Straw Poll 2
Do you agree on including the SLS UL training as an optional mechanism into the 11ay SFD draft?
  Y/N/A:

## Slide 26: References
[1] IEEE 802.11-17/0067r1