## Slide 1: OFDM Pilot Sequences in 11ay
Date: 2017-05-10
Authors:

## Slide 2: Introduction
This presentation proposes frequency domain pilot sequences for EDMG OFDM PHY

## Slide 3: Considerations of Pilot sequences in 11ay(1/2)
Considering channel bonding, frequency domain pilot sequence for EDMG OFDM PHY should be newly defined for each channel bonding case (NCB=2/NCB=3/NCB=4)
Since the maximum number of spatial streams per STA is eight as defined in draft, pilot sequences up to 8 streams should be defined
We assume that
  For single channel transmission, the number of pilot subcarriers is 16 as same as 11ad
  For channel bonding transmission(CB>1), the number of pilot subcarriers is proposed in [1] as follows
    2CB : 16*2 + 4 = 36
    3CB : 16*3 + 4*2 = 56
    4CB : 16*4 + 4*3 = 76

## Slide 4: Considerations of Pilot sequences in 11ay(2/2)
In [2], they show simulation results that mutual orthogonal pilot sequence between spatial streams may give more robust performance(i.e. residual CFO estimation) for correlated channels
Orthogonal pilot sequence design makes pilot tracking more robust against various scenario

## Slide 5: How to design the pilot sequence(1/3)
We consider criteria on how to design the pilot sequence
  1. Simple extension property
    Considering HW complexity, extension method is more desirable than independent sequence for each CB
  2. Mutual orthogonality
    For 8 mutual orthogonal sequences, at least sequence of 8 length(i.e. ) is needed
  3. Low PAPR
When we consider above,
  We propose to define only to make pilot sequence for all CB factor
  With and , it is possible to make mutual orthogonal sequences by simple way as described in next slide

## Slide 6: How to design the pilot sequence(2/3)
The pilot sequence for each channel bonding cases is defined in Table1 below
The pilot sequences and are defined at the next slide
 | Pilot sequences for each channel bonding
1 | 
2 | = [ ]
3 | = [ ]
4 | = [ ]
 | Pilot sequences for each channel bonding
1 | 
2 | 
3 | 
4 | 
Table1. Definition of pilot sequence for each CB

## Slide 7: How to design the pilot sequence(3/3)
The pilot sequences and are defined in table 2 below
is proposed in [3]
1 | [ 1 1 1 -1 1 1 -1 1 1 1 1 -1 -1 -1 1 -1] | [-1 +1 -1 +1 +1 -1 -1 -1 -1 -1 +1 +1]
2 | [-1 -1 -1 1 -1 -1 1 -1 1 1 1 -1 -1 -1 1 -1] | [+1 -1 +1 +1 -1 -1 -1 -1 -1 +1 +1 -1]
3 | [-1 -1 -1 1 1 1 -1 1 -1 -1 -1 1 -1 -1 1 -1] | [-1 +1 +1 -1 -1 -1 -1 -1 +1 +1 -1 +1]
4 | [1 1 1 -1 -1 -1 1 -1 -1 -1 -1 1 -1 -1 1 -1] | [+1 +1 -1 -1 -1 -1 -1 +1 +1 -1 +1 -1]
5 | [-1 -1 1 -1 -1 -1 -1 1 -1 -1 1 -1 1 1 1 -1] | [+1 -1 -1 -1 +1 -1 -1 +1 -1 +1 -1 +1]
6 | [1 1 -1 1 1 1 1 -1 -1 -1 1 -1 1 1 1 -1] | [-1 -1 +1 -1 -1 -1 +1 +1 -1 -1 +1 +1]
7 | [1 1 -1 1 -1 -1 -1 1 1 1 -1 1 1 1 1 -1] | [-1 -1 -1 +1 -1 +1 -1 +1 +1 +1 +1 +1]
8 | [-1 -1 1 -1 1 1 1 -1 1 1 -1 1 1 1 1 -1] | [-1 -1 -1 -1 +1 -1 +1 -1 +1 +1 +1 -1]
1 | [ 1 1 1 -1 1 1 -1 1 1 1 1 -1 -1 -1 1 -1] | [-1 +1 -1 +1 +1 -1 -1 -1 -1 -1 +1 +1]
2 | [-1 -1 -1 1 -1 -1 1 -1 1 1 1 -1 -1 -1 1 -1] | [+1 -1 +1 +1 -1 -1 -1 -1 -1 +1 +1 -1]
3 | [-1 -1 -1 1 1 1 -1 1 -1 -1 -1 1 -1 -1 1 -1] | [-1 +1 +1 -1 -1 -1 -1 -1 +1 +1 -1 +1]
4 | [1 1 1 -1 -1 -1 1 -1 -1 -1 -1 1 -1 -1 1 -1] | [+1 +1 -1 -1 -1 -1 -1 +1 +1 -1 +1 -1]
5 | [-1 -1 1 -1 -1 -1 -1 1 -1 -1 1 -1 1 1 1 -1] | [+1 -1 -1 -1 +1 -1 -1 +1 -1 +1 -1 +1]
6 | [1 1 -1 1 1 1 1 -1 -1 -1 1 -1 1 1 1 -1] | [-1 -1 +1 -1 -1 -1 +1 +1 -1 -1 +1 +1]
7 | [1 1 -1 1 -1 -1 -1 1 1 1 -1 1 1 1 1 -1] | [-1 -1 -1 +1 -1 +1 -1 +1 +1 +1 +1 +1]
8 | [-1 -1 1 -1 1 1 1 -1 1 1 -1 1 1 1 1 -1] | [-1 -1 -1 -1 +1 -1 +1 -1 +1 +1 +1 -1]
Table2. Definition of and

## Slide 8: Simulation Results :PAPR(1/5)
We checked PAPR to verify that proposed OFDM pilot sequences have low PAPR property
The number and location of data, DC and pilot subcarriers are based on [1]
Data : Random data with 64QAM modulation
4 times up-sampling

## Slide 9: Simulation Results :PAPR(2/5)
Data part PAPR with each stream’s pilot sequences for 1CB

## Slide 10: Simulation Results :PAPR(3/5)
Data part PAPR with each stream’s pilot sequences for 2CB

## Slide 11: Simulation Results :PAPR(4/5)
Data part PAPR with each stream’s pilot sequences for 3CB

## Slide 12: Simulation Results :PAPR(5/5)
Data part PAPR with each stream’s pilot sequences for 4CB

## Slide 13: Conclusion
Since the maximum number of spatial streams per STA is eight in 802.11ay, 8 pilot sequences should be defined for 8 streams
Mutual orthogonality between streams should be considered
We propose that pilot sequences for 2CB, 3CB, 4CB with and
  2CB : = [ ]
  3CB : = [ ]
  4CB : = [ ]

## Slide 14: SP/M
Do you agree :
  to define OFDM pilot sequences for NCB>1 as described in (11-17-0712-00-00ay-30 6 1 OFDM Pilot sequences)?

## Slide 15: Reference
[1] 11-17-0597-00-00ay 30 6 1 OFDM Signal Parameters
[2]Aoki, T.; Sandell, M.; , "Analysis of pilots for residual frequency offset estimation in MIMO OFDM systems," Wireless Communications, IEEE Transactions on , vol.8, no.3, pp.1128-1132, March 2009.
[3] 11-17-0627-01-00ay OFDM Pilot Definition in 11ay