## Slide 1: WUR Link Budget Analysis Follow-up: Data Rates and SIG Bits Protection
Date: 2017-05-07
Authors:

## Slide 2: Introduction
[1] Recap: WUR Link budge analysis shows, for 250kbps OOK,
  There is ~30dB link margin at close distance for indoor channels
  The coverage is shorter than 30m in UMi-NLOS channels @2.4G
  Multiple data rates can be beneficial to achieve either better efficiency or coverage
In this contribution, we address two issues:
  Provide simulation results for multiple data rate with and without Manchester Coding (MC).
  Signaling (SIG) bits are needed for each WUR packets to indicate the data rate and packet length options [2]. How many protection bits are needed for the SIG bits?

## Slide 3: Simulation Settings
Device BW: 20MHz
Signal BW: ~4MHz, center 12 tones (without DC)
Waveform: 12 tone sequence
  [-1 -1 -1 1 1 -1 -1 -1 -1 1 -1 1]
  Good property: ave. CP power is similar to ave. signal power for all data rates
Number of information bits: 100
No impairments: phase noise, CFO, IQ imbalance

## Slide 4: Ch: AWGN
Manchester Coding (MC) is beneficial for all data rates

## Slide 5: Ch: DNLos
Manchester Coding (MC) is beneficial for all data rates

## Slide 6: Ch: UMi-Los
Manchester Coding (MC) is beneficial for all data rates
1Mbps rate has error floor above 1% for UMi-Los

## Slide 7: Data Rate Discussion
Confirmed with prior contributions[3][4], Manchester Coding has advantages in WUR OOK waveform design
  2~3dB SNR gain for all channel types
  Simple OOK detection with SNR-based threshold setting
Number of data rates
  125Kbps, 250Kbps, 500Kbps, 1Mbps can cover large range of channels and sensitivity
  2 bits signaling for the data rates

## Slide 8: SIG Bits Protection
The signaling bits need protection for WUR receiver to save power
Assume total 4 bits of WUR-SIG: 2 bits to signal data rate, 2 bits to signal packet lengths
Cyclic redundancy check (CRC) is a popular technique for error detection

## Slide 9: Ch: AWGN
P-false is much higher for 2bit and 3bit CRC, though P-miss is lower

## Slide 10: Ch: DNLos
P-false is much higher for 2bit and 3bit CRC

## Slide 11: Ch: UMi-Los
P-false is much higher for 2bit and 3bit CRC

## Slide 12: Number of CRC Bits
Since there are only 4 SIG bits, 2 or 3 CRC bits are relatively large. The error of CRC bits causes large P-false.
1-bit parity has good balance between P-false and P-miss, and P-miss is roughly one order lower than SIG bits error

## Slide 13: Straw Poll 1
Do you agree to have two SIG bits to signal data rates?
  Yes
  No
  Abstain

## Slide 14: Straw Poll 2
Do you agree to have one bit parity for the SIG bits protection in one WUR packet?
  Yes
  No
  Abstain

## Slide 15: References
[1] Rui Cao et al., “WRU Link Budget Analysis”, IEEE 802.11-17/0339r1, March, 2017
[2] Liwen Chu et al. “WUR MAC and Wakeup Frame”, IEEE 802.11-17/0124r4, March 2017
[3] Eunsung Park and et al., , “Further Investigation on WUR
Performance”, IEEE 802.11-16/1144r0, Sept. 12, 2016.
[4] Steve Shellhammer and et al., “WUR Modulation and Coding”, IEEE 802.11-17/0366r0, Mar., 2017