## Slide 1: Follow-up on Update Wake-Up Information in WLAN with Wake-Up Radio Receivers
Date: 2017-03-10
Authors:
Name | Affiliation | Address | Phone | Email
Jianhan Liu | Mediatek | 2840 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | jianhan.Liu@mediatek.com
Tianyu Wu |  |  |  | 
Thomas Pare |  |  |  | 

## Slide 2: False Wake-up Problems
      Main applications of WUR WLANs include IOT sensors running on batteries. Frequently falsely wake up the main receiver for a regular data packets can quickly drain the battery and ultimately disable the device.
      The following false wake-ups can happen in WUR WLAN
        False wake-ups due to wake-up information collisions in dense OBSS environment;
        Wake-up attacks by self-generating wake-up information or re-play wake-up information.
      When a WUR station detects the false wake-ups or wake-up information collisions, WUR information should be updated or re-assigned.

## Slide 3: Assign or Update Wake-up Information
Wake-up information of WUR STAs are assigned for each STA either:
  As part of the onboarding process, like how a password or a client certificate is provisioned to a STA before it is associated to an AP
  Or as part of the authentication and session key generation process
          Wake-up Information updating can be initiated either by STAs via sending a wake-up information change request or by the AP via sending a packet that contains wake-up information change entities directly.
  A WUR STA can initiate a request to change the wake-up information
    When a STA repeatedly wakes up, but no meaningful regular packet is received or the received packet is not for itself. Then the STA can initiate a process of update of wake-up information
  AP can initiate the update of wake-up information
    When an AP detects there are collisions of wake-up information from OBSS or AP needs to re-assign the wake-up information for a STA or a group of STAs, then AP can initiate the update of wake-up information directly.

## Slide 4: Wake-up information updating
For wake-up information updating, it is important to make sure that both the AP and the WUR station know if the update is successful.
  A simple send the packet and receive ACK scheme may not work well. For example, if the AP sends the packet with wake-up information update information, the WUR station updated its wake-up information, but the ACK is failed at the AP. Then the AP does not know if the WUR station has updated its wake-up information or not.
The wake-up sequence update or assign is regarded as complete only after successful hand-shaking frame exchange.

## Slide 5: Sequence of Wake-Up information Update – Immediate ACK Case
In case there is no TXOP protection for the WU information update message exchange, the exchange sequence can be divided into two updates from both AP and STA sides.
The ACK after SIFS is used instead of immediate UPDATE RSP.

## Slide 6: Straw Poll #1
Do you agree that IEEE 802.11ba shall provide a Wake-Up information update mechanism?

## Slide 7: Straw Poll #2
Do you agree the sequence of Wake-Up information update shown in slide #5?
  The detailed frame formats are TBD.