## Slide 1
WUR with conventional 802.11 power save
Date: 2017-05-08
Authors:

## Slide 2: Introduction
WUR AP could transmit both multicast WUR signal and unicast WUR signal[1]
  Multicast WUR signal could be transmitted for transmitting multicast or broadcast frame(s)
WUR procedures for the conventional 802.11 power save mechanisms are not defined in 802.11ba
  Is it independent issues?
  Or is WUR procedure performed with the conventional power save mechanism?
Multiuser WUR shall be considered because of its delay and power save requirements
  PSMP is the conventional power save mechanism for multi user case

## Slide 3: Recap : 802.11 power save
PS-poll frame can be transmitted after TIM reception
U-APSD is a power save mechanism which is initiated by an uplink STA
PSMP frame is multicast(broadcast) frame for initiating power saving service period for multiple users

## Slide 4: PS-poll with WUR
Without any changes on the conventional power save procedure, WUR could be utilized
However it requires large delay and additional power usage due to TIM reception delay

## Slide 5: U-APSD with WUR
Without any changes on the conventional U-APSD procedure, WUR could be utilized
U-APSD does not require additional delays caused by channel access of an AP because presence check is initiated by an uplink STA

## Slide 6: Unicast WUR power save
From the motion result of the last meeting, unicast wake-up procedure has the following procedure[2]
  R.4.5.2.A: After AP sends a unicast wake-up packet to a STA, AP waits for a timeout interval
    If AP receives any transmission from the STA within the timeout interval, then the wake-up packet transmission is successful
    Otherwise, the wake-up packet transmission fails, and AP may retransmit the wake-up packet to the STA
It means U-APSD could be utilized for WUR procedure but the conventional PS-poll method shall not be supported

## Slide 7: Unicast WUR power save
If PS-poll frame is needed to be utilized in WUR procedure, spec shall specify to regard WUR frame reception as a TIM reception
The procedure is identical to U-APSD but only difference is that the uplink frame is a PS-poll frame

## Slide 8: Multicast WUR power save
From the motion result of last meeting, multicast wake-up procedure has the following procedure[2]
  R.4.5.3.B: After the transmission of broadcast wake-up frame, the AP can transmit broadcast/multicast frames through primary connectivity radio after the preparation period.
It means the AP could transmit Trigger Frame or PSMP frame which initiates multi-user TXOP after the preparation period
  However, MU PPDU is not supported in this case

## Slide 9: PSMP with WUR
Because wake-up frame and the preparation period do a role of time scheduler, additional scheduling procedure for PSMP frame is not needed
Multiple users could be supported and WUR STAs could be set to doze state during PSMP service period

## Slide 10: Conclusions
For unicast wake-up procedure, U-APSD could be utilized and it does not require any changes on existing spec
  In order to utilize PS-poll frame, some changes or some expedients shall be followed(e.g., regarding WUR frame reception as a TIM reception)
For multicast wake-up procedure, using PSMP could be a solution
  It provides scheduling information over its PSMP service period
  If a STA is not scheduling in the PSMP service period, it could be set to doze state immediately
  Group addressed transmission time need to be used for MU transmission period

## Slide 11: References
[1] 11-17-0124-04 “WUR MAC and Wakeup Frame”
[2] 11-17-0575-00 “Specification Framework for TGba”

## Slide 12: Straw poll
Do you agree to add the followings to 802.11ba SFD?
  802.11ba should be able to be operated with the conventional 802.11 power save procedures, i.e., 802.11ba procedure shall be defined to wake up STAs which are turned into the conventional 802.11 power save modes.