## Slide 1: STBC for OFDM PHY in 11ay
Date: 2017-05-07
Authors:

## Slide 2: Introduction
This presentation proposes Space-Time Block Coding (STBC) scheme definition for EDMG OFDM PHY in 11ay.

## Slide 3: STBC in 11n/ac for OFDM PHY
The IEEE 802.11 n/ac standard defines the STBC schemes with the number of input spatial stream NSS and the number of output space-time streams NSTS = 2*NSS.
The signal subcarriers mapping for (NSS = 1, NSTS = 2) scheme is shown in figure below, [1].

## Slide 4: STBC in 11n/ac for OFDM PHY (Cont’d)
Received signals in frequency domain:
  OFDM symbol n = 1:
    R1(k) = H1(k)*X(k) – H2(k)*Y*(k) + Z1(k);
  OFDM symbol n = 2:
    R2(k) = H2(k)*X*(k) + H1(k)*Y(k) + Z2(k);
  where: H1(k) and H2(k) – channel coefficients as shown below;
  Z1(k) and Z2(k) – AWGN ~CN(0, σ2) noise samples;

## Slide 5: STBC in 11n/ac for OFDM PHY (Cont’d)
ZF equalizer solution:
  The estimated X^(k) and Y^(k) signals can be written as follows:
  where H1^(k) and H2^(k) estimations of channel coefficients;

## Slide 6: SQPSK OFDM Modulation in 11ay
SQPSK modulation mapping is shown in figure below:
  Two coded bits (c2k, c2k+1) are modulated to two subcarriers (Xk, XP(k));
  The modulation is performed in 2 steps:
    First, two BPSK points are modulated as x2k = (2*c2k-1), x2k+1 = (2*c2k+1-1);
    Second, two QPSK points are modulated by multiplication on matrix Q;
  P(k) = 168 + k for Static Tone Pairing (STP) mode and can be permutation of indexes for Dynamic Tone Pairing (DTP) mode in the range [168, 335];

## Slide 7: QPSK OFDM Modulation in 11ay
QPSK modulation mapping is shown in figure below:
  Four coded bits (c4k, c4k+1, c4k+2, c4k+3) are modulated to two subcarriers (Xk, XP(k));
  The modulation is performed in 2 steps:
    First, two QPSK points are modulated as x2k = ((2*c4k-1)+j(2*c4k+2-1))/; x2k+1 = ((2*c4k+1-1)+j(2*c4k+3-1))/;
    Second, two 16QAM points are modulated by multiplication on matrix Q;
  In essence, SQPSK and QPSK represent normal BPSK and QPSK modulations accordingly with some precoding by Q matrix of size 2x2;

## Slide 8: STBC for SQPSK/QSPK in 11ay
The STBC mapping scheme with SQPSK, QPSK modulation is shown below. P(k) = NSD/2 + k, i.e. Static Tone Paring (STP) is used.
It occupies 8 subcarriers and extracts space-time-frequency diversity gain.

## Slide 9: STBC for OFDM in 11ay
For 11ay data transmission it is proposed to keep the same scheme with (NSS = 1, NSTS = 2) as defined for 11n/ac.
It is proposed to introduce space-time pilots encoding as shown in figure below.

## Slide 10: STBC for OFDM in 11ay (Cont’d)
The sequences PNSP(iSTS, :) are composed of ±1 symbols, therefore conj() is not required.
NSP defines the number of pilots per OFDM symbol.
It is proposed to reuse sequences PNSP(iSTS, :) defined for regular MIMO transmission.

## Slide 11: SP/M
Do you agree:
  To include spec text proposed in (11-17-0753-00-00ay 30 6 6 2 Space Time Block Coding) defining STBC scheme for OFDM PHY into the spec draft?

## Slide 12: References
IEEE802.11-2016
Draft P802.11ay_D0.3