## Slide 1: Improvements to enhanced SLS beamforming
Date: 2017-05-09
Authors:

## Slide 2: Introduction
Enhanced SLS beamforming [1] can provide significant gains in dense environments or in asymmetrical beamforming configuration [2]
  Use of directive receive patterns in association
    Low collision probability, high link budget
  Prerequisite: Responders require reciprocity
    Responder needs to decide for Tx beam based on Rx beam
This presentation proposes an extension to
  allow responders with weak reciprocity to participate in enhanced SLS
    Lowered reciprocity requirements
  allow for simultaneous Tx and Rx beam improvement for responders with sufficient reciprocity in enhanced SLS

## Slide 3: Enhanced SLS beamforming (recap)
Enhanced SLS comprises three steps [1, 2]
  TRNs are appended to beacon frames in BTI
    Responding STAs can determine best Rx beam
  Beamforming SP holds several listen periods, where the initiator (AP) uses directional Rx beams
    Responders transmit directionally in a space-time slot
      Transmission of a single SSW frame in a slot where the AP receives with appropriate pattern
      Tx beam selection based on best Rx beam
        Reciprocity required
  Feedback phase
    Sector ACK to each successfully received responder

## Slide 4: Enhanced SLS beamforming (recap)
Example of enhanced SLS [1]
slot
space-time slot

## Slide 5: Properties
Enhanced SLS beamforming implies
  Reciprocity at responder
    Responder concludes on Tx beam based on Rx beam
  Successful beam training with a single SSW frame
  Rx and Tx beam granularity of responder is determined by number of TRNs in BTI
    Number of TRNs may be selected low in long BTIs for overhead reasons
Improvements target
  STAs with weak reciprocity
    Remove uncertainty in responder Tx beam by training
  STAs with reciprocity
    Simultaneous improvement of Tx and Rx beam

## Slide 6: Proposal
We propose to enable responders to transmit in several consecutive space-time slots within in a slot for beamforming SP
  The maximum number of space-time slots a responder can use is signaled in the configuration of beamforming SP
Benefits
  Responders with weak reciprocity can train several candidate Tx beams
    Weak reciprocity comes with uncertainty in Tx beams
    Uncertainty can be removed by training
  Responders with sufficient reciprocity can improve beam training
    Short responder sector sweep can improve transmit and receive beam simultaneously

## Slide 7: Signaling Proposal
Signaling for maximum number of consecutive space-time slots which can be occupied by a STA during a slot of beamforming SP
  Use two bits in EDMG Extended Schedule Element when ‘asymmetric beamforming training‘ is set
    Otherwise bits are reserved

## Slide 8: Signaling Proposal (cont)
Exponential encoding of Nmax STS
  Covers wide range
    „00“: A STA can occupy 1 space-time slot
    „11“: A STA can occupy up to 8 space-time slots
Nmax STS value in field | Actual Nmax STS value
00 | 1
01 | 2
10 | 4
11 | 8

## Slide 9: Summary
Extension of Enhanced SLS beamforming
  Extension of beamforming SP to support responders to train in multiple consecutive space-time slots
  Maximum number of occupied space-time slots by a particular responder (Nmax STS) is signaled by the initiator in EDMG Extended Schedule Element
    Exponential signaling
Benefits
  Responders with weak reciprocity can participate in enhanced SLS
  Responders with sufficient reciprocity can improve beam training for transmitter and receiver simultaneously

## Slide 10: Straw Poll
Do you agree to add the amendment text of 11-17/0771r0 to D0.3?

## Slide 11: References
[1] Candidate Draft P802.11ay D0.3
[2] 11-17/0067r1 Enhanced SLS BF flow for efficient AP-STA access in dense environment