## Slide 1: WUR Mode Signaling
Date: 2017-07-10
Authors:
Name | Affiliation | Address | Phone | Email
Suhwook Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | suhwook.kim@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
We have decided to define on/off duty cycle operation for WUR STA in SFD
Also we have decided to define WUR mode signaling
So in this submission, we will address WUR mode signaling issue related to duty cycle operation

## Slide 3: SFD text (DCN: 575r1)
R.4.3.A: STA can have Duty cycle mode for wake-up receiver
R.4.3.C: AP decides the starting point for one WUR duty cycle schedule. How to indicate the starting point is TBD
R.4.5.A: WUR mode signaling shall be defined for the WUR STA to enter the WUR mode
  Explicit or implicit signaling is TBD
  If signaling is explicit, WUR mode signaling is done on the Primary connectivity radio
  Wake-up operating parameter may be notified in WUR mode signaling
    Detailed parameters are TBD

## Slide 4: STA operating mode
We assume that there are three operating modes of WUR STA
  Descriptions of each mode are discussed in another submission [1]
 | Main Radio | Wake-up Radio
WUR normal mode | OFF | Always ON
WUR duty cycle mode | OFF | Switch between ON and OFF
Active mode | ON | OFF

## Slide 5: Mode Signaling
Active mode ↔ WUR normal mode
Active mode ↔ WUR duty cycle mode
WUR duty cycle mode ↔ WUR normal mode (via Active mode)
Active mode ↔ PS mode (Existing power save)

## Slide 6: Explicit or Implicit signaling
Explicit signaling
  A specific management frame is used to indicate mode change
  STA/AP can exchange the detail parameters of mode signaling using the management frame
  Overhead is relatively high

## Slide 7: Explicit or Implicit signaling
Implicit signaling
  There isn’t a specific management frame for mode signaling
    Signaling can be indicated by existing frame exchange
      Power Management bit (in frame control field) may be used
    Signaling can be omitted after broadcast frame transmission in PCR
  Detail parameters cannot be exchanged during mode signaling
  Overhead can be minimized

## Slide 8: Ambiguity in implicit signaling
If a(n) STA/AP use implicit signaling to indicate WUR mode signaling, a specific rule for WUR mode indication should be pre-defined
  because detail parameters for WUR operation cannot be exchanged during implicit signaling
  If a STA sets the PM bit to 1 in UL frame without any additional information, an AP cannot identify the STA’s intention
    The STA may want to operate in legacy power saving feature (PSM)
    The STA may want to operate in WUR normal mode
    The STA may want to operate in WUR duty cycle mode
    The STA may want to maintain WUR mode that had operated before

## Slide 9: Proposed solution
Implicit WUR mode signaling shall be used only when a STA wants to return to WUR mode that had operated just before and WUR mode information isn’t changed
Explicit WUR mode signaling can be used when a STA wants to operate in WUR mode that hadn’t operated just before or WUR mode information should be changed

## Slide 10: Example
If a STA is operating in WUR normal mode
  implicit signaling can be used in returning to WUR normal mode from Active mode
  the STA has to use explicit signaling when it wants to operate in WUR duty cycle mode after data exchange in Active mode

## Slide 11: Example
Signaling example

## Slide 12: Summary
We addressed WUR mode signaling issue related to duty cycle operation
  If we use implicit signaling, there can be ambiguity on mode indication
So we proposed the solutions to resolve the ambiguity
  Implicit WUR mode signaling shall be used only when a STA wants to return to WUR mode that had operated just before without changing WUR mode information

## Slide 13: Straw poll 1
Do you agree to modify the text in SFD as follow?
  WUR mode signaling shall be defined for the WUR STA to enter the WUR mode by explicit or implicit signaling
    Explicit or implicit signaling is TBD
    If signaling is explicit, WUR mode signaling is done on the Primary connectivity radio
    Wake-up operating parameter may be notified in WUR mode signaling
      Detailed parameters are TBD

## Slide 14: Straw poll 2
Do you agree to add following text in SFD?
  Implicit WUR mode signaling is used in only when a WUR STA wants to return to WUR mode that had operated just before without changing WUR mode information
  Otherwise, explicit WUR mode signaling is used

## Slide 15: References
[1] 11-17-0953-00-00ba-WUR-mode-discussion
[2] 11-17-0651-02-00ba-indication-for-wur-duty-cycle