## Slide 1: Signaling Method for Multiple Data Rate
Date: 2017-07-09
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
Jinyong Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com

## Slide 2: Introduction
The Multiple data rate for WUR payload was approved in the last May meeting.
And, to indicate the various data rate for WUR payload, the following methods were discussed.
  Signaling(SIG) field [1] and Signature sequence [2]
In this contribution, we investigate two signaling methods for efficiently delivering data rate.
Also, we provide the simulation results of two methods considering the overhead and range requirement.

## Slide 3: Signature sequence design
To provide the information for data rate, signature sequence can be designed such that :
  One signature sequence indicates one specific data rate.
    For example, if the number of data rate which is used for WUR payload is 4, then we need the 4 different signature sequences.
  Each Signature sequence consists of “0” and “1”. and it also can be designed that “0” is not repeated continuously within sequence.
    For the signature sequence, a Pseudo-random sequence can be used.
  Signature sequence is designed to have a Hamming distance with equal error correction capability.
    By using the sequence with large Hamming distance, we can reduce the wrong detection of sequence due to bit error.

## Slide 4: Configuration of Signature sequence
Error correction is defined by using the following relation according to Hamming distance.
  Given a Hamming distance of HDcode
    Error detection : ed <= HDcode -1
    Error correction : ec <= (HDcode -1)/2
  If we assume that HD is 3 then we can correct the one error which is occurred due to bit flip.
According to Design criteria and Hamming distance, we use the following sequences in this contribution.
  (length , hamming distance)
    (6, 3≤HD<5)
      [0 1 0 1 0 1; 0 1 1 0 1 0; 1 0 0 1 1 0; 1 0 1 0 0 1]
    (9, 5≤HD<7)
      [0 1 0 1 0 1 0 1 1; 0 1 1 0 1 0 1 0 1; 1 0 1 0 1 1 0 1 0; 1 0 1 1 0 1 1 0 1]
    (12, 7≤HD<9)
      [ 0 1 0 1 0 1 0 1 0 1 0 1; 0 1 0 1 1 0 1 0 1 0 1 0; 1 0 1 0 1 0 1 0 1 1 0 1; 1 0 1 1 0 1 0 1 1 0 1 0 ]

## Slide 5: Signaling (SIG) field
We can assume that a information except the information related with decoding of WUR payload may be not transmitted by using the signaling field.
  We do not focus what information is included in signaling field in this contribution.
So, we consider that WUR-SIG consists of bits to signal data rate and CRC bits that are used for error detection.
  Assume 2/3 bits for CRC to detect the error of SIG fields.

## Slide 6: Data rate and required SNR
To indicate the multiple data rate which was discussed in [3], at least, we may need the 1 bit or 2 bits information.
  Assume the 2 bits to signaling data rate in this contribution.
The required SNR of 11ba to satisfy the range requirement in 2.4GHz may be 12 dB lower than that of primary radio transmission due to power regulation and Phase Noise[4].
  So, required SNR (at 1%) for control information(i.e. data rate ) can be obtained by considering the performance of L-SIG(at 1%) or the performance of Data part (at 10%)in primary radio.
  But, to secure the reliable operation of 11ba, we assume that required SNR (at 1%) should be lower than a minimum SNR for the data part of the primary radio.
    -3.7/-2dB is required at the PER of 1% in TGnD/UMi NLoS channels.

## Slide 7: Simulation Assumption
13 subcarriers (4 MHz) are used for a WUR symbol
  A sequences mapped to available subcarriers are optimized in terms of the PAPR
Information for data rate : 2 bits
Number of CRC bits : 2, 3
Length of signature sequence : 6, 9, 12
Data rate : 31.25Kbps, 62.5Kbps, 125Kbps
  We considered the various data rate to search the method which can reach the targeted SNR at 1% PER.
20MHz sampling rate
TGnD and UMi NLoS channels in 2.4GHz
No impairments
SNR is defined considering 20MHz bandwidth

## Slide 8: OOK symbol and length according to data rate
We applied the various data rate to each option to find whether the targeted SNR at 1% PER is achieved or not.
125Kbps
  8us OOK symbol with Manchester coding (4us ON+ 4us OFF and vice versa)
    Option1 (i.e. Signature sequence) : 72us for SS(9,5) , 96us for SS(12,7)
62.5Kbps
  16us OOK symbol with Manchester coding (4us ON+ 4us OFF + 4us ON+ 4us OFF vice versa)
    Option1 (i.e. Signature sequence) : 96us for SS(6,3), 144us for SS(9,5), 192us for SS(12,7)
  8us OOK symbol with Manchester coding (4us ON+ 4us OFF vice versa) and ½ BCC encoding
    Option2 (i.e. SiG field ) : 160us ( 2bits + 2bits CRC), 176us (2bits +3bits CRC)
31.25Kbps
  16us OOK symbol with Manchester coding (4us ON+ 4us OFF + 4us ON+ 4us OFF vice versa) and ½ BCC encoding
    Option2 (i.e. SiG field ) : 320us ( 2bits + 2bits CRC), 352us (2bits +3bits CRC)
      6 tail bits are considered to calculate the overhead

## Slide 9: Performance according to option
TGnD
  Error rate for SIG : ( # of packet with CRC error or # of packet with data error and CRC no error) / (# of total packet)
  Error rate for SS : (# of packet when the transmission and reception1) sequences are different )/( # of total packet)
1) reception sequence means detected sequence which is selected among signature sequences by using the Hamming distance.

## Slide 10: Performance according to option
UMi-NLoS

## Slide 11: SNR at 1% PER
TGnD ( targeted SNR at 1% PER : -3.7dB)
UMi ( targeted SNR at 1% PER : -2dB )
option | SIG field (w/BCC) |  |  |  | Signature sequence |  | 
 | 2bits + 2bitsCRC |  | 2bits + 3bits CRC |  | SS(6,3) | SS(9,5) | SS(12,7)
Data rate | 31.25Kbps | 62.5Kbps | 31.25Kbps | 62.5Kbps | 62.5Kbps | 62.5Kbps | 62.5Kbps
Overhead | 320us | 160us | 352us | 176us | 96us | 144us | 192us
SNR at 1% PER | -5.5dB | -3.7dB | -5dB | -3.6dB | -3dB | -4.8dB | -6dB
option | SIG field (w/ BCC) |  | Signature sequence |  | 
 | 2bits + 2bitsCRC | 2bits + 3bits CRC | SS(6,3) | SS(9,5) | SS(12,7)
Data rate | 62.5Kbps | 62.5Kbps | 62.5Kbps | 125Kbps | 125kbps
Overhead | 160us | 176us | 96us | 72us | 96us
SNR at 1% PER | -4.3dB | -3.4dB | -3dB | -2.6dB | -4dB

## Slide 12: Discussion (1/2)
In TGnD channel,
  Signature sequence (12,7) and (9,5) using the 62.5kbps data rate can meet the targeted SNR.
    As shown in appendix, if Manchester coding is not applied on OOK symbol, it can not meet the targeted SNR.
  if BCC encoding is applied on SIG field, received SNR when 62.5Kbps data rate is applied can approximately reach to the targeted SNR.
    But, for the reliable transmission, option 2(i.e. SIG field) may need to apply the lower data rate such as 31.25Kbps with BCC.
      It can occur the large overhead (i.e. 320us).
  The overhead of SS would be smaller than that of SIG field when we assume that the performance of two methods are reaching the targeted SNR.
    For minimization of overhead, SS(9,5) using 62.5Kbps can be considered.

## Slide 13: Discussion (2/2)
In UMi channel,
  Following cases can meet the targeted SNR
    Option 1 : SS(12,7) and SS(9,5) using 125Kbps data rate, SS(6,3) using 62.5Kbps data rate
    Option 2 : 2bit+CRC2 and 2bit +CRC3 using the 31.25kbps data rate with BCC
  For overhead minimization, the following methods can be considered.
    SS(9,5) using 125Kbps – 72us
    As shown in results, the Use of signature sequence (option 1)has a less overhead than a use of SIG field (option 2).

## Slide 14: Conclusion
In this contribution, we examined the two signaling methods for indicating the data rate of WUR payload.
By using the signature sequence(i.e. SS) for indicating the data rate, we can achieve the targeted SNR which is required for reliable transmission of WUR PPDU.
  SS does not require the larger overhead than SIG field to meet the targeted SNR.
    Overhead due to SS may be reduced by reducing the information for data rate.
  Also, to achieve the required SNR, we could consider the signature sequence that is supported the Manchester coding.

## Slide 15: Straw Poll 1
Do you agree to add following into 11ba SFD?
Signature sequence is used to indicate the data rate for 11ba payload.

## Slide 16: Straw Poll 2
Do you agree to add following into 11ba SFD?
Signature sequence is included in the WUR preamble.

## Slide 17: Straw Poll 3
Do you agree to add following into 11ba SFD?
Manchester code shall be used for Signature sequences .

## Slide 18: Reference
[1] IEEE 802.11-17/676r1, WUR Link Budget Analysis Follow-up: Data Rates and SIG Bits Protection
[2] IEEE 802.11-17/679r1, Preamble Design for WUR WLAN
[3] IEEE 802.11-17/0654r3 Multiple Data Rates for WUR
[4] IEEE 802.11-17/ 965r0 data-rate-for-range-requirement-in-11ba

## Slide 19: Appendix : OOK vs MC
TGnD

## Slide 20: Appendix : OOK vs MC
UMi