## Slide 1: Changes to IEEE 802.11ay in support of mmW Distribution Network Use Cases
Date: 2017-07-10
Authors:

## Slide 2: Abstract
This presentation proposes initial set of changes to IEEE 802.11ay [1] in support of mmW Distribution Network Use Cases [2]
  Ability to latch state of TSF counter to external PPS (e.g. over GPIO) in distribution nodes to enable network wide timing synchronization
    Maximum 1usec timing drift over 100msec
Implicit Block-ACK delayed to next SP allocated in opposite direction
  Golay code index selection per link
  Indication in the Beacon Transmission to indicate subsequent DTI pertains to the mmW Scheduled Access

## Slide 3: mmWave Distribution Network Use Cases [2]
Small cell
Wi-Fi AP
Fiber PoP (cabinet)
  WTTH
  WTTB
Small cell
  WTTB
  WTTH
Wi-Fi-AP
Alternative: Wireless inhouse
  WTTB
RGW
  mmW Distribution NW
  LOS 60 GHz narrow beam system
  Own management and control per mmWave mesh access area
  Route control protocol supports re-routing over radio links
  Auto-alignment installations via adaptive beamforming
  Redundancy of active equipment at “first” pole next to fiber PoP or via connections to 2 or more fiber PoPs
  Radio link degradation and outage recognition w/ failure localisation
Use case c) WiFi AP / SC
Focus on use case specific Mesh WBH requirements
  Mesh WBH
fiber
Provider
Network
mmWave AP
mmWave link
Fiber PoP (to Provider Network)
Use case a) WTTH
Use case b) WTTB

## Slide 4: Main Challenges to Achieve Full Potential for the mmW Distribution NW Use Cases
  Relatively large density with few hundred AP radio sectors per sqkm deployed in multi-hop multi-point topology
Despite DMG PHY, the co-channel interference remains the main impediment
      Random nature of co-channel interference prevents any meaningful interference management and mitigation on L2
      False locks
  mmW Distribution NW use case specifics
      Centralized controller for NW management
      Nodes are static (however, adaptive BF still needed)
      Upgrades for deployed topology are infrequent planned events
    Different set of constrains from typical nomadic use cases with handheld devices

## Slide 5: Co-channel Interference
Typical issues with random nature of co-channel interference, exposed and hidden node problems carry over to the new mmW Distribution NW Use cases
    In example bellow, each lamppost installation has 4 collocated APs (aka radio sectors)
Hidden node
Exposed node

## Slide 6: Interference Between SPs Across Network
Current spec enables data to be organized into CBAPs and SPs
Uncoordinated SPs across APs
  Uncontrolled interference across NW
Coordinated SPs across APs with BACK delayed to next slot in opposite direction
  Interference can be mitigated
Coordinated SPs across APs
  Interference still present from immediate BACK

## Slide 7: Network Wide Node Synchronization and Modified delayed BACK
Since nodes (APs) in mmW Mesh Network are static, random nature of intra-network interference can be minimized by semi-static coordination of transmissions (SPs) across links
  Provision for ability to latch the state of TSF counter to external PPS (ie, over GPIO) in each mesh node to enable network wide timing synchronization
    Maximum 1usec timing drift over 100msec
  Implicit Block-ACK delayed to next SP allocated in opposite direction
For sake of this presentation, we denote this mode as the Centralized Coordination Function (CCF), as opposed to Distributed Coordination Function (DCF)

## Slide 8: CCF and DCF
More than 6.5dB higher SIR for CCF vs DCF
Extra 2dB gain in SIR at 100m link distance for P region rain assumption

## Slide 9: Field Data
DCF
CCF
  * max achievable (MCS12 and MCS9)

## Slide 10: Blocking Effect
In typical wireless distribution system, co-channel interference mainly limits the operating SINR on the link
In WiFi based systems, there is an additional blocking effect
    Packet detection is based on Preamble with STF and CE training sequences which are common to all links in the system
    Segregation of desired and undesired link signals is based on MAC address
Receiver locks onto an early weak interference packet when △T ∈ [1.2usec-𝛼, 2.45us]
    Desired packet may be blocked from being detected
    Exact value of 𝛼 depends on CRS thresholds, and details of AGC and packet detection implementation
    Unduly limits the spectral efficiency in fixed wireless distribution system

## Slide 11: Golay Code Index Selection
Define subset of 3-4 Golay Code Indexes (GIs) with best cross-correlation properties to be assigned to individual links upon association
Default Golay sequence for “onboarding” mmW Distribution NW nodes can be predefined in spec, or receiver can sweep through predefined set (blind detection)
Table 1: Peak suppression as function of GI pair [dB]: Third order set
Table 2: Peak suppression as function of GI pair [dB]: Forth order set
Example: One radio sector on each side of square, Red arrow denotes early weak interference

## Slide 12: Blocking Effect Field Scenario
11-8
11-9
10-5

## Slide 13: Golay Code Index Selection: Field data
CSR default
CSR optimized
MSC9 50% duty cycle (TDD) on both links transmitting simultaneously , max Tput per link 1.05Gbs

## Slide 14: Summary of Proposal
Adopt initial set of changes to Draft 1.0 of 802.11ay to support requirements for the new mmW Distribution Network use cases
Enable centralized co-channel interference management and mitigation
  Ability to latch state of TSF counter to external PPS (e.g. over GPIO) in distribution nodes to enable network wide timing synchronization
    Maximum 1usec timing drift over 100msec. Recommended implementation, does not require spec change.
  Implicit Block-ACK delayed to next SP allocated in opposite direction
    The rest of MSDU to AMPDU data path unmodified
Alleviate the blocking problem
  Golay code index selection per link
Assure co-existence with other use cases in the spec
  Indication in the Beacon Transmission to indicate subsequent DTI pertains to the mmW Scheduled Access

## Slide 15: References
[1] IEEE P802.11ayTM/D0.3, March 2017
[2] IEEE 802.11-17/1019r0 “mmWave Mesh Network Usage Model”