## Slide 1: SU Sounding Measurement Exchange and Feedback
Date: 2017-09-01
Authors:

## Slide 2: VHT Sounding Protocol
Protocol is completely unscheduled
  When medium is idle, initiator can send NDP-A followed by NDP
  If available, responder replies with NDP within SIFS
  Followed by LMR within SIFS, which contains
    Time stamps t2/t3 of this exchange, or
    Time stamps t2/t3 of a previous exchange, or
    No time stamps, if none are ready
SIFS
NDP-A
Initiator
NDP
Responder
SIFS
NDP
SIFS
LMR
SIFS
SIFS
Initiator
Responder

## Slide 3: Processing Time
Initiator needs feedback from responder
  T2 time-of-arrival (ToA) of NDP send by initiator
  T3 time-of-departure (ToD) of NDP send by responder
  The time available to determine t2 is about 70-80 µs
    2·SIFS = 32 µs
    VHT NDP = 40-52 µs (1-4 LTF)
SIFS
NDP-A
Initiator
NDP
Responder
SIFS
NDP
SIFS
LMR
SIFS
SIFS
Initiator
Responder
Processing Time

## Slide 4: Processing Time (cont.)
To determine an accurate ToA requires FFT processing
Implementations can be in
  Hardware (delay on order of 10s of µs)
  Firmware/software (delay on order of ms)
Processing delay can depend on
  Bandwidth
  Number or receive antennas
  Number of LTF received
  Current load of other processing (firmware/software)

## Slide 5: Immediate and Delayed Feedback
Sounding
Sequence 1
Time [ms]
Sounding
Sequence 2
LMR 1
LMR 2
Immediate Feedback
Sounding
Sequence 1
Time [ms]
Sounding
Sequence 2
Empty LMR
LMR 1
Delayed Feedback
Min Processing Time

## Slide 6: Delayed Feedback
FTM Setup/Negotiation
  Responders declares MinToaReady
    Tells the initiator when to expect measurement results availability
    After this interval the initiator can expect the time stamps t2/t3 to be included in the next LMR
  Responder also declares MaxToaAvailable
    Tells the initiator how long the measurement results t2/t3 of a sounding sequence instance will be stored
    If no subsequent sounding sequence is exchanged for a duration of MaxToaAvailable past the measurement, responder may discarded t2/t3
Sounding
Time [ms]
LMR Availability
MinToaReady
MaxToaAvailable

## Slide 7: Straw Poll 1
For SU operation the following behavior bounds the protocol development:
  Only LMR feedback calculation (TOA) and then delivery may require a scheduling mechanism.
  We agree that the SU case does not require a reoccurring availability window mechanism.
  Yes: No: Abstain:

## Slide 8: Motion
Move to:
Adopt the following text to spec framework document,
instruct the SFD editor to include it in the TGaz SFD under the sub-section 3.2 and grant the editorial license to editor.
“For SU operation the following behavior bounds the protocol development:
  Only LMR feedback calculation (TOA) and then delivery may require a scheduling mechanism.
  We agree that the SU case does not require a reoccurring availability window mechanism.”
Moved:
Seconded:
Result:

## Slide 9: Straw Poll 2
Should the SU protocol supports immediate and delayed feedback.
  Report format (e.g. TOA, CSI) is TBD.
  Yes: No: Abstain:

## Slide 10: Motion
We agree that the SU ranging protocol will support both immediate and delayed reporting.
Note:
The report formats (e.g. TOA, CSI) to be defined separately.
Moved:
Seconded:
Result:

## Slide 11: Straw Poll 3
Should the single SU measurement and measurement report sequence be (as described on slide 2):
  NDPA (UL) <-SIFS-> NDP (UL) <-SIFS-> NDP (DL) <-SIFS-> LMR (DL)
  Where for immediate feedback the LMR is of this round and for delayed the LMR is the feedback from previous round.
  Yes: No: Abstain:

## Slide 12: Motion
Move to:
Adopt the following text to spec framework document, instruct the SFD editor to include it in the TGaz SFD under the sub-section 3.2 and grant the editorial license to editor.
The single SU measurement and measurement report sequence shall be:
NDPA (UL) <-SIFS-> NDP (UL) <-SIFS-> NDP (DL) <-SIFS-> LMR (DL)
Where for immediate feedback the LMR is of this round and for delayed the LMR is the feedback from previous round.
Moved:
Seconded:
Result:

## Slide 13: Straw Poll 4
For delayed SU normal operation:
  The iSTA shall not initiate another measurement sequence earlier than MinToaReady.
  If the iSTA initiates a following measurement sequence later than MaxToaAvailable, then the results may not be available (flushed)
  Yes: No: Abstain:

## Slide 14: Motion
Move to:
Adopt the following text to spec framework document, instruct the SFD editor to include it in the TGaz SFD under the sub-section 3.2 and grant the editorial license to editor.
The iSTA shall not initiate another measurement sequence earlier than MinToaReady.
If the iSTA initiates a following measurement sequence later than MaxToaAvailable, then the results may not be available (flushed)
Moved:
Seconded:
Result:
Sounding
Time [ms]
LMR Availability
MinToaReady
MaxToaAvailable