## Slide 1: OOK Waveform Coding Scheme for Frequency Domain Multiplexing
Date: 2017-09-11
Authors:

## Slide 2: Introduction
During the last TGba F2F meeting, we had the following SP and result
  Do you agree that frequency domain multiplexing transmission of multiple WUSs should be one of 11ba system capabilities?
  Y:15, N:2, A: 6
Many use cases in the current 11ba usage models, such as Smart Home, Warehouse and Sensor Networks, can benefit from frequency domain multiplexing (FDM) capability
In this contribution, we compare transmitter structures that enable FDM using two different OOK waveform coding schemes, i.e., sequence-based and mask+filtering-based, and provide some simulation results based on 11n/ac numerologies
  Sequence-based scheme offers very simple Tx structure – the same as transmitting 11n/ac data
  Sequence-based scheme can offer slightly better performance

## Slide 3: Recap: Sequence-based WFC OOK Symbols
In [1, 2], we proposed to generate the WFC OOK symbol(s) by using a set of carefully designed sequences
  Generated from DFT of time domain symbols (e.g. ZC sequences) with proper time domain allocation to represent logic 0 and 1
This method has three main benefits:
  Localizes energy in the spectrum to increase coverage range of 11ba
  Enables envelope detector based WURs and correlator-based WURs
  Easily supports frequency domain multiplexing
At the transmitter, these sequences can be kept in a look-up table (LUT), which maps the logic 0 and 1 to specific frequency domain sequences
Since the sequences are designed to shape the time domain waveform, they removes the need for masking operation and do not need additional filtering operation

## Slide 4: Comparison of Tx Structures for Sequence-based and Mask-based Schemes (1/2)
Single user and single channel transmission
IDFT
(64)
Mapping
Sequence
Masking for Logic 1
Masking for Logic 0
+GI
Filtering
IDFT
(64)
Mapping
Sequence1
+GI
Data (0 or 1)
Sequence2
Data (0 or 1)
Sequence-based Scheme
Mask-based Scheme
time
IDFT output
Amplitude
Logic 0
Logic 1

## Slide 5: Comparison of Tx Structures for Sequence-based and Mask-based Schemes (2/2)
Multi-user and/or multi-channel transmission
Masking for Logic 1
Masking for Logic 0
+GI
Filtering
IDFT
(64)
Mapping
Sequence1
+GI
Sequence2
Sequence1
Sequence2
Sequence1
Sequence2
IDFT
(64)
Mapping
Sequence
IDFT
(64)
IDFT
(64)
Mapping
Mapping
0
0
0
0
Masking for Logic 1
Masking for Logic 0
+GI
Filtering
Masking for Logic 1
Masking for Logic 0
+GI
Filtering
Mask-based Scheme
Sequence-based Scheme
f
20 MHz

## Slide 6: Simulation Assumptions
Sequence-based OOK:
  The base sequence is a ZC-sequence of length of 5 (The OOK sequences are generated by applying DFT of size of 12, see next page for the mapping). The OOK symbol + blank GI duration is 4.
  Frequency domain shaping is applied. The length of windowing is 4 samples on each edge.
Mask-based OOK:
  A fixed sequence, e.g., [1 -1 1 1 1 1 0 1 -1 -1 1 1 -1] is first mapped around DC subcarrier. Time domain signal is generated via an IDFT operation of size of 64. Before CP is prepended to OFDM symbol, the OFDM symbols is masked to generate Manchester coded OOK symbols. The OOK symbol + blank GI duration is 4.
  RC windowing is applied to the “on” duration of OOK symbol to reduce OOB emission (The length of windowing is 4 samples on each edge)
  The BW for WUS is 4 MHz (Sampling rate Fs = 20 MHz). Channel is AWGN.
2nd order Butterworth filter ( = 2.5 MHz, Fs = 20 MHz) is used at the 11ba receiver
Two scenarios are considered:
  11ba standalone, 11ba multiplexing (allocations are provided in the appendix).
WUR compares the energy on first half and second half of the OOK symbols to detect the bit.

## Slide 7: DFT Input Mapping for OOK Symbol with Manchester Coding
DFT Input Index
Symbol = 0
1
2
7
Symbol = 1
0
S
6
0
0
8
12
1
2
7
S
0
6
0
0
8
12
S is a sequence with the length of 5
0.0437 + 0.0106i 0.0437 + 0.0106i
0.1116 + 0.0765i -0.1116 - 0.0765i
0.3611 - 0.2624i 0.3611 - 0.2624i
-0.2923 - 0.2003i 0.2923 + 0.2003i
0.4575 + 0.1108i 0.4575 + 0.1108i
-0.1793 - 0.8567i 0.1793 + 0.8567i
-0.6460 + 0.4693i -0.6460 + 0.4693i
0.6817 + 0.1050i -0.6817 - 0.1050i
-0.1747 - 0.7594i -0.1747 - 0.7594i
-0.6817 - 0.1050i 0.6817 + 0.1050i
-0.6460 + 0.4693i -0.6460 + 0.4693i
0.1793 + 0.8567i -0.1793 - 0.8567i
0.4138 + 0.1002i 0.4138 + 0.1002i
0.2115 + 0.1450i -0.2115 - 0.1450i
0.1906 - 0.1385i 0.1906 - 0.1385i
-0.0309 - 0.0212i 0.0309 + 0.0212i
Logic 0:
Logic 1:
Frequency
S: ZC sequence
DFT+windowing
Windowing coefficients: [0.0955 0.3455 0.6545 0.9045]
Data-to-Sequence LUT
0.0000 + 0.0000i 0.0000 + 0.0000i
1.0000 + 0.0000i 0.0000 + 0.0000i
0.3090 - 0.9511i 0.0000 + 0.0000i
-0.8090 + 0.5878i 0.0000 + 0.0000i
0.3090 - 0.9511i 0.0000 + 0.0000i
1.0000 + 0.0000i 0.0000 + 0.0000i
0.0000 + 0.0000i 0.0000 + 0.0000i
0.0000 + 0.0000i 1.0000 + 0.0000i
0.0000 + 0.0000i 0.3090 - 0.9511i
0.0000 + 0.0000i -0.8090 + 0.5878i
0.0000 + 0.0000i 0.3090 - 0.9511i
0.0000 + 0.0000i 1.0000 + 0.0000i
Logic 0:
Logic 1:
DFT-input (Time):
S
S

## Slide 8: Temporal Characteristics (Sequence-based OOK)
GI
OOK
GI
OOK
GI
OOK
GI
OOK
GI
OOK
GI
OOK
GI
OOK
GI
OOK
GI
OOK
GI
OOK
1
1
1
1
1
1
1
0
0
0
Data

## Slide 9: Spectral Characteristics
While windowing helps to improve the spectral characteristics of mask-based OOK symbols, the sequence-based OOK symbols are confined without any extra operation
Standalone
Frequency multiplexing

## Slide 10: BER Performance
Since sequence-based OOK symbols yield better accumulation after WUR filter, it yields slightly superior performance as compared to mask-based OOK symbols in frequency multiplexing scenarios
Standalone
Frequency Multiplexing

## Slide 11: Conclusions
In this contribution we compared the performance and the transmitter structure needed to support frequency domain multiplexing for sequence-based and mask-based waveform coding schemes
The transmitter structure for sequence-based waveform coding scheme is significantly simpler than that for mask-based waveform coding scheme
  For sequence-based waveform coding scheme, there is no need to change the existing 11n/ac hardware design; apply sequences as 11n/ac data based on a LUT is sufficient
Using 11n/ac numerology, the sequence based scheme can achieve slightly better performance than the mask-based scheme with windowing in FDM case

## Slide 12: References
[1] Alphan Sahin, et. al., “On the Coexistence of 802.11ax and 802.11ba Signals,” IEEE 802.11-17/0659r3
[2] Alphan Sahin, et. al., “Performance Evaluation of OOK Waveform Coding Schemes with Impairments,” IEEE 802.11-17/1037r2

## Slide 13: SP
Do you agree that sequenced-based OOK waveform coding scheme should be considered as one of the OOK waveform coding schemes for 11ba?
Y:
N:
A:

## Slide 14: Appendix

## Slide 15: Appendix - Allocation
Frequency
-8
7
18
27
-28
-17
3.75 MHz (12 tones)
-6
5
Frequency domain windowing
(Implementation dependent)