## Slide 1: Discussion on Preamble Sequences For Indication of the WUR Rates
Date: 2017-11-06
Authors:

## Slide 2: Introduction
In this presentation, options of WUR Preamble to support different data rates are discussed
Considering the discussions in [1-4] and the results of straw polls during the IEEE meeting, the following two cases are discussed to provide two different preamble durations for the rate indication
  Use of one and two 15-bit PN and/or complement of the 15-bit PN sequences
  Shorter OOK symbol duration of 2usec (option 5 in backup slides)

## Slide 3: Proposal 1: Use of 4usec Bit Duration Sequence S
Use S = 15-bit Maximal Length PN sequence for higher rate, and signal the lower rate by including two repetitions of S.
  The bit 0 is added to make it 16 bits, which gives equal number of ones and zeroes
Legacy + WUR Mark
Wake-up preamble
MAC header
Payload
FCS
15-bit PN seq.
15-bit PN seq.
0
0
24 µs
128 µs
15-bit PN seq.
0
64 µs
Low Rate
Higher Rate

## Slide 4: Rate Detection at The Receiver
Earlier proposal [1-2]
  Correlate with 32-bit (128 us) sequence (see backup slides)
    Low rate transmission: 3 peaks, with strong center peak
    High rate transmission: 2 peaks, with similar strength
  The Discussion with other members during the September session and offline indicated that finding 3 peaks and identifying the strongest one appear to be complex to them. Therefore:
Current proposal
  Use 16-bit (64 us) correlator
    Low rate transmission: 2 peaks, separated by PN seq length
    High rate transmission: single peak
  Advantages
      Lower complexity compared to single long (128 us) correlator by exploiting the structure
      Lower overhead for higher rate

## Slide 5: Detection Method for the Common Sequence Case: lower Rate
Correlating with the known sequence results in two peaks:
The two peaks roughly separated by PN seq length
15-bit PN seq.
0
no Peak
15-bit PN seq.
15-bit PN seq.
0
0
Received samples prior to the preamble
Other received samples
15-bit PN seq.
15-bit PN seq.
0
0
Received samples prior to the preamble
Other received samples
15-bit PN seq.
15-bit PN seq.
0
0
Received samples prior to the preamble
Other received samples
15-bit PN seq.
15-bit PN seq.
0
0
Received samples prior to the preamble
Other received samples
2nd Peak
1st Peak
no peak

## Slide 6: Detection Method for the Common Sequence Case: Higher Rate
Correlating with the known sequence results in one peaks:
15-bit PN seq.
0
15-bit PN seq.
0
Received samples prior to the preamble
Other received samples
15-bit PN seq.
0
Received samples prior to the preamble
Other received samples
No Peak
1st Peak
no peak
15-bit PN seq.
0
Received samples prior to the preamble
Other received samples

## Slide 7: Proposal 2: 4usec bit-duration S and Its Complement
Use sequence S = 15-bit Maximal Length PN sequence.
Signal higher rate using ; Signal the lower rate by including concatenating S and S
    is the bit-wise logical complement of
Legacy + WUR Mark
Wake-up preamble
MAC header
Payload
FCS
S
S
24 µs
128 µs
S Complement
64 µs
Low Rate
Higher Rate

## Slide 8: Proposal 2 – (S, S) for Low Rate and for High rate: Rate detection at the receiver
Correlate with short sequence
    Low rate transmission: Two positive peaks, separated by PN seq length
    High rate transmission: one negative peak
Advantages
    Easy to differentiate the two rates compared to proposal 1
    Similar to proposal 1: Lower complexity compared to single long (128 us) correlator
    Similar to proposal 1: Lower overhead for higher rate

## Slide 9: Simulation parameters (Transmitter)
  Low rate transmissions
    Preamble (S, S)
      S: 15-bit PN seq and added 0
      Bit duration: 4 us
      4 MHz, 4 us OOK pulse
    Data
      MC-[1 0 1 0], with bit duration: 4 us
      4 MHz, 4 us OOK pulse
  High rate transmissions
    Preamble
      Two cases: S and
      Bit duration: 4 us
      4 MHz, 4 us OOK pulse
    Data
      MC-[1 0], with Bit duration: 2 us
      4 MHz, 2 us OOK pulse generated using 32 pt FFT in 20 MHz [5]
20MHz Bandwidth (legacy)
Wake-up preamble
MAC header
Payload
FCS
100 symbols of silence

## Slide 10: Simulation parameters (Receiver)
The known S sequence is cross correlated (normalized output) with a sliding window of the received samples
  Low rate: Two positive peaks, spaced apart by PN seq length
  High rate: Single peak (positive or negative)
4 MHz LPF (IIR) – generated using MATLAB
  Numerator order=1, denominator order=1
  Passband freq. = 2MHz, Stopband freq.=6MHz, Sampling freq. =160MHz
WUR with in-phase only (single rx chain)
Channels: AWGN and Channel D
No phase noise
2.4 GHz band operation
25 MHz away ACI: 16 dB higher than the received signal
SNR is measured at 20 MHz bandwidth
Performance quantified with respect to Genie approaches

## Slide 11: Genie Approaches
Genie with ideal rate and timing
  Genie knows incoming rate and the precise Timing
  Best possible performance
  Non-realistic, but acts like a baseline
Genie with ideal rate
  Genie only knows if packet is low/high rate, but not the timing
  Timing acquisition
    Low rate transmission: Considered several approaches and picked the best
      Correlating with 128 us sequence and comparing strongest peak to threshold
      Correlating with 128 us sequence and looking for three peaks (strong center peak)
      Later approach gave better PER performance
    High rate transmission
      Correlating with 64 us sequence and comparing strongest peak to threshold was good

## Slide 12: Miss Classification of Low Rate (S, S) as High Rate (S) (Proposal 1)
16 bit correlator better than 32 bit correlator, as expected

## Slide 13: PER- Low Rate (S, S) Transmission (Proposal 1)
1.5 dB performance gap compared to genie Rate case
2 dB performance gap compared to genie Rate and Timing

## Slide 14: PER- High Rate S Transmission (Proposal 1)
64 us correlator is as good as the genie rate case (No performance gap)
1-2 dB dB performance gap compared to genie Rate and Timing

## Slide 15: Conclusions of proposal 1: S and (S, S)
Repeated PN sequence with 16-bit (64 us) correlator is suited to differentiate two rates
  1 dB Performance gap compared to genie rate case
    No performance gap for high rate transmissions
    Performance gap of 1 dB for low rate transmissions
  2 dB Performance gap compared to genie rate and timing
    Performance gap of 2 dB for high rate transmissions
    Performance gap of 1 dB for low rate transmissions

## Slide 16: PER- Low Rate (S, S) Transmission (Proposal 2)
Performance relative to genie Rate and Timing
  0.3 dB loss in AWGN and 0.6 dB loss in Channel D
Misclassification error is very small

## Slide 17: PER- High Rate Transmission (S, S) is used for Lower Rate (Proposal 2)
Performance relative to genie Rate and Timing
  1.3 dB loss in AWGN and 2 dB loss in Channel D
Misclassification error is very small

## Slide 18: Conclusions of proposal 2: and (S, S)
  Use of complement sequence reduces misclassification rate
  Small misclassification errors
  0.3-0.6 dB loss compared to ideal timing and rate (low rate)
  1.3-2 dB loss compared to ideal timing and rate (high rate)

## Slide 19: Option 3: Single 31-bit sequence
Legacy+WUR mark
Wake-up preamble
MAC header
Payload
FCS
31-bit PN seq.
0
24 µs
128 µs
31-bit PN seq Complement.
1
128 µs
Low Rate: S
Higher Rate:

## Slide 20: PER- Low Rate 31-bit PN Sequence Transmission
Performance relative to genie Rate and Timing
  0.4 dB loss in AWGN and 0.8 dB loss in Channel D

## Slide 21: PER- High Rate: Complement of 31-bit of Low Rate
Performance relative to genie Rate and Timing
  0.6 dB loss in AWGN and 1.3 dB loss in Channel D

## Slide 22: Option 4: Single 15-bit sequence
Legacy+WUR mark
Wake-up preamble
MAC header
Payload
FCS
15-bit PN seq.
0
24 µs
64 µs
15-bit PN seq Complement.
1
64 µs
Low Rate: S
Higher Rate:

## Slide 23: PER- Low Rate 15-bit PN Sequence Transmission
Performance relative to genie Rate and Timing
  1 dB loss in AWGN and 1.2 dB loss in Channel D

## Slide 24: PER- High Rate: Complement of 15-bit of Low Rate
Performance relative to genie Rate and Timing
  2 dB loss in AWGN and 4 dB loss in Channel D
  64 us preamble not sufficient for high rate scenario

## Slide 25: Conclusions
  Use of a structured preamble of (S, S) for low rate and S or for high rate provides
    Lower hardware complexity
    Lower overhead at higher rate
    Very good misclassification rate
    Very good PER performance

## Slide 26: References
[1] 17/0997r0 Preamble Options, IEEE 802.11 TGba, July 2017
[2] 17/1442r0 WUR Preamble Performance Study with Phase Noise and ACI, IEEE 802.11 TGba, September 2017
[3] 17/1355r1 WUR Preamble Evaluation, IEEE 802.11 TGba, September 2017
[4] 17/1345r5 11ba PHY Frame Format Proposal, IEEE 802.11 TGba, September 2017
[5] 17/1615r0 OOK waveform generation for high data rate, IEEE 802.11 TGba, November 2017

## Slide 27: Backup

## Slide 28: Detection Method for the Common Sequence Case: lower Rate
Correlating with the known 32-bit sequence results in three peaks:
15-bit PN seq.
15-bit PN seq.
0
0
3rd Peak
15-bit PN seq.
15-bit PN seq.
0
0
Received samples prior to the preamble
Other received samples
15-bit PN seq.
15-bit PN seq.
0
0
Received samples prior to the preamble
Other received samples
15-bit PN seq.
15-bit PN seq.
0
0
Received samples prior to the preamble
Other received samples
15-bit PN seq.
15-bit PN seq.
0
0
Received samples prior to the preamble
Other received samples
the 2nd larger Peak
1st Peak
no peak

## Slide 29: Detection Method for the Common Sequence Case: Higher Rate
Correlating with the known sequence results in three peaks:
15-bit PN seq.
15-bit PN seq.
0
0
15-bit PN seq.
0
Received samples prior to the preamble
Other received samples
15-bit PN seq.
0
Received samples prior to the preamble
Other received samples
15-bit PN seq.
0
Received samples prior to the preamble
Other received samples
2nd Peak (same size)
1st Peak
no peak
15-bit PN seq.
0
Received samples prior to the preamble
Other received samples
no peak

## Slide 30: Timing Error for Low Rate (S, S) Transmission– AWGN
Genie rate has better timing
Timing error less than 8 samples (2 us), > 99% of times
SNR
ACI

## Slide 31: Timing Error for Low Rate (S, S) Transmission– Channel D
Genie rate has better timing
Timing error less than 8 samples (2 us), > 98% of times
SNR
ACI

## Slide 32: Proposal 1: Timing Error for High Rate S – AWGN
Genie and 16-bit correlator has similar timing
Timing error less than 8 samples (2 us), > 98% of times

## Slide 33: Proposal 1: Timing Error for High Rate S – Channel D
Genie and 16-bit correlator has similar timing
Timing error less than 8 samples (2 us), > 98% of times

## Slide 34: Option 5: Preamble Sequence with Shorter OOK Symbol Duration
Use the same sequence, signal the lower rate by including two repetitions
Legacy
Wake-up preamble
MAC header
Payload
FCS
15-bit PN seq.
15-bit PN seq.
0
0
20 µs
15-bit PN seq.
0
Low Rate: 128 usec Preamble
4 us
4 us
15-bit PN seq.
0
2 us
High Rate: 64 usec Preamble
2 us

## Slide 35: Rate and Timing estimate (Option 5)
Two correlators matched to two preamble sequences
  32 bit (128 us) correlator
  32 bit (64 us) correlator
Rate estimation
  Find the maximum correlation peak at the output of two correlators
  Whichever is higher, we declare it as corresponding rate
Timing estimation
  If max correlation > threshold
    Sync found
    Timing = idx corresponding to the max correlation

## Slide 36: Simulation parameters (Option 5)
Transmitter
  Low rate transmissions
    Preamble
      Repetition of 15-bit PN seq
      Bit duration: 4 us
      Standard 4 MHz, 4 us OOK pulse
    Data
      Manchester [1 0 1 0], Bit duration: 4 us
      Standard 4 MHz, 4 us OOK pulse
  High rate transmissions
    Preamble
      Repetition of 15-bit PN seq
      Bit duration: 2 us
      4 MHz, 2 us OOK pulse generated using 32 pt FFT in 20 MHz
    Data
      Manchester [1 0], Bit duration: 2 us
      4 MHz, 2 us OOK pulse generated using 32 pt FFT in 20 MHz
Receiver
  First order analog 4 MHz LPF
  ACI (pre-filter): 16 dB at 25 MHz spacing
  SNR measured at 20 MHz Bandwidth

## Slide 37: PER (Low rate transmissions)
3-4 dB performance gap from the genie rate and timing
  2 us bit duration for preamble did not work well