## Slide 1: Discussion on OOK Pulse Design for Higher Rate
Date: 2017-11-06
Authors:

## Slide 2: WUR packet structure
Legacy+WUR Mark
Wake-up preamble
MAC header
Payload
FCS
Data
Data
  Low rate (62.5 Kbps) –Manchester code
    ‘1’ – 4us on, 4us off, 4us on, 4us off
    ‘0’ – 4us off, 4us on, 4us off, 4us on
    Standard 4 us OOK pulse in the on period (4 MHz BW)
  High rate (250 Kbps) – Manchester code
    ‘1’ – 2us on, 2us off
    ‘0’ – 2us off, 2us on
    Need to design shorter (2us) OOK pulse
24us

## Slide 3: 2us OOK Pulse Design Options: Time-Masking
Time-Masking approach
  Applying time-mask to 4us OOK pulse as suggested in [1-2]
    Use either first or second half of the 4us pulse
    Issues:
      Distortion in the spectrum of the pulse
        Spillage beyond the 4 MHz bandwidth
      Different error rates for symb ‘0’ and ‘1’
        Different pulse shapes during the ON period
Information “1”
0us 2.0us 4us
Information “0”
0us 2.0us 4us

## Slide 4: 2us OOK pulse design options: FFT based
FFT based approach
  Increase the subcarrier spacing to 625 KHz
    32 pt. FFT in 20 MHz Bandwidth
    WUR pulse occupying the center 7 subcarriers (including DC)
    Can choose subcarrier weights to be subset of the 13 L-STF coefficients
      Example: S=1.436*[-1-1i -1-1i 1+1i 0 -1-1i -1-1i 1+1i]
      They can be optimized further

## Slide 5: Simulation parameters (Transmitter)
  High rate transmissions
    Preamble
      Repetition of 15-bit PN seq
        Just for study (to be consistent with our earlier low rate results)
        Preamble design for high rate under investigation
      Bit duration: 4 us
      Standard 4 MHz, 4 us OOK pulse (0.8 us CP)
        13 L-STF coefficients
    Data
      Manchester code, Bit duration: 2 us
      4 MHz, 2 us OOK pulse
        Time masking Vs FFT approach
Legacy+WUR mark
Wake-up preamble
MAC header
Payload
FCS
24 µs

## Slide 6: Simulation parameters (Receiver)
The known 64 us preamble sequence is cross correlated (normalized output) with a sliding window of the received samples and detect two peaks
4 MHz LPF (IIR) – generated using MATLAB
  Numerator order=1, denominator order=1
  Passband freq. = 2MHz, Stopband freq.=6MHz, Sampling freq. =160MHz
WUR with in-phase only (single rx chain)
Channels: AWGN and Channel D
No phase noise
2.4 GHz band operation
25 MHz away ACI: 16 dB higher than the received signal
SNR is measured after the 4 MHz LPF and 4 MHz sampling

## Slide 7: Performance with timing acquisition
Smaller FFT approach gives better performance than time making approach
  2-3 dB performance gap

## Slide 8: Summary
Discussed two approaches for 2us OOK pulse generation
  Time making
  FFT approach with increased subcarrier spacing
With timing acquisition, FFT based approach performs better by 2-3 dB

## Slide 9: References
[1] Junghoon Suh, et.al., “Blank GI choices under Timing Errors,” IEEE 802.11-17/1390r1
[2] Junghoon Suh, et.al., “ Blank GI for the Waveform Coding ,” IEEE 802.11-17/0696r0

## Slide 10: Backup

## Slide 11: Timing Errors
Similar errors as in Low rate case

## Slide 12: WUR Pulse Shapes
Pulse generated from smaller FFT size
  Energy more concentrated at the center and less at the edges
    Relatively poor OOK decoding performance
    More robust to small timing errors