## Slide 1: WUR Dual SYNC Design and Performance
Date: 2017-11-06
Authors:

## Slide 2: Introduction
In IEEE September meeting, only two data rates (62.5kbps and 250kbps) are agreed for WUR [1].
In [2, 3, 4], the design of dual SYNC sequences are proposed, which can facilitate two rate signaling.
In [5], dual SYNC sequences of different duration are designed to achieve both reliability and efficiency.
In this contribution, we propose a new structured design of dual SYNC sequences with different duration, which facilitates low-complexity receiver design for carrier sensing/symbol timing.

## Slide 3: Recap: Dual WUR SYNC
WUR preamble can have two possible SYNC sequences associated with the two data rates
  If WUR Data is transmitted with 62.5kbps rate, SYNC1 will be used.
  If WUR Data is transmitted with 250kbps rate, SYNC2 will be used.
  Receiver needs to detect SYNC pattern in order to use correct data rate to decode the WUR Data portion.
LSTF
LLTF
LSIG
WUR SYNC1
WUR Data
BPSK
Symbol
LSTF
LLTF
LSIG
WUR SYNC2
WUR Data
BPSK
Symbol

## Slide 4: Long-short Dual SYNC
Dual SYNC with one longer and one shorter duration
  Longer SYNC1 is associated with the lower rate to achieve better reliability.
  Shorter SYNC2 is associated with the higher rate to achieve better efficiency.
    For example, WUR Data has 48bits payload, if SYNC2 for high data rate reduces from 128us to 64us, the packet duration reduces by 20%.
    This reduction can be translated to 20% receiver power consumption reduction and traffic time reduction
In [5], we proposed the design of long-short Dual SYNC based on two M-sequences
  Good autocorrelation and cross-correlations are achieved
  Two separate correlators are needed at the receiver for CS/synchronization.
  Some concern was raised for high receiver complexity.

## Slide 5: Long-short Dual SYNC Design Criteria
Simple receiver processing for carrier sensing and timing synchronization
  For example, usage of only one correlator
Reliable performance
  lower false alarm rate, miss detection rate, and false sync detection between the two data rates
Higher efficiency for 250Kbps without sacrificing complexity and performance
  Use shorter SYNC duration

## Slide 6: Proposed Long-short Dual SYNC Design
Dual sequence design method
  Design one base sequence Z of length N (sequence of 1s and 0s).
    Z can be designed from an M-sequence of length N-1.
    Add one extra 1 or 0 similar to [5] to achieve zero DC receiver correlator template and good correlation properties.
  Construct SYNC1 and SYNC2 based on Z and its complementary 1-Z:
    SYNC1=[Z Z]
    SYNC2=1-Z
  The design can accommodate any base sequence design of Z and the sync ON waveform duration.
1-Z
Z
Z

## Slide 7: Basic Receiver for Long-short SYNC
The receiver will correlate with template (2Z-1), and the correlator output will have:
  two positive peaks if SYNC1 is transmitted, and
  one negative peak if SYNC2 is transmitted.
Carrier sensing
  Claim packet detection if the absolute correlator output pass certain threshold
  SYNC type (i.e data rate) can detected by the sign of the output at the point of carrier sensed.
Timing
  Determine the timing by the peak of the correlator output after carrier sensing within certain window
For low data rate, both carrier sensing and timing can be enhanced by using combined peak output.

## Slide 8: Example of Z Sequence
Z of length N= 32
  Z = [0 0 0 1 0 1 1 0 1 0 1 0 0 0 1 1 1 0 1 0 1 1 1 1 0 0 1 0 0 1 1 0];
  Correlation output based on 2us sync ON waveform duration
  Total duration 64us for high rate and 128us for low data rate

## Slide 9: Simulation Settings
WUR Packet
  WUR Data signal uses center ~4MHz in 20MHz bandwidth
  Payload: 48 bits, Manchester Coding
  2ms noise appended before the WUR packet
SNR defined on 20MHz noise
CFO = 20ppm, fc = 2.4GHz, No phase noise
Receiver
  Realistic AGC: entire packet is normalized to certain gain target
    Noise portion normalized based on the noise power
    WUR portion normalized by 20MHz preamble power
  5th order 4MHz butterworth filter with 2.5MHz cutoff frequency
  8MHz sampling rate with in-phase path
LSTF
LLTF
LSIG
WUR SYNC
WUR Data
BPSK
Symbol
2ms noise

## Slide 10: False Alarm/Miss Detection: AWGN
  threshold ratio: CS detection threshold/correlation peak (noise-free, AWGN)
  Miss detection: No CS found
  False alarm: CS found within 2ms noise portion
  FalseSync: CS found in SYNC portion but SYNC type is detected in error

## Slide 11: Channel: AWGN
  Real timing is close to ideal timing/CS
  False sync detection is clean
  Miss detection rate is one order lower from PER

## Slide 12: Channel: DNLOS
  Real timing is close to ideal timing/CS
  False sync detection is ~0.1%

## Slide 13: Channel: UMi-NLos
  Real timing is close to ideal timing/CS
  False sync detection is below error floor, ~0.1%

## Slide 14: Summary
Long-short dual SYNC design is beneficial for two-rate WUR system with both reliability and efficiency
  High-rate packet can save ~20% packet duration
The proposed long-short SYNC design based on one base sequence and complementary sequence can facilitate simpler receiver design
False SYNC type detection rate is much lower than false detection and miss detection rate

## Slide 15: Straw Poll 1
Do you agree that 11ba preamble to have the following dual SYNC design?
  one SYNC with longer duration to signal 62.5kbps data rate, and
  one SYNC with shorter duration to signal 250kbps data rate.
  Y:
  N:
  A:

## Slide 16: Straw Poll 2
Do you agree that 11ba preamble to have the following design of long-short dual SYNC?
  Design a base sequence Z
  Longer SYNC1 is two repetition of Z
  Shorter SYNC2 is the complementary sequence 1-Z.
  Y:
  N:
  A:
1-Z
Z
Z

## Slide 17: Reference
[1] IEEE 802.11-17/1345r5, “PHY frame format discussions”
[2] IEEE 802.11-17/0679r2, “Preamble Design for WUR WLAN”
[3] IEEE 802.11-17/0997r0, “preamble-options”
[4] IEEE 802.11-17/0991r0, “preamble-design-and-simulations”
[5] IEEE 802.11-17/1343r0, “WUR preamble SYNC design and performance”