## Slide 1: MAC operation of WUR
Date: 2017-11-06
Authors:
Name | Affiliation | Address | Phone | Email
Suhwook Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | suhwook.kim@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Taewon Song |  |  |  | taewon.song@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
Even though our SFD has been almost done, some of basic MAC procedures are still unclear
  We will address and make clear these unclearness

## Slide 3: MAC overall procedure

## Slide 4: 1. Association
WUR capability information will be delivered between AP and STA during association procedure
  Supportability for WUR operation at AP side
  Supported transmission rate for Wake-up packet
  Supported operating class for WUR channel
  Mode transition delay
  Nonzero-length Frame Body support
  Etc...
We may need a new IE for WUR capability

## Slide 5: 2. WUR mode signaling (entry)
Two management frames (WUR mode request/response) will be defined for WUR mode signaling
WUR mode signaling incorporates WUR negotiation
After WUR mode signaling, a STA can enter into PM-WUR mode by existing signaling

## Slide 6: 2. WUR mode signaling (entry)
Parameters for WUR mode signaling
  WUR mode request
    Mode indication (Entry or Termination)
    Channel quality information
    Preferred duty cycle parameter (e.g. ON Duration, Period, etc...)
  WUR mode response
    Status code (accept or deny with reason)
    WUR ID Allocation (Individual, group)
    Duty cycle information
    WUR channel information
    TSF, WUR beacon information (Interval, TBTT)

## Slide 7: 3. Data reception in WUR mode
Detail operation can vary depending on which existing power saving feature was used
  If TWT is used, for example, response frame of wake-up packet may be transmitted in service period
  It may occur inefficient power consumption in some cases
  We may need to define detail operation for each case or define one unified operation regardless of existing power saving feature

## Slide 8: 3. Data reception in WUR mode
If we have an unified rule in WUR mode,
  inefficient power consumption can be mitigated
  latency can be minimized
  status mismatch problem can be solved
  we don’t have to adjust detail operation of each cases

## Slide 9: 4. WUR mode signaling (termination)
WUR mode response can be omitted in WUR mode signaling for termination
Once WUR mode is terminated, the STA can operate in existing PS mode or move to active mode

## Slide 10: Summary
In this submission, we reviewed MAC basic features and proposed detail operations
  WUR capability information element
  Two management frame for WUR mode signaling and negotiation
  Data reception method in WUR mode

## Slide 11: Straw poll 1
Do you agree to add following text in SFD?
  Define Information Element for WUR capability information
    Supportability for WUR operation at AP side
    Supported operating class for WUR channel
    PCR transition delay from doze state to awake state after receiving wake-up packet
    Nonzero-length Frame Body support
    Other information is TBD

## Slide 12: Straw poll 2
Do you support the following?
  Information of Enter WUR Mode Request and Enter WUR Mode Suspend Request
    Preferred duty cycle parameter (e.g. ON Duration, Period, etc...)

## Slide 13: Straw poll 3
Do you support the following?
  Information of Enter WUR Mode Response and Enter WUR Mode Suspend Response
    WUR ID information
      Individual ID
      Group ID (TBD)
    Duty cycle information
    WUR channel information
    TSF, WUR beacon information (Interval, TBTT)

## Slide 14: Straw poll 4
Do you support the following?
  Define an unified rule for WUR mode operation regardless of existing power saving features