## Slide 1: WUR 128 us Preamble Design
Date: 2017-11-06
Authors:

## Slide 2: Abstract
We evaluate three aspects in the preamble design:
Preamble information sequence
  Maximum length sequences [1]
  2xMLS [1, 2]
  Pseudo-random sequence [3]
Size of the active part of the preamble symbols
Symbol rate of the preamble
We fix the length of the preamble to be 128 us long.

## Slide 3: Simulation set-up
Evaluate synchronization word
No payload
Synchronization error means that T_sync is outside the interval |T_ideal – T_sync| < T_NZ/2
T_ideal is synchronization obtained by correlation with a noiseless signal

## Slide 4: Preamble information sequence
We compare the two sequences from [1] and random sequences as in [3]:
MLS:
  [0,1,0,0,0,0,1,0,1,0,1,1,1,0,1,1,0,0,0,1,1,1,1,1,0,0,1,1,0,1,0,0]
Pair of MLS
  [0,1,0,0,0,1,1,1,1,0,1,0,1,1,0,0,0,1,0,0,0,1,1,1,1,0,1,0,1,1,0,0]
A new pseudo-random sequence for each iteration

## Slide 5: Preamble information sequences Simulations
Performance similar
MLS can potentially provide some 0.8-1 dB additional synchronization gain

## Slide 6: Size of the active part
We have seen in [4] that by reducing the active part enables power boost of signal, which gives a performance gain.
Will this gain also be beneficial to the preamble design?
ON
OFF
“WFC”

## Slide 7: Size of active part Simulations
For all channel models, there is a gain of 1-2 dB going from N_active = 4us to N_active = 2us

## Slide 8: Symbol rate of preamble
Maintaining 128 us long preamble, we can change the symbol rate and symbol duration:
8 us long symbols, 16 bit preamble  128 us
4 us long symbols, 32 bit preamble  128 us
2 us long symbols, 64 bit preamble  128 us
Which is the best choice for synchronization?

## Slide 9: Symbol rate of preamble Simulations
Different designs are good for the different channel models

## Slide 10: Conclusions and final result
From this presentation, we see that reducing T_active improves sync performance
Short symbol duration for the synchronization word performs well

## Slide 11: References
[1] Steve Shellhammer, 11-17-1355-01-00ba-wur-preamble-evaluation
[2] Shahrnaz Azizi 11-17-0997-00-00ba-preamble-options
[3] Leif Wilhelmsson and Dennis Sundman 11-17-1018-02-00ba-some-results-on-synchronization-performance
[4] Leif Wilhelmsson
11-17/1673r0 “Partial OOK – Generalizing the Blank GI Idea,”