## Slide 1: Input to ITU-R submission
Date: 2017-12-11
Authors:

## Slide 2: Contents
Statement of Intent
Overview of IEEE 802.11
802.11 candidate technologies
  802.11ac, 802.11ax
Proposal Overview
Configuration Choice for the 5 test environments
IEEE 802 Submission Timeline
(Optional) IMT-2020 Requirements Analysis

## Slide 3: Statement of Intent
IEEE 802 intends to submit a (S)RIT for consideration as a IMT-2020 Technology

## Slide 4: IEEE 802.11 Introduction
IEEE 802.11 is a working group, responsible for writing Wireless Local Area Network (LAN) standards
802.11 operates under
  The “Sponsor”: IEEE LMSC “LAN / MAN Standards Committee” – aka “802”
  IEEE Computer Society
  IEEE-SA Standards Board
Work in 802.11 is divided into various activities
  Task groups – one per approved standard or amendment to be developed
  Study groups or topic interest groups – the precursor to a task group that investigates marketability, feasibility and determines initial requirements
  Various standing committee's responsible for ongoing work, such as “Architecture”

## Slide 5: IEEE 802.11 Scope
Wireless local area networks
Generally use unlicensed spectrum
  Exception for 802.11y: “lightly licensed”
  Exception for TV whitespace
Deployments: Broadband network access, public venue access, sensor networks, mesh networks, automotive.
Present in these devices: laptops, phones, tablets, network infrastructure, home appliances, consumer electronics, healthcare devices
Notes: What’s the scope of IEEE 802.11?

## Slide 6: IEEE 802.11 Revisions
802.11
-2003
802.11
-2012
11w
Management
Frame
Security
IEEE
Std
802.11
-1997
MAC
&
PHY
MAC
11k
RRM
11r
Fast Roam
11a
54 Mbps
5GHz
11b
11 Mbps
2.4GHz
11d
Intl roaming
11v
Network
Management
11s
Mesh
11u
WIEN
11y
Contention
Based
Protocol
11n
High
Throughput
(>100 Mbps)
11z
TDLS
11p
WAVE
802.11
-2016 (TBC)
802.11
-2007
11g
54 Mbps
2.4GHz
11e
QoS
11i
Security
11h
DFS & TPC
11j
JP bands
11f
Inter AP
11aa
Video Transport
11ae
QoS Mgt Frames
11ac -VHT
>1 Gbps @ 5GHz
11ad - VHT
>1 Gbps @ 60GHz
11af
TV Whitespace
Notes: doc.: IEEE 802.11-11/0483r0
May 2011
        Bruce Kraemer (Marvell)
Page 6

## Slide 7: IEEE 802.11 Standards Pipeline
802.11
-2016
MAC & PHY
Sponsor
Ballot
MAC
TIG/Study
groups
Published
Standard
WG
Letter Ballot
802.11ac
VHT 5GHz
TG without
Approved draft
Discussion Topics
Published
Amendment
802.11af
TVWS
802.11ai
FILS
WNG
802.11ae
QoS Mgt Frames
802.11ad
VHT 60 GHz
802.11aq
PAD
802.11aj
CMMW
802.11ak
GLK
802.11ax
HEW
802.11ay
NG60
802.11aa
Video Transport
802.11
-2012
7
802.11az
NGP
LRLP TIG
Long Range
Low Power
802.11ah
< 1Ghz
Notes: doc.: IEEE 802.11-11/0483r0
May 2011
        Bruce Kraemer (Marvell)
Page 7

## Slide 8: IEEE candidate technologies for IMT-2020: 802.11ac
The 802.11ac amendment was published in 2013
  Prevalent Wi-Fi technology today
Key features
  20, 40, 80 and 160 MHz channels
  Gigabit speeds
  Defines MIMO up to 8 streams
  Beamforming, Multi-user MIMO (up to 4 users)
Originally defined to operate in 5 GHz, but waveform could be used unchanged at other carrier frequencies
Deployed in residential, enterprise and operator markets

## Slide 9: IEEE candidate technologies for IMT-2020: 802.11ax
The 802.11ax is under development
  Draft 3.0 scheduled for May 2018
  Final publication by end 2019
Key features (in addition to 11ac)
  UL and DL OFDMA
  UL Multi-user MIMO
  Up to 8 MU-MIMO users
  New power saving modes for mobile devices (TWT)
  Midamble Training for enhance Doppler performance
Defined for both 2.4 GHz and 5 GHz operation, but waveform can be used unchanged at other frequencies

## Slide 10: Proposal Overview (1)

## Slide 11: Configuration for eMBB Indoor Hotspot
For the eMBB Usage Scenario, the Indoor Hotspot Test environment should be tested using Configuration B (30 GHz) for the IEEE 802 proposal
Additional Observations:
  Indoor hotspot is a typical deployment for 802.11ac and 802.11ax
  802.11 waveforms can be used at different carrier frequencies
    Products based on 802.11 waveforms in licensed bands are available today

## Slide 12: Configuration for eMBB Dense Urban
For the eMBB Usage Scenario, the Dense Urban Test environment should be tested using Configuration B (30 GHz) for the IEEE 802 proposal
Additional Observations:
  802.11ax was specifically developed to service dense deployment environments

## Slide 13: Configuration for eMBB Rural
For the eMBB Usage Scenario, the Rural test environment should be tested using Configuration B (4 GHz) and C (700 MHz) for the IEEE 802 proposal
Additional observations:
  Requirements could be met by 802.11ac/ax provided power levels are adjusted to the new bands

## Slide 14: Configuration for mMTC Urban Macro
For the mMTC Usage Scenario, the Urban Macro Test environment should be tested using Configuration B for the IEEE 802 proposal

## Slide 15: Configuration for URLLC Dense Urban
For the URLLC Usage Scenario, the Urban Macro Test environment should be tested using Configuration A (4 GHz) for the IEEE 802 proposal

## Slide 16: IMT-2020 Submission Timeline

## Slide 17: IMT-2020 Requirements (1)

## Slide 18: Appendix

## Slide 19: 802.11 Waveforms vs. 5G Waveforms