## Slide 1: WUR Wake Up Frame Format
Date: 2018-1-11
Authors:
Name | Company | Address | Phone | Email
Lei Huang | Panasonic Corporation |  |  | lei.huang@sg.panasonic.com
Rojan Chitrakar |  |  |  | 
Yoshio Urabe |  |  |  | 

## Slide 2
Background: WUR Wake Up Frame Format
 | Frame Control | Address | TD Control
bits | 8 | 12 | 12
 | Type (1) | Length/Misc | Reserved
Bits: | 3~4 | 3~4 | rest
MAC Header | Frame Body | FCS
WID is provided by the AP and identifies one WUR STA in the BSS of the AP
GID is provided by the AP and identifies one or more WUR STAs in the BSS of the AP
TXID is decided by the AP, e.g., Partial BSSID or BSS Color
The FCS additionally embeds BSSID information. It is not applicable for pre-association WUR frames
Address field | WUR frame
WID | Unicast wake up
Group ID | Multicast wake up
TXID | Beacon or broadcast wake up
OUI1 | Vendor specific

## Slide 3
  Unicast, multicast and broadcast WUR Wake Up frames have the same Type field.
  The challenge is how to differentiate unicast, multicast and broadcast WUR Wake Up frames.
Problem Statement

## Slide 4
Like unicast and multicast WUR Wake Up frames, broadcast WUR Wake Up frame is NOT a pre-association WUR frame and thus its FCS field embeds BSSID information, which identifies the AP transmitting the broadcast WUR Wake Up frame.
The TXID in the Address field is unnecessary for broadcast WUR Wake Up frame.
Discussion

## Slide 5
The Address field contains CGID for multicast WUR Wake Up frame or BID (Broadcast ID) for Broadcast WUR Wake Up frame.
  CGID is converted from its corresponding GID which is used in Group ID related management frames.
CGID and BID take unused values of WID. For example,
  The valid range of WID is 0x800-0xFFF.
  BID takes a specific value (e.g., 0x000).
  CGID has a value range of 0x400-0x4FF.
  Note 1: the MSB of the Address field indicates whether the WUR Wake Up frame is unicast.
  Note 2: the GID used in Group ID related management frames is 8 bits.
  Merit: it is easy for a WURx to identify different types of WUR Wake Up frames.
Proposal
Example addressing space for the Address field
BID
WID
CGID
0x000
0x800-0xFFF
Reserved
0x400-0x4FF
Reserved

## Slide 6
 | Frame Control | Address | TD Control
bits | 8 | 12 | 12
 | Type (1) | Length/Misc | Reserved
Bits: | 3~4 | 3~4 | rest
MAC Header | Frame Body | FCS
Address field | WUR frame
WID | Unicast Wake Up
CGID | Multicast Wake Up
BID | Broadcast Wake Up
TXID | Beacon
OUI1 | Vendor specific
Proposal (cont.)

## Slide 7: Reference
IEEE 802.11-17/0575r8, Specification framework for TGba, December 2017
IEEE 802.11-17/0977r4, Address structure in unicast wake-up frame, July 2017

## Slide 8: SP
Do you support to modify R4.9.1.F of 11ba SFD as follows?
R4.9.1.F: The contents of the Address field are as defined below:
  where
  CGID is converted from its corresponding GID, which is GROUP ID provided by the AP and identifies one or more WUR STAs
  BID is the BROADCAST ID and identifies all WUR STAs in the BSS of the AP transmitting the broadcast WUR Wake Up frame
  Y/N/A:
Address field | WUR frame
WID | Unicast Wake Up
CGID | Multicast Wake Up
BID | Broadcast Wake Up
TXID | Beacon, Broadcast Wake Up
OUI1 | Vendor specific