## Slide 1: WUR Wake Up Frame Format
Date: 2018-1-15
Authors:
Name | Company | Address | Phone | Email
Lei Huang | Panasonic Corporation |  |  | lei.huang@sg.panasonic.com
Rojan Chitrakar |  |  |  | 
Yoshio Urabe |  |  |  | 

## Slide 2
Background: WUR Wake Up Frame Format
 | Frame Control | Address | TD Control
bits | 8 | 12 | 12
 | Type (1) | Length/Misc | Reserved
Bits: | 3~4 | 3~4 | rest
MAC Header | Frame Body | FCS
WID is provided by the AP and identifies one WUR STA in the BSS of the AP
GID is provided by the AP and identifies one or more WUR STAs in the BSS of the AP
TXID is decided by the AP
Address field | WUR frame
WID | Unicast wake up
Group ID | Multicast wake up
TXID | Beacon or broadcast wake up
OUI1 | Vendor specific

## Slide 3
  Unicast, multicast and broadcast WUR Wake Up frames have the same Type field.
  The challenge is how to differentiate unicast, multicast and broadcast WUR Wake Up frames.
Problem Statement

## Slide 4
The Address field contains CGID for multicast WUR Wake Up frame.
  CGID is converted from its corresponding GID, which is used in Group ID related management frames, in such a manner that CGID takes consecutive value range which is not used by WID and TXID.
  Example:
    TXID is 0x000.
    GID has a value range of 0x00-0xFF and CGID has a value range of 0x400-0x4FF.
Proposal
Example addressing space for the Address field
TXID
WID
CGID
0x000
0x800-0xFFF
WID
0x400-0x4FF
0x001-0x3FF

## Slide 5
 | Frame Control | Address | TD Control
bits | 8 | 12 | 12
 | Type (1) | Length/Misc | Reserved
Bits: | 3~4 | 3~4 | rest
MAC Header | Frame Body | FCS
Address field | WUR frame
WID | Unicast Wake Up
CGID | Multicast Wake Up
TXID | Beacon, Broadcast Wake Up
OUI1 | Vendor specific
Proposal (cont.)

## Slide 6: Reference
IEEE 802.11-17/0575r8, Specification framework for TGba, December 2017
IEEE 802.11-17/0977r4, Address structure in unicast wake-up frame, July 2017

## Slide 7: SP
Do you support to modify R4.9.1.F of 11ba SFD as follows?
R4.9.1.F: The contents of the Address field are as defined below:
  where
  CGID is converted from its corresponding GID, which is GROUP ID provided by the AP and identifies one or more WUR STAs, in such a manner that CGID takes consecutive value range which is not used by WID and TXID
  Y/N/A:
Address field | WUR frame
WID | Unicast Wake Up
CGID | Multicast Wake Up
TXID | Beacon, Broadcast Wake Up
OUI1 | Vendor specific