## Slide 1: WUR SYNC DESIGN
Date: 2018-01-12
Authors:

## Slide 2: Preamble structure to support two rates
Based on the discussions [1]-[5], the motion has been passed for the following preamble structure to support two different rates
  The exact bit sequence S and the bit duration is TBD
Legacy+WUR mark
Wake-up preamble
MAC header
Payload
FCS
S
24 µs
128 µs
64 µs
Low Rate
Higher Rate
S
S Complement

## Slide 3: Rate and timing detection the receiver
Received samples correlated with sequence S
Rate detection
  Low rate transmission: 2 positive peaks, separated by PN seq length
  High rate transmission: Single negative peak
Timing estimation
  Correlation exceeds a threshold

## Slide 4: Candidate sequence S: PN sequence with different bit durations
Sequence S (64 us duration)
  Zero padded 15 bit PN sequence, with 4 us bit duration
  Zero padded 31 bit PN sequence, with 2 us bit duration
We evaluate and compare the performance of 4 us and 2 us preamble bit durations
  Sequences with even smaller bit duration (1 us and below) can result in significant ISI and hence are not considered.

## Slide 5: Simulation parameters (Transmitter)
  Preamble: Low rate: [S S], High rate: [S complement]
    Case 1: S - [0 15 bit PN seq.], with 4 us bit duration
      4 us OOK pulse constructed using 13 L-STF coefficients
    Case 2: S - [0 31 bit PN seq.], with 2 us bit duration
      2 us OOK pulse generated using 32 pt. FFT in 20 MHz
  Data portion: Manchester coding
    Low rate scenario
      ‘0’- 4 us ON, 4 us OFF, 4 us ON, 4 us OFF
      ‘1’- 4 us OFF, 4 us ON, 4 us OFF, 4 us ON
      4 us OOK pulse constructed using 13 L-STF coefficients
    High rate scenario
      ‘0’- 2 us ON, 2 us OFF
      ‘1’- 2 us OFF, 2 us ON
      2 us OOK pulse generated using 32 pt. FFT in 20 MHz
Legacy+WUR mark
Wake-up preamble
MAC header
Payload
FCS
24 µs

## Slide 6: Simulation parameters (Receiver)
4 MHz LPF (IIR) – generated using MATLAB
  Third order Butterworth filter
  Cutoff freq. = 2.5 MHz, Sampling freq. =160 MHz
WUR processes (i) in-phase only (single rx chain); (ii) processes both I and Q
Channels: AWGN and Channel D
No phase noise and ACI modeled
2.4 GHz band operation
SNR is measured at 20 MHz bandwidth, post 4 MHz LPF
Performance quantified with respect to ideal rate and timing

## Slide 7: Performance of 4 us bit duration (WUR processes both I and Q)
Low rate scenario: No observable gap between ideal and estimated timing
High rate scenario: 0.25 dB loss in AWGN and 0.5 dB loss in Channel D

## Slide 8: Performance of 2 us bit duration (WUR processes both I and Q)
Performance gap < 0.2 dB, for both low and high rate scenarios

## Slide 9: Performance comparison (4 us Vs 2 us)
Performance measured with respect to ideal rate and ideal timing
  Delta SNR corresponding to 10% PER levels
Good performance for both 2 us and 4 us bit durations
  2 us case is little better for High rate scenario in Channel D
 | AWGN , Low rate | Channel D, Low rate | AWGN, high rate | Channel D, High rate
L – [], H – [] ( – 16 bit (64 us) PN sequence) | < 0.1 dB | < 0.1 dB | 0.15 dB | 0.5 dB
L – [], H – [] ( – 32 bit (64 us) PN sequence) | < 0.1 dB | 0.2 dB | 0.1 dB | < 0.1 dB
 | AWGN , Low rate | Channel D, Low rate | AWGN, high rate | Channel D, High rate
 | < 0.1 dB | < 0.1 dB | 0.15 dB | 0.5 dB
 | < 0.1 dB | 0.2 dB | 0.1 dB | < 0.1 dB

## Slide 10: Other metrics for picking a preamble sequence
Desirable metrics for picking a preamble sequence
  Good PER performance, measured in terms of SNR gap between the ideal timing and estimated timing
    Ratio of strongest peak/next strongest peak in auto-correlation of sequence is one indicator
  Smaller OFF (Silence) period in the preamble
    Maximum consecutive 1’s or 0’s (run length) in the sequence S
    Smaller OFF period is desirable
      Other devices does not sense the channel as idle
      Good for AGC implementation
    Atleast 8 us (4 us) with 4 us (2 us) preamble bit duration
  Sequence that enables efficient AGC implementation
    Desirable to have small silence period at the beginning of the sequence

## Slide 11: Impact of silence period on AGC (1)
6us OOK symbol gap
8us OOK symbol gap
Legacy Preamble + WUR-Mark
(24μs)
WUR Preamble (32- bit, 2us bit duration)
Energy accumulation window
for AGC gain setting
AGC gain typically set based on energy in the legacy preamble portion
  Energy accumulation window location can be arbitrary because of unknown packet start
  Large silence period results in inaccurate gain setting
Small OFF period in preamble is desirable
  Enables smaller accumulation window and faster AGC gain convergence

## Slide 12: Impact of silence period on AGC (2)
6us OOK symbol gap
8us OOK symbol gap
Legacy Preamble + WUR-Mark
(24μs)
WUR Preamble (32- bit, 2us bit duration)
Energy accumulation window
for AGC gain setting
Desirable to have smaller silence period at the beginning of the sequence
  Consecutive zeros in the beginning can cause significant fluctuations in the AGC gains.
  Enables faster AGC gain convergence and locking
  Metric (Silence Period Location): How far into the preamble sequence, do we get a silence period of 4 us or more
    For ex: [1 0 1 0 1 0 0 1……] with bit duration of 2 us, Metric = 10 us
    Larger values are better for AGC

## Slide 13: Candidate sequences S with 2 us bit durations
Sequence S1: Zero padded PN sequence
  S1 = [0 1 1 1 0 1 0 1 0 0 0 0 1 0 0 1 0 1 1 0 0 1 1 1 1 1 0 0 0 1 1 0]
  Maximum off time in S/S-Complement = 10 us
  Silence period location: 2 us into the sequence
Sequence S2: Proposed sequence in [6]
  S2 = [0 1 1 1 0 1 0 1 0 0 1 0 1 0 0 1 0 1 1 0 0 1 1 0 1 1 0 0 0 1 1 0]
  Maximum off time in S/S-Complement = 6 us
  Silence period location: 2 us into the sequence
Sequence S3: Proposed sequence in [7]
  S3 = [1 0 1 0 0 1 0 0 1 0 1 1 1 0 1 1 0 0 0 1 0 1 1 1 0 0 1 1 1 0 0 0]
  Maximum off time in S/S-Complement = 6 us
  Silence period location: 6 us into the sequence

## Slide 14: Candidate sequences S with 2 us bit durations
Sequence S4: Our proposed sequence
  S4 = [1 0 0 1 1 0 0 1 1 0 0 1 0 1 1 0 0 1 0 1 1 0 1 0 1 0 1 0 0 1 0 1]
  Maximum off time in S/S-Complement = 4 us
  Silence period location: 2 us into the sequence
  Generated by applying Manchester encoding [1 0]/[0 1] to zero padded 15 bit PN sequence
Sequence S5: Our proposed sequence
  S5 = [1 0 1 0 1 0 1 0 0 1 0 1 1 0 0 1 1 0 0 1 1 0 0 1 0 1 1 0 0 1 0 1]
  Maximum off time in S/S-Complement = 4 us
  Silence period location: 14 us into the sequence
  Generated by applying cyclic shift to Sequence S4

## Slide 15: Metrics of sequences S1-S5
Sequence | ACM (first maximum/second maximum) | Max OFF time in S/S-complement | Silence period location
S1 | 8 | 10 us | 2 us
S2 | 5.33 | 6 us | 2 us
S3 | 8 | 6 us | 6 us
S4 | 5.33 | 4 us | 2 us
S5 | 5.33 | 4 us | 14 us
S4 and S5 have the least OFF times
S4 and S5 have smaller ACM values than S1 and S3
  Does not necessarily translate to higher PER, as can be seen from simulation results
S5 has the maximum silence period location
  Consecutive 0’s/1’s in the sequence will start much later into the sequence

## Slide 16: PER with ideal rate and timing
Color codes: 5 different sequences – S1 to S5
Very similar PER values for different sequences S
  Expected as the timing is perfect

## Slide 17: PER with estimated rate and timing
Very similar performance for different sequences S, under different Tx rates and channel conditions
  Performance gap between different sequences < 0.2 dB (@10% PER, 1% PER)
PER includes miss detection, rate miss classification, and false alarms

## Slide 18: Summary
Evaluated and compared the performance of preamble sequences with 2us and 4 us bit durations
  Very similar performance for low rate scenario
  2 us case slightly better in Channel D, for high rate scenario
Proposed 2 us bit duration sequences (S4 and S5), suitable for efficient AGC implementation
  Smaller off period (especially at the beginning of preamble) is better for AGC
Evaluated the performance of different 32-bit preamble sequences S, with bit duration of 2 us
  Similar PER values for different channel models and Tx rates
  The proposed sequences S4 and S5 have smallest OFF period (4 us)
  Among the studied sequences, S5 has the OFF period (>2 us), farthest into the preamble sequence

## Slide 19: Straw poll 1
Which of the options do you support for preamble bit duration
Option 1: 4 us bit duration
  Yes
  No
  Abstain
Option 2: 2 us bit duration
  Yes
  No
  Abstain

## Slide 20: Straw Poll 2
Do you support the following proposal?
We propose to use the following 32-bit preamble sequence S (S5 in the presentation), with 2 us bit duration.
S = [1 0 1 0 1 0 1 0 0 1 0 1 1 0 0 1 1 0 0 1 1 0 0 1 0 1 1 0 0 1 0 1].
(Low rate is indicated by [S S], High rate is indicated by [S complement])
Yes
No
Abstain

## Slide 21: References
[1] 17/0997r0 Preamble Options, IEEE 802.11 TGba, July 2017
[2] 17/1781r1 Sync Structure Motions, IEEE 802.11 TGba, Nov. 2017
[3] 17/1355r1 WUR Preamble Evaluation, IEEE 802.11 TGba, September 2017
[4] 17/1345r5 11ba PHY Frame Format Proposal, IEEE 802.11 TGba, September 2017
[5] 17/1614r1 Preamble studies to indicate different data rates, IEEE 802.11 TGba, Nov. 2017
[5] Reference for Steve Shellhammer sequence: Options for 32-bit S in Sync Field
[6] Reference for Justin sequence (the new sequence): 20180102r2-WUR Preamble Sequence Performance Evaluation

## Slide 22
Appendix

## Slide 23: Performance of 4 us bit duration (WUR processes only Inphase component)
Low rate scenario: No observable gap between ideal and estimated timing
High rate scenario: 0.5 dB loss in AWGN and 1 dB loss in Channel D

## Slide 24: Performance of 2 us bit duration (WUR processes only Inphase component)
Performance gap < 0.2 dB, for high rate scenarios
Performance gap of 0.4 dB for low rate scenario

## Slide 25: Performance comparison (4 us Vs 2 us) (WUR processes only Inphase component)
Performance measured with respect to ideal rate and ideal timing
  Delta SNR corresponding to 10% PER levels
2 us case is better for High rate scenario
 | AWGN , Low rate | Channel D, Low rate | AWGN, high rate | Channel D, High rate
L – [], H – [] ( – 16 bit (64 us) PN sequence) | < 0.1 dB | < 0.1 dB | 0.5 dB | 1 dB
L – [], H – [] ( – 32 bit (64 us) PN sequence) | 0.4 dB | 0.4 dB | <0.1 dB | 0.2 dB
 | AWGN , Low rate | Channel D, Low rate | AWGN, high rate | Channel D, High rate
 | < 0.1 dB | < 0.1 dB | 0.5 dB | 1 dB
 | 0.4 dB | 0.4 dB | <0.1 dB | 0.2 dB

## Slide 26: PER with estimated rate and timing (WUR processing Only Inphase component)
Very similar performance for different sequences S
  Performance gap between different sequences < 0.2 dB (@10% PER, 1% PER)