## Slide 1: MU Beamforming for mmWave Distributed Network
Date: 2018-01-10
Name | Affiliation | Address | Phone | Email
Tony Xiao Han | Huawei Technologies |  |  | Tony.hanxiao@huawei.com
Mengyao Ma | Huawei Technologies |  |  | 
Yan Xin | Huawei Technologies |  |  | 
Chenlong Jia | Huawei Technologies |  |  | 

## Slide 2: Outline
Background and motivation
TDD MU BF Training Procedure
TDD SSW frame for TDD MU BF
Comparison of time cost
Conclusion

## Slide 3
In [1], it is pointed out that the BF paradigm defined in 11ad/11ay is not suitable to networks employing the TDD channel access [2][3].
However, the scheme proposed in [1, 6] is not efficient
  The TDD SSW is unicast frame.
  Hence, if there are N DNs/CNs (i.e., the Responder) which need to perform BF training with an Initiator, then X frames (the number of sweeping frames for BF for each DN/CN) will be repeated (by Initiator) for N times for all DNs/CNs (i.e., the Responder).
  The “Repeating and low efficiency” issue may happen in following situation
  When there are more than one DN/CN which need to do initial BF training together
    e.g., more than one DN/CN boot up simultaneously
  When more than one DN/CN lose their links because of, e.g., some network failure. It requires redoing BF training.
Background and motivation
Notes: Some possible network failure:
natural disasters like thunder and lightening;
replacing a DN (may need redo BF training with all serving CN)
Failure of TDD Sector Switch (A responder that reverted to the antenna configuration at the time indicated by the Revert Timestamp subfield value and that did not receive a PPDU from the initiator at a TDD slot occurring after the Revert Timestamp subfield value shall start the TDD beamforming procedure as a responder as described in 10.38.10.)

## Slide 4
Hence, we propose an approach to enhance the scheme in [1, 6], in order to solve the “Repeating and low efficiency” issue, by
  Adding another procedure for TDD MU BF
  Modifying the content of the following frames in the case of TDD MU BF
    TDD SSW frame
Background and motivation

## Slide 5
The procedure of TDD MU BF Training is modified as the following figure with the following changes
  Different time could be scheduled for different Responder (STA) to send TDD SSW Feedback
  Different time could be indicated for Initiator (AP) to send TDD SSW ACK for different Responder (STA)
TDD MU BF Training Procedure

## Slide 6: TDD SSW frame for TDD SU BF
When TDD SSW frame is only for one Responder, then the same format kept as it is in [6] (could reduce the overhead, since if there are more than 27 bytes, at least one more LDPC coding block is needed)
 | Frame Control | Duration | RA | TA | TDD BF Control | TDD BF Information | FCS
Octets : | 2 | 2 | 6 | 6 | 1 | 6 | 4
TDD SSW frame format for TDD SU BF
TDD BF Control field format
 | TDD BF Frame Subtype | End of Training | Reserved
Bits: | 2 | 1 | 5

## Slide 7: TDD SSW frame for TDD MU BF
 | Frame Control | Duration | RA | TA | TDD BF Control | TDD BF Information | FCS
Octets : | 2 | 2 | 6 | 6 | 1 | Variable | 4
TDD SSW frame format for TDD MU BF
TDD BF Control field format
 | TDD BF Frame Subtype | End of Training | Reserved
Bits: | 2 | 1 | 5
When TDD SSW frame is for more than one Responder, the TDD SSW frame is modified as the following figure with the following changes
  the RA of TDD SSW frame is changed from Unicast to Broadcast MAC address
  The Number of Responders subfield is indicated
  Responder Feedback Offset and Initiator Ack Offset are indicated in Responder Info subfield for each responder
  The ID of the Responder could be 10 bits special ID
    The 10 special ID could be derived based on the 48 MAC address, with a predefined scheme known by DN and CN ( e.g., based on the same scheme in 30.9.1.2 in [5] )

## Slide 8: Comparison of time cost
Assumption and configuration
  TDD slot Duration = 66us, SBIFS = 1us,
  For the scheme in [1, 6], every TDD slot filled with four TDD SSW frames
  For our scheme, every TDD slot filled with three TDD SSW frames (for 2-4 Responders), or two TDD SSW frames (for 5-10 Responders)
Following figures shows the comparison of time cost for BF training with different number of Responder (calculation details could be found in Appendix I, II)
  Time cost for scheme in [1, 6]: with very high time cost
  Our scheme: time cost is much reduced.
TDD SSW
Every TDD slot filled with three or four TDD SSW frames
IFS options (RIFS, SBIFS, SIFS or programmable) under study
TDD SSW
……

## Slide 9: Comparison of time cost
  Noting that the gain of our scheme could be larger when the following are considered
  If the failure of BF is considered here, the gain of our scheme could be larger .
  By the scheme proposed in [1, 6], multiple Responders could only be trained sequentially. Since there may be data transmission between the BF training, the delay for the later on training Responder will be very large, e.g., maybe more than hundreds of ms. However, our scheme allows to train multiple Responder simultaneously. This will significantly reduce the BF training time.
Notes: Based on the assumption of slide 6 of “11-17-1679-00-00ay-beamforming-protocol-reuse-for-mmwave-distribution-networks.pptx”, assume 16 TX beams, and repeat TDD SSW frame 32 times for each TX Beam, then
For the Scheme in [1, 6], BF training time for 1 Responder is (at least): 400*(32/4)*16 = 51200 us, then for n Responder is: n*51200 us
For our scheme, BF training time for n Responder is 400*⌈32/3⌉ *16 = 70400 us

## Slide 10: Conclusions
This contribution proposes a BF training procedure for a scenario in which the Initiator (DN) can efficiently perform BF training with multiple Responders (DNs/CNs).
The frame format presented in [6] is expanded, in order to perform the proposed multiple Responder (DNs/CNs) BF (But for single Responder BF scheme, the BF training scheme remains unchanged as [6])
The BF efficiency in terms of elapsed time is improved.

## Slide 11: Straw Poll/Motion 1
Do you think a TDD MU Beamforming is needed for distributed network, by which the Initiator (DN) can efficiently perform BF training with multiple Responders (DNs/CNs)?
  Yes
  No
  Abstain

## Slide 12: Straw Poll/Motion 2
Do you agree to adopt the scheme described in slides 5-7 into the spec?
(This is just for SP, and the draft text will be provided in the near future for Motion)
  Yes
  No
  Abstain
Notes: Do you agree to include the text for TDD MU Beamforming proposed in “11-18-0234-00-00ay-Draft-text-for-MU-beamforming-for-mmwave-distributed-network.docx” to the spec draft?

## Slide 13: References
[1] 802.11-17/1646r1-00ay-beamforming-for-mmwave-distribution-networks
[2] 802.11-17/1019r2 “mmWave Mesh Network Usage Model”
[3] 802.11-17/1321r0 “Features for mmW Distribution Network Use Case”
[4] 802.11-2016.pdf
[5] Draft P802.11ay_D1.0.pdf
[6] 11-18-0179-02-00ay-beamforming-for-mmwave-distributed-network

## Slide 14: Appendix I-1: TXTIME(X) [4]
TXTIME (20.12.3 TXTIME calculation in [4])
TXTIME(TDD SSW_old)
=𝑇_(𝑆𝑇𝐹−𝐶𝑃)+𝑇_(𝐶𝐸−𝐶𝑃)+(11×8+(𝐿𝑒𝑛𝑔𝑡ℎ−6)×8+𝑁_𝐶𝑊×168)×𝑇_𝐶×32+𝑁_𝑇𝑅𝑁×𝑁_(𝑇𝑅𝑁−𝑈𝑛𝑖𝑡)
=3.636us+655ns+(11×8+(27-6)×8+2×168)×0.57ns×32 = 15.08908us (SSW is 14.94316us)
TXTIME(TDD SSW_new) (when use 10 bit ID of Responder)
=𝑇_(𝑆𝑇𝐹−𝐶𝑃)+𝑇_(𝐶𝐸−𝐶𝑃)+(11×8+(𝐿𝑒𝑛𝑔𝑡ℎ−6)×8+𝑁_𝐶𝑊×168)×𝑇_𝐶×32+𝑁_𝑇𝑅𝑁×𝑁_(𝑇𝑅𝑁−𝑈𝑛𝑖𝑡)
  =3.636us+655ns+(11×8+( 34 -6)×8+ 3×168)×0.57ns×32 = 19.17484 us (when used for 2 Responders)
  =3.636us+655ns+(11×8+(38 -6)×8+ 3×168)×0.57ns×32 = 19.75852 us (when used for 3 Responders)
  =3.636us+655ns+(11×8+( 42 -6)×8+ 3×168)×0.57ns×32 = 20.3422 us (when used for 4 Responders)
TXTIME(TDD SSW Feedback)
=𝑇_(𝑆𝑇𝐹−𝐶𝑃)+𝑇_(𝐶𝐸−𝐶𝑃)+(11×8+(𝐿𝑒𝑛𝑔𝑡ℎ−6)×8+𝑁_𝐶𝑊×168)×𝑇_𝐶×32+𝑁_𝑇𝑅𝑁×𝑁_(𝑇𝑅𝑁−𝑈𝑛𝑖𝑡)
=3.636us+655ns+(11×8+(27-6)×8+2×168)×0.57ns×32 = 15.08908us (SSW is 14.94316us)
TXTIME(TDD SSW ACK)
=𝑇_(𝑆𝑇𝐹−𝐶𝑃)+𝑇_(𝐶𝐸−𝐶𝑃)+(11×8+(𝐿𝑒𝑛𝑔𝑡ℎ−6)×8+𝑁_𝐶𝑊×168)×𝑇_𝐶×32+𝑁_𝑇𝑅𝑁×𝑁_(𝑇𝑅𝑁−𝑈𝑛𝑖𝑡)
=3.636us+655ns+(11×8+(27-6)×8+2×168)×0.57ns×32 = 15.08908us (SSW is 14.94316us)
𝑇_(𝑆𝑇𝐹−𝐶𝑃)=3.636 μs =50 × Tseq
𝑇_(𝐶𝐸−𝐶𝑃)=655 ns=9 × Tseq
The total (header and additional data) number of bits in the first LDPC codeword is LDPFCW =(LHDR + LFDCW )× 8= 88
168 is the maximal number of data bits in each LDPC codeword
NCW: the number of LDPC codeword. For the SSW frame, Length=26 Octets, So 𝑁_𝐶𝑊=2 , 𝑁_𝑇𝑅𝑁=0
32 is the golay sequence spreading
𝐿_𝐶𝑊𝐷=168 , Length=26 Bytes
Tc: SC Chip Time, i.e., 0.57ns=1/Fc
Notes: 3.636us+655ns+(11×8+(27-6)×8+2×168)×0.57ns×32
=3.636us+655ns+(11×8+2×168)×0.57ns×32 + (27-6)×8 ×0.57ns×32
= 12.02476 + 3.06432=15.08908

## Slide 15: Appendix II-1: Time cost example 1
Assumption and configuration
  16 TX Beams, and repeat TDD SSW frame 32 times for each TX Beam
  TDD slot Duration = 66us, SIBFS = 1us,
  For the scheme in [6], every TDD slot filled with four TDD SSW frames
  For our scheme, every TDD slot filled with three TDD SSW frames
T_(BFT_old) * 2
= [T_(TDD slot Duration) * N_(number of TDD slot) + TXTIME(TDD SSW Feedback) + TXTIME(TDD SSW ACK) ] * 16 * 2
= [ 66* ⌈32/4⌉ + 15.08908 + 15.08908 ] * 16 * 2 = 558.17816 * 16 * 2 = 17861.70112 us
T_(BFT_old) * 3
= [T_(TDD slot Duration) * N_(number of TDD slot) + TXTIME(TDD SSW Feedback) + TXTIME(TDD SSW ACK) ] * 16 * 3
= [ 66 * ⌈32/4⌉ + 15.08908 + 15.08908 ] * 16 * 3 = 558.17816 * 16 * 3 = 26792.55168 us
T_(BFT_old) * 4
= [T_(TDD slot Duration) * N_(number of TDD slot) + TXTIME(TDD SSW Feedback) + TXTIME(TDD SSW ACK) ] * 16 * 4
= [ 66 * ⌈32/4⌉ + 15.08908 + 15.08908 ] * 16 * 4 = 558.17816 * 16 * 4 = 35723.40224 us
And the corresponding Time cost for scheme in our scheme (ID of the Responder is 10 bits special ID)
T_(BFT_new_2 )
= {T_(TDD slot Duration) * N_(number of TDD slot) + [ TXTIME(TDD SSW Feedback) + TXTIME(TDD SSW ACK) ] * 2+ (2-1)×SBIFS + (2-1)×SBIFS }*16
= {66 * ⌈32/3⌉ + [ 15.08908 + 15.08908 ] * 2 + 1 + 1}*16 = {726 + 30.17816 * 2 + 2}*16= 12613.70112 us
T_(BFT_new_3 )
= {T_(TDD slot Duration) * N_(number of TDD slot) + [ TXTIME(TDD SSW Feedback) + TXTIME(TDD SSW ACK)] * 3 + (3-1)×SBIFS + (3-1)×SBIFS}*16
= {66 * ⌈32/3⌉ + [ 15.08908 + 15.08908 ] * 3 + 4}*16= {726 + 30.17816 * 3 + 4}*16= 13128.55168 us
T_(BFT_new_4 )
= {T_(TDD slot Duration) * N_(number of TDD slot) + [ TXTIME(TDD SSW Feedback) + TXTIME(TDD SSW ACK)] * 4 + (4-1)×SBIFS + (4-1)×SBIFS}*16
= {66 * ⌈32/3⌉ + [ 15.08908 + 15.08908 ] * 4 + 6}*16= {726 + 30.17816 * 4 + 6}*16= 13643.40224 us