## Slide 1: Discussion on theWUR Minimum Sensitivity Level
Date: 2018-03-05
Authors:

## Slide 2: Introduction
This presentation discusses whether WUR sensitivity for the low rate should be defined better than the sensitivity of primary connectivity radio (PCR), i.e., -82dBm @ 20MHz
  The subject was brought up during the spec PHY development [1], and is motivated by
    11ba PAR statement, “The WUR is a companion radio to the primary connectivity radio and meets the same range requirement as the primary connectivity radio.”

## Slide 3: Background - Factors Impacting Link Budget
The link budget, in comparison to PCR, was previously brought up in [2]
  There could be a max Tx-PSD limit per MHz of bandwidth imposed by regulatory bodies.
    Because WUR bandwidth is 4MHz, therefore it transmission may be done at ddB lower than WUR
      Typically d=4 in 2.4 GHz band, and 7 dB in 5 GHz band
  WUR noise figure is assumed to be 8 dB higher than that of the PCR, due to lower power consumption [3]

## Slide 4: Range of WUR vs. PCR
Because of the limitation in Tx-PSD, a concern was raised that in certain regions of the world, WUR may not necessarily meet the same range as PCR, and therefore, not being able to meet PAR
  For this, some have argued to define lower sensitivity for WUR
    There is an additional 7dB due to the reduction in noise bandwidth for 4MHz WUR as opposed to 20MHz that of the PCR
      We note that this 7dB is already accounted for the low rate link budget analysis

## Slide 5: A Look At Definition Of Sensitivity For PCR (1/2)
As it is well understood majority of devices in the market meet better sensitivity than what is required by the spec.
  However, spec defines minimum sensitivity requirement for all implementations
  Allows development of variety of devices at different price point for different applications
  Encourages competition to meet better coverage/price
  The least costly devices do not transmit at maximum Tx limit either

## Slide 6: A Look At Definition Of Sensitivity For PCR (2/2)
The max Tx power limit is different in 5GHz band compared to 2.4GHz
The max Tx power limit is also different in different regulatory domains
  Spec defines uniform sensitivity level in 11a/g/n/ac/ax for 20MHz of bandwidth
  Note that when 11a was developed, UNII low (5.15-5.25 MHz) had 7dB lower max Tx power required by FCC (just recently FCC has increased the level to be the same as UNII-2 & 3).
The definition of sensitivity level for PCR is not coupled with regulatory domains (Tx power or the range of coverage)

## Slide 7: Definition Of Sensitivity For WUR
The minimum sensitivity level of WUR should be defined independent of the regulatory domain requirements on Tx-power
For the low rate, it cannot be better than PCR because in regions that there is no Tx-PSD limit, the range of WUR will become better than PCR
  A better range for WUR will cause PCR to go off the range of its BSS unnoticed because WUR will continue to receive WUR beacons
    Creates problems with roaming
A shorter range of WUR is also problematic
Devices need to develop implementation specific recovery mechanisms because the two radios will not have identical ranges

## Slide 8: Recommendations
Define the WUR minimum sensitivity level for the low rate to be the same as PCR, i.e., -82dBm
The actual range depends on the receiver implementation such as noise figure.
The main target of WUR is to enable a low power receiver. Therefore spec should define a minimum sensitivity that all implementation can meet without incurring higher power consumption or cost.
  Cost is also important for successful penetration of WUR to IoT devices and use cases as defined in the usage model document [4]
We will meet PAR
  Assuming same Tx-power for PCR & WUR, WUR will achieve the same range as PCR
  With an optimal implementation regardless of geo location
    Example: 11ax PAR calls for enabling at least one mode of operation for 4x throughput improvement

## Slide 9: Straw Poll: Receiver minimum input level sensitivity
Do you agree to include the following text into the WUR PHY spec?
The packet error rate (PER) shall be less than 10% for a WUR PPDU with the rate-dependent input levels listed in below.
Receiver minimum input level sensitivity:
Low Data Rate: -82dBm for a WUR PPDU that contains WUR frame with no Frame Body. Note, this level is the same as the PCR receiver minimum input level sensitivity for a 2048 octets packet of BPSK ½.
High Data Rate: TBD
Yes
No
Abstain

## Slide 10: References
[1] 18/0152r0 Proposed Draft WUR PHY Specification, IEEE 802.11 TGba, January 2018
[2] 17/0365r0 Regulations and Noise Figure – Impact on SNR, IEEE 802.11 TGba, March 2017
[3] 17/0188r9 Simulation Scenario and Evaluation Methodology, IEEE 802.11 TGba, July 2017
[4] 17/0029r10 WUR Usage Model Document, IEEE 802.11 TGba, September 2017