## Slide 1: Discussion on WUR Multi-Antenna Transmission
Date: 2018-03-05
Authors:

## Slide 2: Introduction
WUR transmitter likely shares the same radio with main WiFi radio using multiple-antennas.
In WiFi main radio, cyclic shift diversity (CSD) technique is adopted to avoid unintentional spatial nulling
In this contribution, we discuss the necessity and feasibility of CSD for WUR, and simulate the WUR performance with different CSD values

## Slide 3: Review: 11n/ac/ax CSD
From 802.11n, cyclic shift diversity (CSD) is defined for MIMO systems to avoid unintentional destructive beamforming
  In Pre-HT/VHT/HE portion of the packet, CSD is defined per antenna as the spatial mapping technique.
  In HT/VHT/HE portion, CSD is defined per-stream. Spatial mapping is up to the transmitter’s design. Beamforming can be applied to get the spatial mapping/steering matrix.
LSTF
LLTF
LSIG
VHT STF LTF SIGB DATA
VHT
SIGA
Pre-VHT Portion
VHT Portion

## Slide 4: WUR Multi-Antenna Transmission
WUR packet is “single-stream”: both Legacy portion and WUR portion.
For a WUR transmitter equipped with multiple antennas, if similar CSD design as 802.11n/ac/ax is adopted
  Legacy portion uses the same spatial CSD values as 802.11n/ac/ax. This is important for other main radios to correctly set CCA.
  WUR portion will not need “per-steam” CSD.
  WUR transmitter can determine its spatial mapping matrix based on instantaneous or statistical channel information.
LSTF
LLTF
LSIG
WUR SYNC
WUR Data
BPSK
Mark
Legacy
WUR

## Slide 5: WUR Spatial Mapping
WUR transmitter equipped with multiple antennas may perform beamforming on WUR portion.
  WUR does not define explicit sounding protocol
  Some implicit channel information may be obtained from main radio.
If beamforming is not available at a WUR transmitter, CSD can be a good spatial mapping candidate.
For broadcast/multicast wake-up, CSD will also be effective.

## Slide 6: CSD for WUR
11n/ac/ax CSD is designed according to minimum 20MHz signal bandwidth [1]
  The minimum shift is 50ns (<=4Tx) or 25ns(<=8Tx)
  The maximum shift is 200ns
WUR signal bandwidth is 4MHz
  The resolvable channel delay is 250ns.
  With 11n/ac/ax per-antenna CSD, shifted delay taps from all Tx antennas are not resolvable. The spatial diversity benefit will be limited.
  Larger CSD values is meaningful for WUR.
WUR CSD design:
  reuse 11n/ac/ax per-antenna CSD table [1], and WUR portion applies N times of 11n/ac/ax CSD values. For example, N = 5.

## Slide 7: Simulation Settings
WUR Packet
  WUR Data signal uses center 13 tones in 20MHz bandwidth
  Payload: 48 bits, Manchester Coding
  2ms noise appended before the WUR packet
SNR defined on 20MHz noise
CFO = 20ppm, fc = 2.4GHz, No phase noise
Receiver
  Realistic AGC: entire packet is normalized to certain gain target
    Noise portion normalized based on the noise power
    WUR portion normalized by 20MHz preamble power
  3th order 4MHz butterworth filter with 2.5MHz cutoff frequency
  4MHz sampling rate with in-phase path
LSTF
LLTF
LSIG
WUR SYNC
WUR Data
BPSK
Mark
2ms noise

## Slide 8: B-LOS 2x1
  More diversity gain is achieved with 5x 11ac CSD

## Slide 9: B-LOS 4x1
  ~1dB loss for HDR with 11ac CSD
  Huge diversity gain is achieved with 5x 11ac CSD

## Slide 10: B-LOS 8x1
  More diversity gain is achieved with 5x 11ac CSD

## Slide 11: D-NLOS 2x1
  ~0.5dB loss for HDR with 11ac CSD
  More diversity gain is achieved with 5x 11ac CSD

## Slide 12: D-NLOS 4x1
  More diversity gain is achieved with 5x 11ac CSD

## Slide 13: D-NLOS 8x1
  More diversity gain is achieved with 5x 11ac CSD

## Slide 14: Discussion
It is important to inherit the CSD design on the Legacy portion for CCA.
CSD does not need to be mandated for the WUR portion.
  CSD can be a good candidate for WUR portion when beamforming is not available.
If CSD is applied, 11n/ac/ax CSD table is not effective for WUR portion to achieve spatial diversity.
  Even performance degradation is observed for some cases.
Evaluated larger CSD values using N times of 11n/ac/ax CSD values
  Simulations with N=5 shows very good diversity gain

## Slide 15: Straw Poll 1
Do you agree that the Legacy portion of an 11ba multi-antenna transmission uses spatial mapping with the same pre-VHT CSD table in [1]?
  Y:
  N:
  A:

## Slide 16: Straw Poll 2
Do you agree that for the WUR portion of an 11ba multi-antenna transmission, the standards
  Option A: do not mandate any spatial mapping technique
  Option B: mandate using CSD
  Y:
  N:
  A:

## Slide 17: Straw Poll 3
Do you agree that 11ba CSD values to be 5 times of pre-VHT CSD values as in Table 21.10 of IEEE P802.11-REVmc/D8.0?
  Y:
  N:
  A:

## Slide 18: Reference
[1] Table 21.10, IEEE P802.11-REVmc/D8.0

## Slide 19: Appendix

## Slide 20: UMi-NLOS 2x1

## Slide 21: UMi-NLOS 4x1

## Slide 22: AWGN: DFT 2x1

## Slide 23: AWGN: DFT 4x1

## Slide 24: AWGN: DFT 8x1