## Slide 1: Discussion on WUR Multi-Antenna Transmission
Date: 2018-03-05
Authors:

## Slide 2: Introduction
WUR transmitter likely shares the same radio with main WiFi radio using multiple-antennas.
In WiFi main radio, cyclic shift diversity (CSD) technique is adopted to avoid unintentional spatial nulling
In this contribution, we discuss the necessity and feasibility of CSD for WUR, and simulate the WUR performance with different CSD values

## Slide 3: Review: 11n/ac/ax CSD
From 802.11n, cyclic shift diversity (CSD) is defined for MIMO systems to avoid unintentional destructive beamforming
  In Pre-HT/VHT/HE portion of the packet, CSD is defined per antenna as the spatial mapping technique.
  In HT/VHT/HE portion, CSD is defined per-stream. Spatial mapping is up to the transmitter’s design. Beamforming can be applied to get the spatial mapping/steering matrix.
LSTF
LLTF
LSIG
VHT STF LTF SIGB DATA
VHT
SIGA
Pre-VHT Portion
VHT Portion

## Slide 4: WUR Multi-Antenna Transmission
WUR packet is “single-stream”: both Legacy portion and WUR portion.
For a WUR transmitter equipped with multiple antennas, if similar CSD design as 802.11n/ac/ax is adopted
  Legacy portion uses the same spatial CSD values as 802.11n/ac/ax. This is important for other main radios to correctly set CCA.
  WUR portion will not need “per-steam” CSD.
  WUR transmitter can determine its spatial mapping matrix based on instantaneous or statistical channel information.
LSTF
LLTF
LSIG
WUR SYNC
WUR Data
BPSK
Mark
Legacy
WUR

## Slide 5: WUR Spatial Mapping
WUR transmitter equipped with multiple antennas may perform beamforming on WUR portion.
  WUR does not define explicit sounding protocol
  Some implicit channel information may be obtained from main radio.
If beamforming is not available at a WUR transmitter, other spatial mapping techniques can be applied, for example,
  CSD can be a good spatial mapping candidate.
  Random phase rotation across antennas
For broadcast/multicast wake-up, CSD will also be effective.

## Slide 6: CSD for WUR
11n/ac/ax CSD is designed according to minimum 20MHz signal bandwidth [1]
  The minimum shift is 50ns (<=4Tx) or 25ns(<=8Tx)
  The maximum shift is 200ns
WUR signal bandwidth is 4MHz
  The resolvable channel delay is 250ns.
  With 11n/ac/ax per-antenna CSD, shifted delay taps from all Tx antennas are not resolvable.
  Larger CSD values create better diversity, but the longer delay spread will cause more CS/timing inaccuracy for WUR.
Simple WUR CSD design:
  reuse 11n/ac/ax per-antenna CSD table [1], and WUR portion applies N times of 11n/ac/ax CSD values.

## Slide 7: Simulation Settings
WUR Packet
  WUR Data signal uses center 13 tones in 20MHz bandwidth
  Payload: 48 bits, Manchester Coding
  2ms noise appended before the WUR packet
SNR defined on 20MHz noise
CFO = 20ppm, fc = 2.4GHz, No phase noise
Receiver
  Realistic AGC: entire packet is normalized to certain gain target
    Noise portion normalized based on the noise power
    WUR portion normalized by 20MHz preamble power
  3th order 4MHz butterworth filter with 2.5MHz cutoff frequency
  4MHz sampling rate with in-phase path
LSTF
LLTF
LSIG
WUR SYNC
WUR Data
BPSK
Mark
2ms noise

## Slide 8: D-NLOS 2x1
  11ac CSD show performance improvement for LDR, but degradation for HDR
  Random phase helps

## Slide 9: D-NLOS 4x1
  11ac CSD show performance improvement for LDR, but degradation for HDR
  Random phase helps

## Slide 10: B-LOS 2x1
  11ac CSD show good performance improvement
  Random phase also helps

## Slide 11: B-LOS 4x1
  11ac CSD show performance degradation, >1dB for HDR
  Random phase helps

## Slide 12: D-NLOS 2x1
  Larger CSD improves sensitivity significantly
  Performance gets close to 1Tx performance

## Slide 13: D-NLOS 4x1
  Larger CSD improves sensitivity significantly
  Performance gets close to 1Tx performance

## Slide 14: B-LOS 2x1
  Larger CSD improves sensitivity significantly
  Performance gets close to 1Tx performance

## Slide 15: B-LOS 4x1
  Larger CSD improves sensitivity significantly
  Performance gets close to 1Tx performance

## Slide 16: Discussion
It is important to inherit the CSD design on the Legacy portion for CCA.
Spatial mapping in WUR portion
  Beamforming is preferable if channel is known from PCR.
  CSD can be a good candidate when beamforming is not available.
  11n/ac/ax CSD table is not effective for WUR portion to achieve spatial diversity. Performance degradation is observed for some cases.
  Evaluate larger CSD values using N times of 11n/ac/ax CSD values
  Some diversity gain is achieved at sensitivity point
  In some configuration/channel, high error floor is also observed
Prefer to let the transmitter to decide the spatial mapping techniques, like in 11n/ac/ax.

## Slide 17: Straw Poll 1
Do you agree that the Legacy portion of an 11ba multi-antenna transmission uses spatial mapping with the same pre-VHT CSD table in [1]?
  Y:
  N:
  A:

## Slide 18: Straw Poll 2
Do you agree that 11ba multi-antenna transmission does NOT mandate the spatial mapping technique for the WUR portion?
  Y:
  N:
  A:

## Slide 19: Reference
[1] Table 21.10, IEEE P802.11-REVmc/D8.0